## Slide 1: SDN and Virtualization
“Can the Production Network Be the Testbed?” (Flowvisor), OSDI, 2010
“Network Virtualization in Muti-tenant Datacenters,” NSDI 2014

## Slide 2: Flowvisor Overview
Windows
(OS)
Windows
(OS)
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
App
App
Linux
Linux
Mac
OS
Mac
OS
Virtualization
App
Simple, common, stable, hardware substrate below
+ Programmability + Strong isolation model
Controller 1
App
App
Controller
2
Virtualization (FlowVisor)
App
OpenFlow
Controller 1
Controller 1
Controller
2
Controller
2

## Slide 3
Flowvisor Overview (Cont’d)
• Divide the production network into logical slices
o each slice/service controls its own packet forwarding o users pick which slice controls their traffic: opt-in o existing production services run in their own slice e.g., Spanning tree, OSPF/BGP
• Enforce strong isolation between slices
o actions in one slice do not affect another
• Allows the (logical) slice to mirror the production network o real hardware, performance, topologies, scale, users

## Slide 4: Network slice and flowspace
A network slice controls a subset of traffic
The subset is defined by a collection of packet headers.
  n-bit headers has n-dimension space – flowspace
Example:
  HTTP traffic – TCP port = 80
  All traffic from node 127.2.1.12 – IP_SRC=127.2.1.12
A subset of flowspace + a subset of topology = network slice

## Slide 5: Substrate: “Flowspace”
Payload
Ethernet
DA, SA, etc
IP
DA, SA, etc
TCP
DP, SP, etc
Collection of bits to plumb flows
(of different granularities)
between end points
Payload
Header
User-defined flowspace
“OpenFlow++”

## Slide 6: Properties of Flowspace
Backwards compatible
  Current layers are a special case
  No end points need to change
Easily implemented in hardware
  e.g. TCAM flow-table in each switch
Strong isolation of flows
  Simple geometric construction
  Can prove which flows can/cannot communicate

## Slide 7
FlowSpace: Maps Packets to Slices

## Slide 8
Real User Traffic: Opt-In
• Allow users to Opt-In to services in real-time
o Users can delegate control of individual flows to Slices
o Add new FlowSpace to each slice's policy
• Example:
o "Slice 1 will handle my HTTP traffic" o "Slice 2 will handle my VoIP traffic" o "Slice 3 will handle everything else"
• Creates incentives for building high-quality services

## Slide 9: Slicing control & data planes

## Slide 10: Slicing OpenFlow

## Slide 11
Network Slicing Architecture
A network slice is a collection of sliced switches/routers
• Data plane is unmodified
- Packets forwarded with no performance penalty
- Slicing with existing ASIC
• Transparent slicing layer
- each slice believes it owns the data path
- enforces isolation between slices
• i.e., rewrites, drops rules to adhere to slice police
- forwards exceptions to correct slice(s)

## Slide 12
Slicing Policies
The policy specifies resource limits for each slice:
- Link bandwidth
- Maximum number of forwarding rules
- Topology
- Fraction of switch/router CPU
FlowSpace: which packets does the slice control?

## Slide 13
OpenFlow
Switch
OpenFlow
Protocol
FlowVisor
Bob’s
Controller
Alice’s
Controller
OpenFlow
Protocol
FlowVisor Slicing Example
OpenFlow
Switch
OpenFlow
Switch

## Slide 14
OpenFlow
Protocol
FlowVisor
Broadcast
Multicast
OpenFlow
Protocol
http
Load-balancer
FlowVisor Slicing Example (Cont’d)
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch

## Slide 15
OpenFlow Protocol
FlowVisor Slicing Example (Cont’d)
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Network Administrator’s
FlowVisor
OpenFlow Protocol
Production
Network
Controller
Alices’s
FlowVisor
GENI’s
FlowVisor
Bob’s
FlowVisor
Learning
switch
Mobile VMs
New BGP
LTE-WiFi
Handover
Tricast Lossless
Handover

## Slide 16
FlowVisor Implemented on OpenFlow
Custom
Control
Plane
Network
Stub
Control
Plane
Data
Plane
Server
OpenFlow Controller
OpenFlow
Protocol
OpenFlow
Firmware
Data Path
Switch/
Router
Servers
OpenFlow OpenFlow OpenFlow
Controller Controller Controller
OpenFlow
FlowVisor
OpenFlow
OpenFlow
Firmware
Data Path
Switch/
Router

## Slide 17
FlowVisor Message Handling
Alice Bob
Controller Controller
OpenFlow
Rule
Cathy
Controller
Policy Check:
Is this rule allowed?
Full Line Rate Forwarding
Packet
FlowVisor
OpenFlow
Exception
OpenFlow
Firmware
Data Path
Policy Check:
Who controls this packet?
Source: R. Sherwood

## Slide 18: Flowvisor implementation
Message to control plane
Message to forwarding plane
Bandwidth isolation
Device CPU isolation
Flow entry isolation

## Slide 19: Flowvisor implementation
Message to control plane
  Rewrites message from OpenFlow switch to slice controller for transparency
  only send message when switch is in slice topology
  slice controller only sees the ports that appears in the slice
  port up/down message only to affected slices
Message to forwarding plane
  rewrite the insert and delete flow table messages
  only to the switches in the slice

## Slide 20: Flowvisor implementation
Bandwidth isolation
  per-port queues in switch hardware
  Flowvisor creates a per-slice queue on each port
  queue is configured for a certain bandwidth as defined in slice definition
  rewrite rules from “send out port X” to “send out queue Y on X”.

## Slide 21: Flowvisor implementation
CPU isolation
  Device CPU on commodity network hardware are low-power embedded processors, easily overloaded, no isolation mechanism
  Work around: no slice monopolizes device CPU
  Limiting rule insertion rate from controller
  Use periodic drop rules to throttle exceptions
Flow table entry isolation
  Enforce what is defined by the slice

## Slide 22
Conclusion
• Network slicing can help perform more realistic evaluations and support multiple tenants
• FlowVisor allows experiments to run concurrently but safely on the production network
• Currently limited to subsets of actual topology
  - Add virtual links, nodes support

## Slide 23: SDN and Virtualization
“Can the Production Network Be the Testbed?” (Flowvisor), OSDI, 2010
“Network Virtualization in Multi-tenant Datacenters,” NSDI 2014

## Slide 24: Multi-tenant datacenter challenges
Tenants want to move their code from their enterprises directly to datacenters without modification
  Different services require different topologies – flat L2, some L3, multiple levels of services
  Address space: virtualized workload should not operate in the same address space as the physical network (VM’s IP is learned from the first L3 router!)
    Cannot move MV to arbitrary locations
    Tenant cannot manage its own IP
    Operator cannot change the addressing type.

## Slide 25: Multi-tenant datacenter challenges
Ideal multi-tenant datacenter:
  Arbitrary network topologies and addressing architectures could be overlayed over the same physical network.
  Network virtualization: not clear what it is
    a network virtualization layer allows for the creation of virtual networks, each with independent service models, topologies, and addressing architectures, over the same physical network. Tenants can configure its virtual network
    Existing mechanisms all fall short: VLAN, NAT, MPLS, VRB (Virtualized L3 FIB),

## Slide 26: Network hypervisor
Network virtualization platform
  Control abstraction: allow tenants to define logical network elements that can be configured
  Packet abstraction: Packets from the end hosts to have the same switching, forwarding, and filtering behavior as configured by the tenant

## Slide 29: Virtualization architecture
Implement the logical data path in the host vswitch inside the host hypervisor for point-to-point traffic – tunnel between hypervisor
  Use SDN controller to set the first-hop vswitch.
Use service node to support broadcast/multicast
Use gateway node to support communication with outside

## Slide 31: Computation challenges
Most maintain O(N^2) flows for N end-points with frequent dynamic changes.
  Controllers learn the location of VMs
  Controllers proactively compute and push all forwarding state required to connect the VMs
    Forwarding State = F(configuration, VM locations)

## Slide 32: Solution to computation challenges
Incremental computation and pushing for quick updates.
  Share the computation across controller cluster.
Use a language to program F
  avoid handwritten finite state machines, all are generated

## Slide 36: Conclusion
Openflow can facilitate network virtualization
The current practice of network virtualization is not ideal. This paper presents a limited form of network virtualization for special cases.