## Slide 1: SDN controller scalability issue
Fundamental issue: the speed gap between data plane and control plane.
Switch OS
Switch HW
10-100 Gbps
Switch OS
Switch HW
10-100 0Mbps
Switch OS
Switch HW
???
SDN controller

## Slide 2: SDN controller scalability issue
Data plane can overwhelm control plane by design
  Control channel or controller resources
SDN controller has a fundamental scalability issue
Data plane
Control plane
2. Stress the control channel
1. Stress controller resources

## Slide 3: Solutions 1: Increase controller capacity - distributed controllers
Flat structure multiple controllers
  ONIX (OSDI’10)
  ONOS(HostSDN’14)
Data plane
Control plane
2. Stress the control channel
1. Stress controller resources
Control plane
Control plane

## Slide 4: Solutions 2: reduce traffic to controller -- Hierarchical controller
Hierarchical controller design
  Kandoo (HotSDN’12)
Data plane
2. Stress the control channel
1. Stress controller resources
Control plane
Data plane
Root Control
Local Control

## Slide 5: Solutions 2: Reduce traffic to controller – offload control to switch
Offload to switch control plane
  Diffane (SIGCOMM’10)
  DevoFlow(SIGCOMM’11)
Data plane
2. Stress the control channel
1. Stress controller resources
Control plane
Data plane
Root Control
offload Control

## Slide 6: ONIX
ONIX’s view of network components
  Physical infrastructure: switches, routers, etc
  Connectivity infrastructure: channels for messages.
  Onix: A distributed system running the controller
  Control logic: network management applications running on top on Onix

## Slide 7: Onix architecture

## Slide 8: Onix NIB
Holds a collection of network entities
  Can be viewed as a centralized graph with notification mechanism
Updates to the NIB are asynchronous.

## Slide 9: Onix NIB API
Query: find entities
Create/destroy: create and remove entities
Access attributes: inspect and modify entities
Notification: receive update about changes
Synchronize: wait for updates being export to network elements and controllers
Configuration: configure how state is imported to and exported from the NIB
Pull: ask entities to be imported on-demand

## Slide 10: Onix abstraction
Global view: Observe and control a centralized network view (NIB) which contains all physical network elements
Flow: the first packet and subsequent packets with the same header are treated in the same way.
Switch: with flow tables <header: counters, actions>
Event-based operation: the controller operations are triggered by routers or applications.

## Slide 11: Onix API
The global view is represented as a network graph
Nodes represent physical network entities
Developers program over the network graph
Write flow entry
List ports
Register for updates
……

## Slide 12: Network Information Base
The NIB is the focal point of the system
  State for applications to access
  External state changes imported into it
  Local state changes exported from it

## Slide 13: Onix scalability
A single physical controller won’t work for large network
  NIB will overrun the memory in one server
  CPU and bandwidth for one server will not be enough
Onix solution: Partition, aggregation, and consistency.
  Partition:
    Each Onix instance may have connections to a subset of network elements
    Network control logic can configure to keep a subset of the NIB in memory

## Slide 14: Onix scalability
Partition, aggregation, and consistency.
  Aggregation:
    Each Onix instance can be configured to expose a subset of elements in its NIB as an aggregate element (reduce fidelity) to another Onix instance.
  Consistency and durability
    Control logic dictates the consistency requirement of the network state it manages
      Two storage options
        Replicated transactions (SQL) storage
        One-hop memory-based DHT
    Control logic resolve conflicts when necessary.

## Slide 15: Onix reliability
Network element and link failures
  Control logic reconfigures to deal with such failures
Management connectivity infrastructure failures
  Assumed reliable (remember Google B4 issue?)
Onix failures:
  Distributed coordination facilities to provide failover

## Slide 16: Onix Summary
Onix provides state distribution capability
The developers of management applications still have to understand the scalability implications of their design
One of the earlier SDN controllers: the controller functionality and application functionality are not clearly partitioned.

## Slide 17: Distributed SDN controller Research issues?

## Slide 18: Distributed SDN research issues
Network abstraction for distributed SDN
  Need concrete understanding of network abstraction in the current systems
Exploit existing distributed system techniques to address distributed network abstraction issues
  Consistency, usability, synchronization, fault tolerance, etc
Adapting distributed system techniques specifically to SDN controller
  No need to reinvent the wheel

## Slide 19: ONOS: Towards an Open, Distributed SDN OS
Earlier NOS dodges the distributed system issues.
Earlier distributed NOS may try to reinvent the wheel.
ONOS is a second generation of distributed NOS, separating distributed systems issues with network management issues
  We know how to distribute and maintain information in a distributed manner. Many systems are available.
  Distributed NOS can utilize the existing distributed information systems and focus on network management issues.

## Slide 20: Distributed system building blocks
Distributed storage system
  Cassandra
  RAMcloud (in memory storage)
Distributed graph database (Titan)
Distributed event notification(HazelCast)
Distributed coordination service (Zookeeper)
Distributed system data structures and algorithms
  Distributed hash table (DHT)
  Consensus algorithm
  Failure detector
  Checkpointing
  Transaction

## Slide 21: Onos architecture

## Slide 22: Onos abstraction: Global network view

## Slide 23: Onos summary
Use existing distributed system infrastructure.
Focus on making it efficient with known distributed system applications.
  E.g. how to maintain, lookup, and update the topology effectively

## Slide 24: Kandoo: A framework for efficient and scalable offloading of control applications

## Slide 25: Local Apps

## Slide 26: Local Apps

## Slide 27: Where to run the local apps

## Slide 28: Kandoo

## Slide 29: An example: Elephant flow rerouting

## Slide 30: An example: Elephant flow rerouting

## Slide 31: Kandoo variations

## Slide 32: Kandoo summary
2 levels of controller
Deal with the scalability issue by moving software closer to the data plane
Future: a generalized hierarchy
  Filling the gap between local and non-local apps
  Finding the right scope is quite challenging

## Slide 33: Devoflow
DevoFlow: scaling flow management for high-performance networks, SIGCOMM’2011.
OpenFlow is good; but fine-grain per flow management creates too much overhead
  Flow setup
  Statistics collection
Devoflow – a new paradigm to reduce the control and overhead while providing fine control for important flows.

## Slide 34: Dilemma
Control dilemma:
  Role of controller: visibility and mgmt capability however, per-flow setup too costly
  Flow-match wildcard (existing hardware), hash-based: much less load, but no effective control
Statistics-gathering dilemma:
  Pull-based mechanism: counters of all flows full visibility but demand high BW
  Wildcard counter aggregation: much less entries but lose trace of elephant flows
Aim to strike in between

## Slide 35: Main Concept of DevoFlow
Devolving most flow controls to switches
  Use the default wildcard match
Maintain partial visibility
Keep trace of significant flows
Default v.s. special actions:
  Security-sensitive flows: categorically inspect
  Normal flows: may evolve or cover other flows become security-sensitive or significant
  Significant flows: special attention
Collect statistics by sampling, triggering, and approximating

## Slide 36: Design Principles of DevoFlow
Try to stay in data-plane, by default
Provide enough visibility:
  Esp. for significant flows & sec-sensitive flows
  Otherwise, aggregate or approximate statistics
Maintain simplicity of switches

## Slide 37: Mechanisms
Control
  Rule cloning
  Local actions
Statistics-gathering
  Sampling
  Triggers and reports
  Approximate counters

## Slide 38: Rule Cloning – identify elephant flow
ASIC clones a wildcard rule as an exact match rule for new microflows
  Timeout or output port by probability

## Slide 39: Rule Cloning
ASIC clones a wildcard rule as an exact match rule for new microflows
  Timeout or output port by probability

## Slide 40: Rule Cloning
ASIC clones a wildcard rule as an exact match rule for new microflows
  Timeout or output port by probability

## Slide 41: Local Actions
Rapid re-routing: fallback paths predefined Recover almost immediately
Multipath support: based on probability dist. Adjusted by link capacity or loads

## Slide 42: Statistics-Gathering
Sampling
  Pkts headers send to controller with1/1000 prob.
Triggers and reports
  Set a threshold per rule
  When exceeds, enable flow setup at controller
Approximate counters
  Maintain list of top-k largest flows

## Slide 43: DevoFlow Summary
Per-flow control imposes too many overheads
Balance between
  Overheads and network visibility
  Effective traffic engineering, network management
Switches with limited resources
  Flow entries, control-plane BW
  Hardware capability, power consumption