## Slide 1: Networks without SDN
Challenges facing network managers

## Slide 2: Routing and Switch are complicated
Multiple routing and switching protocols
  Each router has its own control plane
  Protocols are designed to make routers understand network topology
  No one protocol that can handle all the network demands
    BGP, OSPF, EIGRP, STP, PIM
  IP header examine and routing table look up often slow things down
  Various technology invented to speed up
    MPLS, FIB, QoS, NP on each module, VSS

## Slide 3: Routing and Switch are complicated
VPN, GRE tunnels, DMVPN
Other network devices like firewalls, IPS, wireless
Branches, remote campuses, DR sites, Campus dorms
PCI compliance requirements
Demand for research fast lane
Tens of thousands lines of router and firewall configures

## Slide 4: Network operations are expensive
The demand for wire speed routing and high capacity resulting very expensive network operations
  The two ISP grade routers FSU use cost $1.4 million
  Firewalls also cost half million
  IPS devices add another half million
  Yearly maintenance fee over quarter million

## Slide 5: Difficult to Operate
Difficult to troubleshoot
  There are so many layers, protocols, and extremely detailed configurations and settings
Difficult to make modification
  Once a protocol is in place, it’s very hard to change it
  Florida Highway Safety example
Difficult to adapt dynamic demands
  Network design principle is to make network predictable
  Demands are dynamic and sometime unpredictable

## Slide 6: Current Solutions
Build a network that with high speed 10g, 40g, and hope network will not outgrow it in five years
Define network flows to limit cross network traffics
Rely on vendors to provide solutions
  Wireless system performance
  Data Center traffic congestions

## Slide 7: Why Adopting SDN is Slow
Most network admins cannot program
Most programmers lack understanding of networks
Vendors are concerned
  Routers/switches become commodity goods
SDN is not mature
Security concerns
Performance concerns
Reliability concerns
Programmer/netadmin turnovers
Someone to blame