## Slide 1: Example: Obstacle Modeling for Wireless Transmissions
Andy Wang
CIS 5930
Computer Systems
Performance Analysis

## Slide 2: Motivation
Typical studies of mobile wireless networks assume an open field
  No physical obstacles (e.g., no buildings)
  Not reflective of urban settings

## Slide 3: Goals
Validate the open-field wireless signal attenuation model used in NS-2
Model the signal attenuation caused by physical obstacles

## Slide 4: Services
Wireless network signal transmissions
  Broadcast signals
  Listen to signals

## Slide 5: Outcomes
Sufficient signal strength for data transmission
  Successful transmissions
  Unsuccessful transmissions (e.g., due to interferences)
Insufficient signal strength for data transmission
  No service

## Slide 6: Metric
Signal strength
  dBm (decibels relative to 1 mWatt)
    Decibels are ratios (no units)
      Log transformed
        1 mW = 10log10(1mW/1mW) = 0 dBm
      Tricky unit conversions
        (XWatts* 1000)mWatts
        (XdBW + 30)dBm
        Note: 30 = 10log10(1000mW/1mW)
    Measured in electric power

## Slide 7: Implicit Assumptions
Bandwidth, latency, and packet loss rate are largely a function of signal strength
Not measured

## Slide 8: Parameters
Open field
  Type of base station and receiver
  Distance between sender and receiver
  Presence of interference
    Self interference
      Ground surface, signal reflections
    Other transmissions
  Weather conditions
  Height of transmission source

## Slide 9: Parameters
With obstacles
  Location of obstacles
  Type of obstacles
    Different building codes
Problem
  Difficult to quantify obstacles and their relationship to the base station and receiver

## Slide 10: Factors and Evaluation Techniques
Factors
  Distance between sender and receiver
  Presence of obstacles
Evaluation techniques
  Empirical measurements

## Slide 11: Workloads
One sender, one receiver
  Continuous transmissions
Open field
  Mike Long Track on campus
With obstacles
  Around a block in downtown Tallahassee
  Around Keen Building

## Slide 12: Workloads
Problems
  No interferences
  Only measured two scenarios

## Slide 13: Experimental Settings
Base station
  802.11b Linksys
Receiver
  Linux laptop with wireless PCI card
  Used Wavemon to log transmission signals

## Slide 14: Downtown Tallahassee

## Slide 15: Keen Building GPS Coordinates
30.445825, -84.301432
30.445806, -84.301347
30.446075, -84.301314
30.446056, -84.301239
30.446093, -84.301389
30.445973, -84.301486
30.445862, -84.301486
30.446010, -84.301143
30.445779, -84.301229
30.445880, -84.301175
30.445862,
-84.300896
30.445723,
-84.300939
30.445779,
-84.301089
30.445917,
-84.301035
1
3
2
g
f
e
d
c
b
a
h
j
k
i
Possible base station locations

## Slide 16: Experimental Design
Ideally, start with 23r factorial design to identify major factors and interactions

## Slide 17: Experimental Design
What really happened
  22 factorial design

## Slide 18: Experimental Design
Problems
  Cumbersome setup
    Needed portable battery
    Network measurements drain batteries quickly
  Missing data points for temperature
  Ground surfaces correlate to the presence of obstacles

## Slide 19: Experimental Design
Open-field model validation
  Simple design
    Varied the distance between base station and receiver
Obstacle model
  Simple design
    Varied the distance between base station and receiver

## Slide 20: Data Analysis
22 factorial design (example 1)
Fractions of variations explained
  * 36% due to the presence of obstacles
  * 60% due to distance
  * 4% due to the interaction between the two
    Okay to create separate models
      With obstacles
      Without obstacles

## Slide 21: Open-field Data Analysis
Simple linear regression (example 2)
  Signal = -46 – 0.57(distance)
  R2 = 0.78
  Both coefficients are significant
Chart: distance (meters)
| 0 | 12 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80
measured | -26 | -56 | -65 | -69 | -72 | -73 | -76 | -76 | -79 | -80 | -81 | -82 | -83 | -84
predicted | -45.5481 | -52.3579 | -59.7353 | -62.5727 | -65.4101 | -68.2476 | -71.085 | -73.9224 | -76.7599 | -79.5973 | -82.4348 | -85.2722 | -88.1096 | -90.9471
90% confidence interval | -53.3959 | -62.0428 | -71.4102 | -75.0131 | -78.6159 | -82.2188 | -85.8216 | -89.4245 | -93.0274 | -96.6302 | -100.2331 | -103.8359 | -107.4388 | -111.0416
y_hat_max | -37.7002 | -42.673 | -48.0603 | -50.1323 | -52.2043 | -54.2764 | -56.3484 | -58.4204 | -60.4924 | -62.5644 | -64.6365 | -66.7085 | -68.7805 | -70.8525

## Slide 22: Open-field Data Analysis
However, ANOVA
not satisfactory
Chart: predicted dBm
| -45.548061232419002 | -52.357914367860758 | -59.735255264589327 | -62.572694071023392 | -65.410132877457457 | -68.247571683891522 | -71.085010490325587 | -73.922449296759652 | -76.759888103193717 | -79.597326909627782 | -82.434765716061847 | -85.272204522495912 | -88.109643328929977 | -90.947082135364042
ei | 19.5481 | -3.6421 | -5.2647 | -6.4273 | -6.5899 | -4.7524 | -4.915 | -2.0776 | -2.2401 | -0.40267 | 1.4348 | 3.2722 | 5.1096 | 6.9471
Chart: experimental number
ei | 19.5481 | -3.6421 | -5.2647 | -6.4273 | -6.5899 | -4.7524 | -4.915 | -2.0776 | -2.2401 | -0.40267 | 1.4348 | 3.2722 | 5.1096 | 6.9471
Chart: normal quantiles
| -1.8055703758353747 | -1.2412086960391087 | -0.91886662364998406 | -0.67234481227438181 | -0.46191319854665858 | -0.27071369175356519 | -8.923994280381807E-2 | 8.923994280381807E-2 | 0.27071369175356519 | 0.46191319854665913 | 0.67234481227438181 | 0.91886662364998406 | 1.2412086960391087 | 1.8055703758353747
e | -6.5899 | -6.4273 | -5.2647 | -4.915 | -4.7524 | -3.6421 | -2.2401 | -2.0776 | -0.40267 | 1.4348 | 3.2722 | 5.1096 | 6.9471 | 19.5481

## Slide 23: Try Transforms (Ex.3)
distance’ = 1/distance
  Signal = -91 + 682/distance
  R2 = 0.98
  Both coefficients are significant
Chart: distance (meters)
| 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80
measured | -65 | -69 | -72 | -73 | -76 | -76 | -79 | -80 | -81 | -82 | -83 | -84
predicted | -64.1311 | -68.6787 | -71.927 | -74.3633 | -76.2581 | -77.774 | -79.0142 | -80.0478 | -80.9223 | -81.6719 | -82.3216 | -82.89
90% confidence interval | -67.6504 | -71.8264 | -74.8093 | -77.0465 | -78.7866 | -80.1786 | -81.3175 | -82.2666 | -83.0697 | -83.7581 | -84.3546 | -84.8767
y_hat_max | -60.6119 | -65.5311 | -69.0447 | -71.68 | -73.7296 | -75.3693 | -76.7109 | -77.8289 | -78.7749 | -79.5858 | -80.2885 | -80.9034

## Slide 24: Try Transforms (Ex.3)
distance’ = 1/distance
  R2 = 0.98
  Weird error patterns
Chart: normal quantiles
| -1.7341562983883385 | -1.1492082681575793 | -0.81009162949687807 | -0.54653689842413589 | -0.31729887872592571 | -0.10416467748839144 | 0.10416467748839034 | 0.31729887872592571 | 0.54653689842413589 | 0.81009162949687807 | 1.1492082681575793 | 1.7341562983883385
e | -1.11 | -0.86886 | -0.67843 | -0.32809 | -0.32125 | -0.077698 | -0.072963 | 0.014216 | 0.047762 | 0.25809 | 1.3633 | 1.774
Chart: experimental number
ei | -0.86886 | -0.32125 | -0.072963 | 1.3633 | 0.25809 | 1.774 | 0.014216 | 0.047762 | -0.077698 | -0.32809 | -0.67843 | -1.11
Chart: predicted dBm
| -64.131140978834424 | -68.678747126165931 | -71.927037231402721 | -74.363254810330318 | -76.258090705051771 | -77.773959420828945 | -79.014215642828447 | -80.047762494494691 | -80.922302138212302 | -81.671907547113094 | -82.321565568160452 | -82.890016336576892
ei | -0.86886 | -0.32125 | -0.072963 | 1.3633 | 0.25809 | 1.774 | 0.014216 | 0.047762 | -0.077698 | -0.32809 | -0.67843 | -1.11

## Slide 25: Try Transforms (Ex. 4)
distance’ = 1/distance2
  Signal = -84 + 12925/distance2
  R2 = 0.92
  Both coefficients are significant
Chart: distance (meters)
| 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80
measured | -65 | -69 | -72 | -73 | -76 | -76 | -79 | -80 | -81 | -82 | -83 | -84
predicted | -62.9116 | -69.2305 | -73.0406 | -75.5136 | -77.209 | -78.4217 | -79.319 | -80.0014 | -80.5325 | -80.9539 | -81.2939 | -81.5722
90% confidence interval | -67.7447 | -73.0286 | -76.2146 | -78.2824 | -79.7002 | -80.7142 | -81.4645 | -82.0352 | -82.4793 | -82.8317 | -83.116 | -83.3487
y_hat_max | -58.0785 | -65.4325 | -69.8667 | -72.7447 | -74.7178 | -76.1292 | -77.1734 | -77.9676 | -78.5857 | -79.0762 | -79.4719 | -79.7957

## Slide 26: Try Transforms (Ex. 4)
distance’ = 1/distance2
  R2 = 0.92
  Weird error patterns
Chart: normal quantiles
| -1.7341562983883385 | -1.1492082681575793 | -0.81009162949687807 | -0.54653689842413589 | -0.31729887872592571 | -0.10416467748839144 | 0.10416467748839034 | 0.31729887872592571 | 0.54653689842413589 | 0.81009162949687807 | 1.1492082681575793 | 1.7341562983883385
e | -2.4278 | -2.0884 | -1.7061 | -1.0461 | -0.46747 | 0.0014213 | 0.23054 | 0.31897 | 1.0406 | 1.209 | 2.4217 | 2.5136
Chart: experimental number
ei | -2.0884 | 0.23054 | 1.0406 | 2.5136 | 1.209 | 2.4217 | 0.31897 | 0.0014213 | -0.46747 | -1.0461 | -1.7061 | -2.4278
Chart: predicted dBm
| -62.911623999709093 | -69.230540656758905 | -73.040648103031984 | -75.513554378257297 | -77.208970779296536 | -78.421692157922266 | -79.318968828232116 | -80.001421322184711 | -80.532529836258959 | -80.953948183752985 | -81.293927002035815 | -81.572174752559306
ei | -2.0884 | 0.23054 | 1.0406 | 2.5136 | 1.209 | 2.4217 | 0.31897 | 0.0014213 | -0.46747 | -1.0461 | -1.7061 | -2.4278

## Slide 27: Try Transforms (Ex. 5)
distance’ = 1/sqrt(distance)
  Signal = -107 + 211/sqrt(distance)
  R2 = 0.99
  Both coefficients are significant
Chart: distance (meters)
| 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80
measured | -65 | -69 | -72 | -73 | -76 | -76 | -79 | -80 | -81 | -82 | -83 | -84
predicted | -64.9556 | -68.638 | -71.5 | -73.807 | -75.718 | -77.3345 | -78.7253 | -79.9384 | -81.0087 | -81.9622 | -82.8186 | -83.5935
90% confidence interval | -68.7055 | -72.1996 | -74.9153 | -77.1043 | -78.9176 | -80.4515 | -81.7712 | -82.9222 | -83.9378 | -84.8425 | -85.6552 | -86.3904
y_hat_max | -61.2057 | -65.0764 | -68.0848 | -70.5097 | -72.5184 | -74.2176 | -75.6795 | -76.9546 | -78.0796 | -79.0819 | -79.9821 | -80.7966

## Slide 28: Try Transforms (Ex. 5)
distance’ = 1/sqrt(distance)
  R2 = 0.99
  Errors not normally
  distributed
Chart: normal quantiles
| -1.7341562983883385 | -1.1492082681575793 | -0.81009162949687807 | -0.54653689842413589 | -0.31729887872592571 | -0.10416467748839144 | 0.10416467748839034 | 0.31729887872592571 | 0.54653689842413589 | 0.81009162949687807 | 1.1492082681575793 | 1.7341562983883385
e | -0.49996 | -0.40651 | -0.36197 | -0.28204 | -0.27466 | -0.18136 | -0.061558 | -0.044439 | -0.03781 | 0.0087294 | 0.80704 | 1.3345
Chart: experimental number
ei | -0.044439 | -0.36197 | -0.49996 | 0.80704 | -0.28204 | 1.3345 | -0.27466 | -0.061558 | 0.0087294 | -0.03781 | -0.18136 | -0.40651
Chart: predicted dBm
| -64.955561351014211 | -68.638027567393664 | -71.500038645618076 | -73.80703935352301 | -75.717961844287899 | -77.334545461345385 | -78.725339777601675 | -79.93844229443765 | -81.008729417978145 | -81.962189735681164 | -82.81863897067629 | -83.593485580442916
ei | -0.044439 | -0.36197 | -0.49996 | 0.80704 | -0.28204 | 1.3345 | -0.27466 | -0.061558 | 0.0087294 | -0.03781 | -0.18136 | -0.40651

## Slide 29: Try Transforms (Ex. 6)
distance’ = log10(distance)
  Signal= -18 – 35*log(distance)
  R2 = 0.99
Chart: distance (meters)
| 12.000000000000005 | 25.000000000000018 | 30.000000000000004 | 35.000000000000007 | 40 | 45.000000000000014 | 50.000000000000014 | 55.000000000000014 | 60.000000000000036 | 65.000000000000043 | 70.000000000000028 | 75.000000000000043 | 80.000000000000043
measured | -56 | -65 | -69 | -72 | -73 | -76 | -76 | -79 | -80 | -81 | -82 | -83 | -84
predicted | -55.2727 | -66.396 | -69.159 | -71.4952 | -73.5188 | -75.3038 | -76.9006 | -78.345 | -79.6636 | -80.8767 | -81.9998 | -83.0454 | -84.0235
90% confidence interval | -59.3754 | -70.9759 | -73.8575 | -76.2939 | -78.4043 | -80.2659 | -81.9311 | -83.4375 | -84.8127 | -86.0778 | -87.2491 | -88.3395 | -89.3596
y_hat_max | -51.1699 | -61.816 | -64.4606 | -66.6965 | -68.6333 | -70.3418 | -71.87 | -73.2525 | -74.5146 | -75.6756 | -76.7505 | -77.7512 | -78.6873

## Slide 30: Try Transforms (Ex. 6)
distance’ = log10(distance)
  R2 = 0.99
Chart: normal quantiles
| -1.7715030999501589 | -1.1974821718495816 | -0.86736957687875682 | -0.61305163637170978 | -0.39412551726874989 | -0.19317456337086084 | 0 | 0.19317456337086084 | 0.39412551726874989 | 0.61305163637170978 | 0.86736957687875682 | 1.1974821718495816 | 1.7715030999501595
e | -0.72732 | -0.69617 | -0.65501 | -0.50483 | -0.33636 | -0.12331 | -0.0002119 | 0.02345 | 0.045372 | 0.15903 | 0.51884 | 0.90057 | 1.396
Chart: experimental number
ei | -0.72732 | 1.396 | 0.15903 | -0.50483 | 0.51884 | -0.69617 | 0.90057 | -0.65501 | -0.33636 | -0.12331 | -0.0002119 | 0.045372 | 0.02345
Chart: predicted dBm
| -55.272683651578042 | -66.395952929695909 | -69.159027783899717 | -71.495174286150529 | -73.518836433927163 | -75.303832952148724 | -76.900566747972363 | -78.344988163617643 | -79.66364160217617 | -80.876685175981748 | -81.999788104426997 | -83.045371916221384 | -84.023450252203631
ei | -0.72732 | 1.396 | 0.15903 | -0.50483 | 0.51884 | -0.69617 | 0.90057 | -0.65501 | -0.33636 | -0.12331 | -0.0002119 | 0.045372 | 0.02345

## Slide 31: Validate Open-field Model
dBmr = -18 – 35*log(distance)
NS-2 model
  * Wattr = Watts*α/distance2
  * dBmr = 10*log(Powers*α/distance2) + 30
  = dBms + 10*log(α) – 20*log(distance)
  = (dBms + A) – B*log(distance)

## Slide 32: Obstacle Data Analysis
Simple linear regression
  Signal = -50 – 0.64(distance)
  R2 = 0.48
  The second coefficient is not significant

## Slide 33: Obstacle Data Analysis (Ex. 7)
ANOVA
  Weird error patterns
Chart: predicted dBm
Chart: experiment number
Chart: normal quantiles

## Slide 34: Try Log Transform (Ex. 10)
R2 = 0.24
ANOVA shows
patterns
Chart: normal quantiles
Chart: experiment number
Chart: predicted dBm

## Slide 35: Analyze a Subset of Data
30.445825, -84.301432
30.445806, -84.301347
30.446075, -84.301314
30.446056, -84.301239
30.446093, -84.301389
30.445973, -84.301486
30.445862, -84.301486
30.446010, -84.301143
30.445779, -84.301229
30.445880, -84.301175
30.445862,
-84.300896
30.445723,
-84.300939
30.445779,
-84.301089
30.445917,
-84.301035
1
3
2
g
f
e
d
c
b
a
h
j
k
i
Possible base station locations
Focus on this data set

## Slide 36: Keen Building Location 1 (Ex. 13)
Signal = -27 – 36*log10(distance)
R2 = 0.70
Both coefficients are significant
Chart: distance (meters)
| 25.000000000000018 | 30.000000000000004 | 35.000000000000007 | 30.000000000000004 | 35.000000000000007 | 30.000000000000004 | 25.000000000000018 | 50.000000000000014 | 55.000000000000014 | 70.000000000000028 | 70.000000000000028 | 25.000000000000018 | 30.000000000000004 | 35.000000000000007 | 30.000000000000004 | 35.000000000000007 | 30.000000000000004 | 25.000000000000018 | 50.000000000000014 | 55.000000000000014 | 70.000000000000028 | 70.000000000000028
measured | -80 | -84 | -85 | -89 | -82 | -79 | -72 | -93 | -88 | -96 | -90 | -73 | -76 | -82 | -88 | -80 | -80 | -74 | -91 | -89 | -93 | -91
predicted | -77.5779 | -80.4173 | -82.818 | -80.4173 | -82.818 | -80.4173 | -77.5779 | -88.3729 | -89.8572 | -93.6131 | -93.6131 | -77.5779 | -80.4173 | -82.818 | -80.4173 | -82.818 | -80.4173 | -77.5779 | -88.3729 | -89.8572 | -93.6131 | -93.6131
90% confidence interval | -104.6504 | -108.2063 | -111.2128 | -108.2063 | -111.2128 | -108.2063 | -104.6504 | -118.1693 | -120.0282 | -124.7318 | -124.7318 | -104.6504 | -108.2063 | -111.2128 | -108.2063 | -111.2128 | -108.2063 | -104.6504 | -118.1693 | -120.0282 | -124.7318 | -124.7318
y_hat_max | -50.5053 | -52.6283 | -54.4233 | -52.6283 | -54.4233 | -52.6283 | -50.5053 | -58.5764 | -59.6862 | -62.4943 | -62.4943 | -50.5053 | -52.6283 | -54.4233 | -52.6283 | -54.4233 | -52.6283 | -50.5053 | -58.5764 | -59.6862 | -62.4943 | -62.4943

## Slide 37: Keen Building Location 1
ANOVA so so
Errors not quite
normally distributed
Chart: predicted dBm
| -77.577858337168749 | -80.417318888875258 | -82.818048578140136 | -80.417318888875258 | -82.818048578140136 | -80.417318888875258 | -77.577858337168749 | -88.372874079332533 | -89.85722678281607 | -93.61306432030392 | -93.61306432030392 | -77.577858337168749 | -80.417318888875258 | -82.818048578140136 | -80.417318888875258 | -82.818048578140136 | -80.417318888875258 | -77.577858337168749 | -88.372874079332533 | -89.85722678281607 | -93.61306432030392 | -93.61306432030392
ei | -2.4221 | -3.5827 | -2.182 | -8.5827 | 0.81805 | 1.4173 | 5.5779 | -4.6271 | 1.8572 | -2.3869 | 3.6131 | 4.5779 | 4.4173 | 0.81805 | -7.5827 | 2.818 | 0.41732 | 3.5779 | -2.6271 | 0.85723 | 0.61306 | 2.6131
Chart: experiment number
ei | -2.4221 | -3.5827 | -2.182 | -8.5827 | 0.81805 | 1.4173 | 5.5779 | -4.6271 | 1.8572 | -2.3869 | 3.6131 | 4.5779 | 4.4173 | 0.81805 | -7.5827 | 2.818 | 0.41732 | 3.5779 | -2.6271 | 0.85723 | 0.61306 | 2.6131
Chart: normal quantiles
| -2.0035550572994825 | -1.4904145645700559 | -1.2065648405710736 | -0.99645157842515553 | -0.82338158450904175 | -0.67234481227438181 | -0.53555493189607772 | -0.40833987545174932 | -0.2875786604797087 | -0.17098729305342714 | -5.6742971011575931E-2 | 5.6742971011575931E-2 | 0.17098729305342769 | 0.2875786604797087 | 0.40833987545174877 | 0.53555493189607772 | 0.67234481227438181 | 0.82338158450904175 | 0.99645157842515553 | 1.2065648405710736 | 1.4904145645700555 | 2.0035550572994834
ei | -8.5827 | -7.5827 | -4.6271 | -3.5827 | -2.6271 | -2.4221 | -2.3869 | -2.182 | 0.41732 | 0.61306 | 0.81805 | 0.81805 | 0.85723 | 1.4173 | 1.8572 | 2.6131 | 2.818 | 3.5779 | 3.6131 | 4.4173 | 4.5779 | 5.5779

## Slide 38: Downtown Data Set (Ex. 15)
Signal = -16 – 39*log10(distance)
R2 = 0.71
Only the second coefficient is significant
Chart: distance (meters)
| 40 | 81.000000000000028 | 87 | 77.000000000000014 | 65.000000000000043 | 33.000000000000014
measured | -76 | -86 | -97 | -95 | -86 | -80
predicted | -79.7502 | -91.7964 | -93.0164 | -90.9318 | -88.0393 | -76.4659
90% confidence interval | -170.1314 | -190.3538 | -192.4019 | -188.9023 | -184.0466 | -164.6179
asdfasd | 10.631 | 6.761 | 6.3691 | 7.0388 | 7.968 | 11.6861

## Slide 39: Downtown Data Set
ANOVA
Chart: normal quantiles
| -1.3832136965638231 | -0.67234481227438181 | -0.20950688738296824 | 0.2095068873829688 | 0.67234481227438181 | 1.3832136965638224
ei | -4.0682 | -3.9836 | -3.5341 | 2.0393 | 3.7502 | 5.7964
Chart: experiment number
ei | 3.7502 | 5.7964 | -3.9836 | -4.0682 | 2.0393 | -3.5341
Chart: predicted dBm
| -79.750226220014184 | -91.796411949713885 | -93.016430257613806 | -90.931771913304857 | -88.039297189895294 | -76.465862469458017
ei | 3.7502 | 5.7964 | -3.9836 | -4.0682 | 2.0393 | -3.5341

## Slide 40: Unified Model (Ex. 17)
Signal = -22 - 5.3*(if ob) – 33*log10(dist)
R2 = 0.32
All coefficients are significant
Passed F test
The presence of obstacles costs 5.3 dBm

## Slide 41: Unified Model (Ex. 17)
Signal = -22 - 5.3*(if ob) – 33*log10(dist)
R2 = 0.32
All coefficients are significant
Chart: distance (meters)

## Slide 42: Unified Model
ANOVA not so good…
Chart: normal quantiles
Chart: experiment number
Chart: predicted dBm

## Slide 43: Problems
Need better ways to describe the relationship between obstacles, sender, and receiver

## Slide 44: White Slide