## Slide 1: CUDA programming (continue)
Acknowledgement: the lecture materials are based on the materials in NVIDIA teaching center CUDA course materials, including materials from Wisconsin (Negrut), North Carolina Charlotte (Wikinson/Li) and NCSA (Kindratenko).

## Slide 2: Topics
Implementing MM on GPU
  Memory hierarchy
  synchronization

## Slide 3: More about threads/block
See matrixmul.cu. Following is the execution trace: A warp can only contain threads in one block. We need at least 32 threads in one block!!
<gpu1:816> time ./a.out
3.318u 3.402s 0:06.85 97.9% 0+0k 0+0io 0pf+0w
<gpu1:817> time ./a.out 8
5.526u 3.200s 0:08.84 98.6% 0+0k 0+0io 0pf+0w
<gpu1:818> time ./a.out 4
18.193u 3.129s 0:21.41 99.5% 0+0k 0+0io 0pf+0w
<gpu1:819> time ./a.out 2
61.975u 3.227s 1:05.29 99.8% 0+0k 0+0io 0pf+0w
<gpu1:820> time ./a.out 1
231.894u 3.917s 3:55.94 99.9% 0+0k 0+0io 0pf+0w
<gpu1:821>

## Slide 4: CUDA extension to declare kernel routines
__global__ indicates routine can only be called from host and only executed on device
__device__ indicates routine can only be called from device and only executed on device
__host__ indicates routine can only be called from host and only executed on host

## Slide 5: Routine for device
__global__ routine must have a void return value.
Generally cannot call C library routines except CUDA built-in math routines such as sin, cos, etc.
  Check NVIDIA CUDA programming guide for details.
CUDA also has device only routines.

## Slide 6: Example for 2D grid/blocks
Matrix multiply:
for (i=0; i<N; i++)
for(j=0; j<K; j++)
for (k=0; k<M; k++)
c[i][j] += a[i][k] * b[k][j]
2D mesh must be stored in the linear (1D) array (column major order)
    c[i][j] = c[i+N*j] = *(c+i+N*j);
    a[i][k] = a[i+K*j] = *(a+i+K*k);

## Slide 7: First cut
Using one thread to compute one c[i][j], a total of N*K threads will be needed.
  N*K blocks of threads and 1 thread each block
  See mm0.cu
  // kernel MM routine
  __global__ void mmkernel(float *a, float *b, float *c, int N, int M, int K)
  {
  int i = blockIdx.x, j = blockIdx.y;
  float sum = 0.0f;
  for (int k = 0; k< M; k++) sum += a[i+N*k] * b[k+K*j];
  c [i+N*j] = sum;
  }
dim3 dimBlock(1); dim3 dimGrid(N, N);
mmkernel<<<dimGrid, dimBlock>>> (dev_A, dev_B, dev_C, N, M, K);

## Slide 8: Another try
  See mm0_1.cu
  // kernel MM routine
  __global__ void mmkernel(float *a, float *b, float *c, int N, int M, int K)
  {
  int i = threadIdx.x, j = threadIdx.y;
  float sum = 0.0f;
  for (int k = 0; k< M; k++) sum += a[i+N*k] * b[k+K*j];
  c [i+N*j] = sum;
  }
dim3 dimBlock(1); dim3 dimGrid(N, K);
mmkernel<<<dimBlock, dimGrid>>> (dev_A, dev_B, dev_C, N, M, K);
Another thing wrong here?

## Slide 9: Second try
Add threads to blocks to exploit the SIMT (SIMD) support
  need to have at least 32 threads per block to have one 32 thread warp.
  The more the better (GPU will have more options).

## Slide 11: CPU and GPU memory
Mm with blocks of threads
__global__ void mmkernel(float *a, float *b, float *c, int N, int M, int K)
{
int i = blockIdx.x * BLOCK_SIZE + threadIdx.x, j = blockIdx.y;
float sum = 0.0f;
for (int k = 0; k< M; k++) sum += a[i+N*k] * b[k+K*j];
c [i+N*j] = sum;
}
dim3 dimBlock(BLOCK_SIZE);
dim3 dimGrid(N/BLOCK_SIZE, K);
mmkernel<<<dimGrid, dimBlock>>> (dev_A, dev_B, dev_C, N, M, K);
Notice the relationship between index calculation and kernel invocation.
Try mm1.cu with different BLOCK_SIZE’s

## Slide 12: CUDA memory hierarchy
Register: per-thread basis
  Private per thread
  Can spill into local memory (perf. hit)
Shared Memory: per-block basis
  Shared by threads of the same block
  Used for: Inter-thread communication
Global Memory: per-application basis
  Available for use to all threads
  Used for: Inter-thread communication
  Also used for inter-grid communication
Thread
Register
Grid 0
. . .
Global
Device
Memory
. . .
Grid 1
Sequential
Grids
in Time
Block
Shared
Memory
12

## Slide 13: CUDA memory allocation
Memory Declaration Scope Lifetime
Registers Auto variables Thread Kernel
other than arrays
Local Auto arrays Thread Kernel
Shared __shared__ Block Kernel
Global __device__ Grid Application
Constant __constant__ Grid Application

## Slide 14: An example
__global__ float A[1000];
__global__ void mmkernel(float *a, float *b, float *c, int N, int M, int K)
{
int i = blockIdx.x * BLOCK_SIZE + threadIdx.x;
int j = blockIdx.y;
int tx = threadIdx.x;
__shared__ float cb[BLOCK_SIZE];
int workb[BLOCK_SIZE];
……
}
Which type of variables are A, i, j, cb, workb?

## Slide 15: MM with shared memory
In mm1.cu, threads use register variables and global arrays
A block of BLOCK_SIZE threads is used to compute: BLOCK_SIZE c items: c[0][0], c[1][0], c[2][0], …. C[BLOCK_SIZE][0]
  The calculation:
    C[0][0] = A[0][0] * B[0][0] + A[0][1]*B[1][0] + A[0][2] * B[2][0] …
    C[1][0] = A[1][0] * B[0][0] + A[1][1]*B[1][0] + A[1][2] * B[2][0] …
    C[2][0] = A[2][0] * B[0][0] + A[2][1]*B[1][0] + A[2][2] * B[2][0] …
  A matrix has different values in different threads – can’t use shared memory
  B matrix has the same items
    Put B in shared memory may reduce the (global) memory traffic.
    Shared memory in GPU is limited, can’t hold the whole column: need to reduce the memory footprint. How?
      for(k=0; i<M; k++) C[i][j] += A[i][k]*B[k][j]

## Slide 16: MM with shared memory
for(k=0; i<M; k++) C[i][j] += A[i][k]*B[k][j]
For (ks=0; ks < M; ks+=TSIZE)
for(k=ks; k<ks+TSIZE; k++) C[i][j] += A[i][k] * B[k][j];
For(ks=0; ks<M; ks+=TSIZE)
Forall (k=ks; k<ks+TSIZE; k++) workB[k][j] = B[k][j];
for (k=ks; k<ks+TSIZE;k++) C[i][j] += A[i][k] * workB[k][j];

## Slide 17: MM with shared memory
__global__ void mmkernel(float *a, float *b, float *c, int N, int M, int K)
{
int i = blockIdx.x * BLOCK_SIZE + threadIdx.x;
int j = blockIdx.y;
int tx = threadIdx.x;
__shared__ float cb[BLOCK_SIZE];
float sum = 0.0f;
for (int ks = 0; ks < M; ks+= BLOCK_SIZE) {
cb[tx] = b[ks+tx+M*j]; // copy from global to shared, all threads parallel read
for (int k = ks; k< ks+BLOCKINGSIZE; k++) sum += a[i+N*k] * cb[k-ks];
}
c [i+N*j] = sum;
}
Any problem here?

## Slide 18: MM with shared memory
__global__ void mmkernel(float *a, float *b, float *c, int N, int M, int K)
{
int i = blockIdx.x * BLOCK_SIZE + threadIdx.x;
int j = blockIdx.y;
int tx = threadIdx.x;
__shared__ float cb[BLOCK_SIZE];
float sum = 0.0f;
for (int ks = 0; ks < M; ks+= BLOCK_SIZE) {
cb[tx] = b[ks+tx+M*j]; // all BLOCK_SIZE threads parallel read
for (int k = ks; k< ks+BLOCKINGSIZE; k++) sum += a[i+N*k] * cb[k-ks];
}
c [i+N*j] = sum;
}
True dependence due to shared memory
Anti-dependence

## Slide 19: MM with shared memory
__global__ void mmkernel(float *a, float *b, float *c, int N, int M, int K)
{
int i = blockIdx.x * BLOCK_SIZE + threadIdx.x;
int j = blockIdx.y;
int tx = threadIdx.x;
__shared__ float cb[BLOCK_SIZE];
float sum = 0.0f;
for (int ks = 0; ks < M; ks+= BLOCK_SIZE) {
cb[tx] = b[ks+tx+M*j]; // all BLOCK_SIZE threads parallel read
__syncthreads(); // barrier among all threads in a block
for (int k = ks; k< ks+BLOCKINGSIZE; k++) sum += a[i+N*k] * cb[k-ks];
__syncthreads(); // barrier among all threads in a block
}
c [i+N*j] = sum;
}
See mm2.cu

## Slide 20: More schemes to improve MM performance
Compute multiple points in each threads
  See mm3.cu
Using 2D block and 2D grid.

## Slide 21: More information about __syncthreads()
All threads must reach the barrier before any thread can move on.
  Threads arrives early must wait
__syncthreads() is kernel only.

## Slide 22: More information about __syncthreads()
Only synchronize within a block.
Barriers in different blocks are independent.
Barrier
Block 0
Continue
Barrier
Block n-1
Continue
Separate barriers

## Slide 23: More information about __syncthreads()
CUDA requires threads to synchronize using the exact the same __syncthreads() calls. Cannot do
    if ... __syncthreads()
    else … __syncthreads()
What if we want synchronize among all threads?
  Make separate kernel invocations.