## Slide 1: MISP Assembly

## Slide 2: Constant or Immediate Operands
Many times we use a constant in an operation
  For example, i++, i--, i += 4, and so on
Since constant operands occur frequently, we should include constants inside arithmetic operations so that they are much faster
  MIPS has an add instruction that allows one operand to be a constant
  The constant must be in 16 bits, as a signed integer in 2’s complement format
    addi $s1, $s2, 100 # $s1 = $s2 + 100

## Slide 3: Logical Operations
Often we need to operate on bit fields within a word.
  Which allow us to pack and unpack bits into words and perform logical operations such as logical and, logical or, and logical negation

## Slide 4: Logical operations
And:
  0 and 0 = 0, 0 and 1 = 0, 1 and 0 = 0, 1 and 1 = 1
Or:
  0 or 0 = 0, 0 or 1 = 1, 1 or 0 = 1, 1 or 1 = 1
Xor:
  0 xor 0 = 0, 0 xor 1 = 1, 1 xor 0 = 1, 1 xor 1 = 0

## Slide 5: Bit-wise AND
Apply AND bit by bit
  The resulting bit is 1 if both of the input bits are 1 and zero otherwise
    and $t2, $t0, $t1
  There is also a version of AND with an immediate
    andi $t2, $t1, 12
    The immediate is treated as an unsigned 16-bit number

## Slide 6: Bit-wise OR
Apply OR bit by bit
  The resulting bit is 1 if at least one of the input bits is 1 and zero otherwise
    or $t2, $t0, $t1
  There is also a version of OR with an immediate
    ori $t2, $t1, 12
    The immediate is treated as an unsigned 16-bit number

## Slide 7: Bit-wise XOR
Apply XOR bit by bit
  The resulting bit is 1 if two bits are different
    xor $t2, $t0, $t1
  There is also a version of OR with an immediate
    xori $t2, $t1, 12
    The immediate is treated as an unsigned 16-bit number

## Slide 8: NOR
Since NOT takes one operand and results in one operand, it is not included in MIPS as an instruction
  Because in MIPS each arithmetic operation takes exactly three operands
  Instead, NOR is included
    The resulting bit is 0 if at least one of the input bits is 1
    nor $t2, $t0, $t1
  How to implement NOT using NOR?
    Using $zero as one of the input operands
    It is included in MIPS as a pseudoinstruction

## Slide 9: Questions
With these instructions, how can we load an integer value (like 100) into a register ($t0)?
Notes:   addi $t0, $zero, 100
  ori $t0, $zero, 80

## Slide 10: Questions
How to tell if $t0 is equal to $t1? Suppose you need to set $s0 to be 0 if they are equal and any non-zero value otherwise
Notes: Xor, sub, both will work

## Slide 11: Questions
How to tell if $t0 is an odd number? Suppose you need to set $t1 to be 1 if so and 0 otherwise
Notes: andi $t1, $t0, 1

## Slide 12: Shifts
Shift instructions move all the bits in a word to the left or to the right
  Shift left logical (sll) move all the bits to the left by the specified number of bits
    sll $t2, $t0, 2
  Shift right logical (srl) move all the bits to the right
    srl $t2, $t0, 2
  Filling the emptied bits with 0’s

## Slide 13: Example
Suppose register $s0 ($16) is 9ten
  What do we have in $t2 ($10) after
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1

## Slide 14: Example
Suppose register $s0 ($16) is 9ten
  We have in $t2 ($10) after
    The value is 144ten = 9ten  24
  In general, shifting left by i bits gives the same result as multiplying by 2i
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0

## Slide 15: Example
Suppose register $s0 ($16) is 9ten
  We have in $t2 ($10) after
    The value is NOT 9ten  228 noting that the number is a signed number.
    Overflow happens this time
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 16: Questions
Suppose $t0 is storing 30, $t1 is storing 20. After the following instructions, what will be the value in $t2?
  sub $t2, $t0, $t1
  srl $t2, $t2, 2
  ori $t2, $t2, 10
  (a) 8
  (b)10
  (c)18
  (d) None of the above.
Notes: 30-20=10=1010. srl =10, or with 10 becomes 10. So. (b)

## Slide 17: Questions
Suppose word array A stores 0,1,2,3,4,5,6,7,8,9, in this order. Assume the starting address of A is in $s0. After the following instructions, what will be the value in $t0?
addi $s0, $s0, 32
lw $t0, 4($s0)
andi $t0, $t0, 1
  (a) 0
  (b) 8
  (c) 9
  (d) None of the above.
Notes: (d) 1

## Slide 18: Questions
Assume A is an integer array with 10 elements storing 0,1,2,3,4,5,6,7,8,9. Assume the starting address of A is in $s0 and $t0 is holding 3. After the running the following code, what will be the content of $t0?
sll $t0, $t0, 3
add $t0, $s0, $t0
lw $t0, 0($t0)
srl $t0, $t0, 1
  (a) 3
  (b) 1
  (c) 0
  (d) None of the above.
Notes: Answer: a.