## Slide 1: Distributed Operating Systems
Andy Wang
COP 5611
Advanced Operating Systems

## Slide 2: Outline
Introductory material
Distributed IPC
Distributed file systems
Security for distributed systems

## Slide 3: Outline of Introductory Materials
Why distributed OSes?
Important issues in distributed OSes
Important distributed OS tools and mechanisms

## Slide 4: Why Bother?
Economics of hardware
Resource sharing
Effective use of networks
Reliability

## Slide 5: Economics of Hardware
Cheaper to build many small machines than one large one
Due to
  Economics of scale
  Chip design and fabrication issues
    E.g., clock, power, heat
Gives purchasers easy options to increase computer power

## Slide 6: Resource Sharing
Users need to share resources
Hardware resources
  CPU, memory, storage, printers
Software resources
  Data
  Access to software services

## Slide 7: Network Usage
Users often want to communicate
  With other local users
  And to make data available to world
System needs to support user interactions
Generally demands cooperation among machines

## Slide 8: Reliability
Failure of a single machine no longer halts everyone
Graceful degradation of the overall system’s resources
Can apply fault tolerance for tasks at a high architectural level

## Slide 9: Problems with Distributed Systems
More complex
Harder to achieve correctness
Harder to allocate resources properly
Security
Dealing with partial failures
Scaling issues
Heterogeneity

## Slide 10: Complexity of the Model
Problem for
  Designers
  Users
  System software
Harder to understand what will happen at any given case
  Network oscillations, cycles
Harder to design software to handle even understood complexities

## Slide 11: Difficulties with Correct Operation
Distribution requires more complex synchronization
  Hard to synchronize at fine time scale
  Example, distributed make
Differences between similar operations with remote and local (pointer passing)
New sources of nonuniform timings

## Slide 12: Difficulties of Allocating Resources
Local machine may have inadequate resources for a task
  While a remote machine lies idle
Infeasible to control resources centrally
  Do I need to go remote to satisfy malloc()?
Using remote resources conflicts with local autonomy

## Slide 13: Security
Much trickier with no centralized control
Data communications more subject to eavedropping
Physical security measures typically infeasible for many problems
In very widely distributed systems, very tricky problems

## Slide 14: Dealing with Partial Failures
Single machines usually have easy failure modes
Distributed systems face complications
Even detecting failure of a remote machine is nontrivial
  A slow network vs. a failed network vs. a crashed machine

## Slide 15: Scaling Issues
Distributed systems control much larger pools of resources
So, algorithms that scale well become much more important
Scaling puts severe limits on close cooperation

## Slide 16: Heterogeneity Problems
Most distributed systems must address problems of differing HW and SW
  Same disk model has different number of tracks
Different data and executable formats
Different software versions
Different OSes

## Slide 17: Resource Sharing
Resource sharing helps somewhat
Motivations for resource sharing
  Information exchange
  Load distribution
  Computational parallelism
The fundamental distributed system problem
The tragedy of the commons
  Roommates…

## Slide 18: Distribution Complicates Everything
Process control and synchronization
Interprocess communications
File systems
Security
Device management

## Slide 19: Important Research Areas in Distributed Operating Systems
In the area of processes
  Remote interprocess communications
  Synchronization
  Naming
  Distributed process management

## Slide 20: More Research Areas
In the area of resource management
  Resource allocation
  Distributed deadlock mechanisms
  Protection and security
  Managing communication resources
  Performance isolation

## Slide 21: Taxonomy of Distributed Systems
Data Stream
Instruction
Stream
Single
Multiple
Single
Multiple
SISD
(von Neumann
architecture)
SIMD
(vector
processors)
MISD
(pipeline)
MIMD
(distributed
shared memory)

## Slide 22: Network vs. Distributed OSes
Network OSes control a single machine, plus some remote access facilities
Distributed OSes control a collection of machines
Not a hard and fast distinction

## Slide 23: Network OS Diagram
Network OS
Network OS
Network OS
Network OS
Network OS

## Slide 24: Distributed OS Diagram
Network OS
Network OS
Network OS
Network OS
Network OS
Distributed Operating system

## Slide 25: Characteristics of Network OSes
Private per-machine OS
Normal operations only on local machine
Machine boundaries are explicit
Little per-user fault tolerance

## Slide 26: Characteristics of Distributed OSes
Single system controls multiple machines
Use of remote machines invisible
Users treat system as virtual uniprocessor
Strong fault tolerance

## Slide 27: Reality is Somewhere in Between
Relatively few true distributed OSes
Network OS model…
But many modern systems have distributed OS-like capabilities
  Like remote file access
And they also support network OS operations
  Like remote shell
WWW access is in between

## Slide 28: The Role of the Network
Distributed OSes made possible by network
Two fundamental types
  Local area networks
  Long haul networks
With very different characteristics

## Slide 29: Local Area Networks
High bandwidth
Low delay
Shared by modest number of machines
Covers modest geographical area
Dedicated to small group of users
Can be regarded as extension to computer’s backplane

## Slide 30: Long Haul Networks
Lower bandwidth
Longer delays
Shared by large numbers of machines
Covers very wide area
Typically shared by many independent groups
  Problematic for cloud computing

## Slide 31: Communication Protocols
Well defined methods of intermachine data exchange
To handle problems of connecting network automatically
Many different types required/available

## Slide 32: Using Protocols in Distributed OSes
Any intermachine operation requires a protocol to control it
So, all machines involved can understand data exchange
Fundamental choice
  General vs. special purpose protocols

## Slide 33: General- vs. Special-purpose Protocols
General protocols try to handle any kind of traffic
Special-purpose protocols are customized for one situation
General protocols simplify everything
Special-purpose protocols may perform better

## Slide 34: Important Issues in Distributed Operating Systems
Communication model
Process interaction
Transparency
Heterogeneity
Resource allocation
Autonomy
Consistency and transactions

## Slide 35: Communication Models for Distributed OSes
How do machines communicate?
  Generally, message-based, at some level
ISO model adds too much overhead
  So, special-purpose protocols or simplified protocol stacking model is typically used

## Slide 36: Process Interaction in Distributed OSes
How do processes interact in a distributed system?
  Pipe model
  Uninterpreted message model
  Client/server model
  Peer-to-peer model
  Integrated model
  RPC model
  Shared memory model

## Slide 37: Pipe Model
Processes interact through pipes
  Named (has an associated file name) or unnamed
  Local or remote

## Slide 38: Pros/Cons of Pipe Model
+ Simple transfer of large blocks of data
+ Hides many aspects of distribution
- Offers little organizational benefits
- Short on flexibility
- May be hard to get good performance

## Slide 39: Uninterpreted Message Model
Processes send explicit messages
System provides general message delivery service
Higher-level semantics (blocking/nonblocking) handled by processes
Libraries can provide useful message services
Example: Isis

## Slide 40: Pros/Cons of Uninterpreted Message Model
+ Simple and powerful
+ Relatively easy to implement
+ Can scale well
- Offers little organizational support
- Encourages asynchrony
- Not everyone’s favorite programming paradigm

## Slide 41: Client/Server Process Interaction Model
Processes are either clients or servers
Clients send request messages to servers
Servers send response messages to clients
Clients compete for server resources
Control of system distributed among servers
Examples: Name servers, IPC servers, file servers, WWW servers, etc.

## Slide 42: Pros/Cons of Client/Server Model
+ Simple model
+ Hides much distribution
- Servers are bottlenecks
- Multiple implementations of servers to overcome bottlenecks increase complexity

## Slide 43: Peer-to-Peer Model
A process serves as a client and a server
Control of the total system is distributed among peers

## Slide 44: Pros/Cons of Peer-to-Peer Model
+ No centralized bottleneck
+ Can scale well
Difficult to control the global behavior
  Censorship-proof

## Slide 45: Integrated Process Interaction Model
All system resources implemented in integrated way
Remote/local resources treated identically
System makes decisions on resource allocation
E.g., Locus

## Slide 46: Pros/Cons of Integrated Process Interaction Model
+ Hides distributed complexity
+ Reduces bottlenecks
Hard to implement correctly
  How do you migrate a process?
- Performance problems likely
- Big scaling problems

## Slide 47: RPC Model
Processes communicate through RPC
  Client/server often built on top of this
  But this model makes lower level more explicit

## Slide 48: Pros/Cons of RPC Model
+ Simple programming model
+ Good scaling potential
+ Potentially good performance
- Potential for deadlock and blocking
- Potential bottleneck problems

## Slide 49: Shared Memory Model
Provide distributed shared memory as the basic IPC mechanism
Emulating local shared memory
Possibly without substantial HW support

## Slide 50: Pros/Cons of Shared Memory Model
+ Simple user model
+ Easy to build other mechanisms on top
- Hard to provide complete transparency
- Hard to provide good performance
- Serious scaling, heterogeneity questions

## Slide 51: Transparency
Invisible (like a pane of glass)
Hiding machine boundaries
  From both users and system itself
Transparent systems much easier to work with
Providing at a low level has strong benefits
Not everything should be transparent

## Slide 52: Kinds of Transparency
Data transparency
Process-access transparency
Location transparency
Name transparency
Control transparency
Execution transparency
Performance transparency

## Slide 53: Data Transparency
Allow transparent access to remote data
Benefit: allows use of remote data resources
NFS is (largely) data transparent

## Slide 54: Process Access Transparency
Local resources accessed with same mechanisms as remote resources
Benefit: user doesn’t need to worry what’s local and what’s not
NFS, RPC are process access transparent
WWW is not process access transparent

## Slide 55: Location Transparency
Where resources are located is invisible
Benefit: resources can be moved without disruption
RPC can be location transparent
WWW is not location transparent

## Slide 56: Name Transparency
A given name has the same meaning throughout the distributed system
Benefit: same name gets to same resource from anywhere
URLs are name transparent
/tmp in most distributed FSes is not

## Slide 57: Control Transparency
Control of system resources is transparent to its users (e.g., remote processes controlled like local)
Benefit: easier control of distributed applications
Locus provides control transparency on processes
Typical UNIX network of workstation does not provide it on processes

## Slide 58: Execution Transparency
Allows processes to execute on any machine in system (and more, perhaps)
Benefit: easier handling of distributed applications, load balancing
Java is execution transparent (not load balancing, though)
NFS provides no execution transparency

## Slide 59: Performance Transparency
Users don’t notice difference when something must be done remotely
Benefit: if achievable, frees user of worrying about costs of going remote
NFS has high degree of performance transparency
WWW often does not

## Slide 60: Benefits of Transparency
Easier software development
Support for incremental changes
Potentially better reliability
Simpler user model
Flexibility in resource location
Support for scaling

## Slide 61: When can you provide transparency?
In applications (especially databases)
In programming languages
In OS itself

## Slide 62: When don’t you want transparency?
When it’s too complex to provide
  E.g., heterogeneous systems
When you want particular resources
  E.g., /tmp
When remote performance is terrible
  E.g., over very slow links
Must be able to bypass transparency

## Slide 63: Heterogeneity
How transparent should heterogeneous networks be?
And at what cost?
Generally, how does the network deal with heterogeneity?

## Slide 64: Types of Heterogeneity
Computer heterogeneity
Network heterogeneity
OS heterogeneity

## Slide 65: Computer Heterogeneity
Handling different types of computers
Most IPC mechanism easier if machines are homogeneous
  Easier sharing of certain kinds of data
Technology trends towards homogeneity
  But that can change

## Slide 66: Network Heterogeneity
Handling different types of networks
  Wired vs. wireless
Dominance of IP making network interoperability a reality
But problems remain with differing network performances

## Slide 67: OS Heterogeneity
Different OSes are not generally prepared to work together
Prevents easy load sharing, migration of tasks

## Slide 68: Solutions to Heterogeneity problems
Enforced coherence
  Happening at de facto level
High-level standards
  E.g., external data representations
Bridges
Virtualization
…

## Slide 69: Resource Allocation
Min-max allocation
  Example network bandwidth allocation of 10MBps
  Users 1, 2, 3, 4 need {2, 2.6, 4, 5 Mbps)
  Step 1: allocate for the smallest demand
    User 1 gets 2 Mbps
    Remaining = 10 – 2 = 8 Mbps
Step 2: three users share 8 Mbps, or 2.67 Mbps each
  2.6 is less than 2.67
  User 2 gets 2.6 Mbps
  Remaining = 8 – 2.6 = 5.4 Mbps
Step 3: two users share 5.4 Mbps

## Slide 70: Resource Allocation
Min-max allocation
  Step 3: two users share 5.4 Mbps
  Each gets 2.7 Mbps
Final allocation
  User 1: 2 Mbps
  User 2: 2.6 Mbps
  User 3: 2.7 Mbps
  User 4: 2.7 Mbps
+ general
+ performance isolation
+ each user gets all of its requests or above 1/n fair share
- Single resource type

## Slide 71: How about multiple resources?
User A tasks (1 CPU, 4 GB RAM)
User B tasks (3 CPUs, 1 GB RAM)
How do we allocate fairly?

## Slide 72: Solution Properties
Sharing incentive: should not allocate more tasks using > 1/n of resources
Strategy-proofness: can’t lie to gain resources
Envy-freeness: fairness
Pareto efficiency: can’t increase one’s alloc w/o decreasing another one’s alloc

## Slide 73: Strategy Proofness
Scheduler manipulations
  If map slots are contended, do all jobs in the reduce phase…
  A datacenter provides dedicated machine if a user has a high utilization
    Users would add small useless loops to inflate utilization levels

## Slide 74: Other Desirable Properties of Resource Allocation
Single resource fairness: for one resource, the solution same as max-min
Bottleneck fairness: the most demanded resource solution same as max-min

## Slide 75: Other Desirable Properties of Resource Allocation
Population monotonicity: when a user leaves the system, none of the allocs of the remaining users should decrease
Resource monotonicity: when resources are added, non of the allocs of existing users should decrease

## Slide 76: Dominant Resource Fairness (DRF)
Dominant resource for a CPU-bound job is CPU
Dominant resource for a I/O-bound job is bandwidth

## Slide 77: DRF Example
System with 9 CPUs, 18 GB RAM
A tasks (1 CPU, 4 GB)
  1/9 of CPUs, 2/9 of RAM
  RAM is dominant resource with 2/9 of RAM
B tasks (3 CPUs, 1 GB)
  1/3 of CPUs, 1/18 of RAM
  CPU is dominant resource with 1/3 of CPUs

## Slide 78: DRF Example Solution
Three tasks for A
  3 CPUs
  12 GB (2/3 RAM)
Two tasks for B
  6 CPUs (2/3 CPUs)
  2 GB

## Slide 79: How to Solve…
A tasks uses
  x CPU, 4x GB
B tasks uses
  3y CPU, y GB
Total CPU
  x + 3y < 9
Total RAM
  4x + y < 18
Equalize the dominant shares of resources
  4x/18 = 3y/9
x = 3, y = 2

## Slide 80: Incremental Algorithm
Add tasks with least dominant share until the dominant shares equalize
Randomly picked first

## Slide 81: Alternatives of DRF
Asset Fairness
  All resources are worth the same
    1% of CPUs = 1% of RAM
  Max-min on sum of all resources
- A user may get < 1/n for each of all resources

## Slide 82: Alternatives of DRF
Competitive Equilibrium from Equal Incomes (CEEI)
  Each user gets 1/n of each resource
  Trade with other users
  Maximize (x times y)
+ Envyfree and Pareto efficient
- Not strategy-proof
- Violates population monotonicity

## Slide 83: Quick Summary