## Slide 1
Networks
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Networking
Transport Protocols
  UDP
  TCP
Sockets – Programming Review
Sockets – TCP/IP Implementation

## Slide 3: Communication Is Important
Various computer environments
  Embedded devices (sensors)
  Hand-held devices
  Desktop computers and Servers
  Large-scale data centers and supercomputers
Performance, power, and reliability
  Main energy consumer in embedded and mobile devices
  Main latency bottlenecks in wide-area networks
    Propagation delay: 2*108 meters/sec; 5 ns per meter.
Latency matters in servers and data centers
  Processor: 1 IOPS  1 ns per instruction
  Memory: 10 GB/sec  1 ns per 10B

## Slide 4: Conventional Communication Stack
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment (20 bytes – 64K)
IP packet
IP packet
IP packet
(20 bytes – 64K)
(Synchronous Optical Network )
(packet size: 64B - 1518B)

## Slide 5: Transport Protocols
Provide logical communication between application processes running on different hosts
Run on end hosts
  Sender: breaks application messages into segments, and passes to network layer
  Receiver: reassembles segments into messages, passes to application layer
Multiple transport protocol available to applications
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 6: Roles of Transport Layer
Application layer
  Communication for specific applications
  E.g., HTTP and FTP
Transport layer
  Communication between processes (e.g., socket)
  Relies on network layer and serves the application layer
  E.g., TCP and UDP
Network layer
  Logical communication between nodes
  Hides details of the link technology
  E.g., IP

## Slide 7: Internet Transport Protocols
Datagram messaging service (UDP)
Reliable, in-order delivery (TCP)
  Connection set-up
  Discarding of corrupted packets
  Retransmission of lost packets
  Flow control
  Congestion control
Other services not available
  Delay guarantees
  Bandwidth guarantees

## Slide 8: Simple Demultiplexer (UDP)
Extends host-to-host delivery service of the underlying network into a process-to-process communication service (via ports)
Adds a level of demultiplexing which allows multiple application processes on each host to share the network

## Slide 9: UDP multiplexing of applications
UDP Message Queue

## Slide 10: Transmission Control Protocol (TCP)
Connection oriented
  Explicit set-up and tear-down of TCP session
Stream-of-bytes service
  Sends and receives a stream of bytes, not messages
Reliable, in-order delivery
  Checksums to detect corrupted data
  Acknowledgments & retransmissions for reliable delivery
  Sequence numbers to detect losses and reorder data
Flow control
  Prevent overflow of the receiver’s buffer space
Congestion control
  Adapt to network congestion for the greater good

## Slide 11: TCP Byte stream definition
TCP is a byte-oriented protocol, which means that the sender writes bytes into a TCP connection and the receiver reads bytes out of the TCP connection.
Although “byte stream” describes the service TCP offers to application processes, TCP does not, itself, transmit individual bytes over the Internet.

## Slide 12: TCP: Byte Streaming
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
Byte 80

## Slide 13: TCP Segment
TCP on the source host buffers enough bytes from the sending process to fill a reasonably sized packet and then sends this packet to its peer on the destination host.
TCP on the destination host then empties the contents of the packet into a receive buffer, and the receiving process reads from this buffer at its leisure.
The packets exchanged between TCP peers are called segments.

## Slide 14: Emulated Using TCP “Segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment = max segment size (MSS),
Not full, but times out, or
“Pushed” by application.

## Slide 15: Sliding Window
Allow a larger amount of data “in flight”
  Allow sender to get ahead of the receiver
  … though not too far ahead
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received

## Slide 16: Receiver Buffering
Window size
  Amount that can be sent without acknowledgment
  Receiver needs to be able to store this amount of data
Receiver advertises the window to the sender
  Tells the sender the amount of free space left
  … and the sender agrees not to exceed this amount
Window Size
Outstanding
Un-ack’d data
Data OK
to send
Data not OK
to send yet
Data ACK’d

## Slide 17: Three-way Handshake to Establish Connection
Three-way handshake to establish connection
  Host A sends a SYN (open) to the host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
SYN
SYN ACK
ACK
Data
A
B
Data
Each host tells its initial sequence number (ISN) to the other host.

## Slide 18: Tearing Down the Connection
Closing the connection
  Finish (FIN) to close and receive remaining bytes
  And other host sends a FIN ACK to acknowledge
  Reset (RST) to close and not receive remaining bytes
SYN
SYN ACK
ACK
Data
FIN
FIN ACK
ACK
time
A
B
FIN
ACK

## Slide 19: Outline
Transport Protocols
  UDP
  TCP
Sockets – Programming Review
Sockets – TCP/IP Implementation

## Slide 20: Socket: End Point of Communication
Sending message from one process to another
  Message must traverse the underlying network
Process sends and receives through a “socket”
  In essence, the doorway leading in/out of the house
Socket as an Application Programming Interface
  Supports the creation of network applications
socket
socket
User process
User process
Operating
System
Operating
System

## Slide 21: Identifying the Receiving Process
Sending process must identify the receiver
  Name or address of the receiving end host
  Identifier that specifies the receiving process
Receiving process
  Host with a 32-bit IP address that uniquely identifies the host
  And a 16-bit port that uniquely identifies the socket/service
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client

## Slide 22
socket()
bind()
close()
data
data
Server
Client
accept()
read()
Blocks until server receives a connect request
TCP Socket
listen()
write()
socket()
close()
read()
connect()
write()
3-way handshaking

## Slide 23: Example – TCP Client and Server
Initialization:
  socket – create socket
  bind – bind to an address
Connection Establishment
  listen – listen to new connection request
  accept – accept request and create a new socket
  connect – request for new connection
Transmission:
  write – send message to server
  read – receive message from server
Termination:
  close - close socket

## Slide 24
socket()
bind()
close()
sendto()
data
data
Server
Client
recvfrom()
sendto()
recvfrom()
close()
socket()
optional bind()
Blocks until server receives data from client
UDP socket

## Slide 25: UDP Client and Server
Initialization:
  socket – create socket
  bind – bind to an address. Optional for the client
  Must use SOCK_DGRAM for the protocol
  No connection establishment. Less overhead
Transmission:
  sendto – send message
  recvfrom – receive message from socket
  Must be done at the boundaries of datagrams
Termination:
  close - close socket

## Slide 26: Software Architecture of Sockets
TCP
ARP
UDP
Application
BSD Socket
INET Socket
IP (caches some MAC addr)s
Networks (Ethernet, WIFI, etc)
Address resolution protocol: maps IP address to MAC addresses
Notes: 26

## Slide 27: Socket buffer: struct sk_buff
Double Link List of sk_buff
Pointers to the data buffer

## Slide 28: sk_buff cont’d

## Slide 29: Sending Data via Sockets
Courtesy of Glenn Herrin, Univ. of New Hampshire

## Slide 30: Receiving Data
Courtesy of Glenn Herrin, Univ. of New Hampshire

## Slide 31: Example Data Flow from A to B
socket()
bind()
User space
A
B
accept()
write()
listen()
socket()
connect()
3-way handshaking
Kernel space
sys_write()
socket_write()
socket_sendmesg()

## Slide 32: Socket  INET  TCP
A
socket_sendmesg()
inet_sendmesg()
tcp_v4_sendmesg()
tcp_do_sendmesg()
allocate sk_buff and data storage skb_put(): copy data from user space skb_push(): add header
tcp_send_skb()
tcp_transmit_skb()
Complete TCP header and checksum it
Ready to send sk_buff’s

## Slide 33: TCP IP Device  Media
A
tcp_transmit_skb()
ip_queue_xmit()
Find destination Possible fragmentation Add IP header Checksum the header
skb->output()
dev_queue_xmit()
dev->hard_start_xmit()
q->enqueue()

## Slide 34: Media Device
B
net_bh()
do_bottom_half()
skb_queue_tail()
netif_rx()
ei_interrupt()
ei_receive()

## Slide 35: Device IP
B
Find header
Extract Protocol
ip_local_deliver()
ip_recv()
net_bh()
skb_clone()
Possible reassembly

## Slide 36: IP TCP
B
Validate TCP header Send ACK
skb_queu_tail()
tcp_v4_do_rcv()
ip_recv()
tcp_v4_rcv()
tcp_data_queue()
data_ready()
Recv’d packet queue

## Slide 37: TCP Application
Recv’d packet queue
Sock_read()
B
socket()
connect()
read()
sys_read()
Inet_rcvmesg()
tcp_rcvmesg()

## Slide 38: Data Flow Summary
At least four data copies
  Application to TCP sk_buff’s
  Sk_buff’s to network media
  Media to TCP sk_buff’s
  TCP to Application
Cost per byte: checksum and data copying
Cost per packet:
  Interrupt processing
  sk_buff management
  header filling in and extraction

## Slide 39: Sockets Performance Metrics
Latency
  Time for an end-to-end message from source to destination
  Typically measure with a ping-pong or request/reply pair of same-size messages
Breakdown of Latency
  Sender and Receiver overheads
  Queue delay
  Propagation delay

## Slide 40: Bandwidth and CPU Utilization
Bandwidth (throughput)
  The amount of data transferred in a unit of time
  Dependent on data size, block size of transfer, etc
CPU Utilization
  CPU time spent in processing network protocols
  Include per-packet cost and per-byte cost

## Slide 41: CPU Utilization
Measures the amount of CPU time spent in networking
CPU may also be referred as overhead
  As it is needed because of network protocols
High for small message transfers
Low for large messages
Much is also due to interrupt handling

## Slide 42: Benchmark: netperf
Available:
  ftp://ftp.netperf.org//netperf/
Compilation
  ./configure && make
Programs:
  ./netserver
  ./netperf -H hostname [options]
Tests:
  TCP_RR, TCP_STREAM, TCP_MAERTS
  UDP_RR, UDP_STREAM
  Also can measure CPU utilization

## Slide 43: Benchmark: iperf
Available:
  http://sourceforge.net/projects/iperf/
Compilation
  ./configure && make
Programs:
  ./iperf [-s|-c host] [options]
Tests:
  TCP
  UDP with an option: –u
  Multiple parallel flows: -P#

## Slide 44: Performance Tunables
Socket Buffer Size
  net.ipv4.tcp_rmem (/proc/sys/net/ipv4/tcp_rmem)
  (min, default, max)
  tcp_wmem:
  tcp_mem (threshold for memory pressure)
Send and Receive Segment Offload
Interrupt coalescing
Others
  TCP_NODELAY
  TCP SACK

## Slide 45
Topic 3
TCP/IP Congestion Avoidance
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 46: TCP Congestion Control
A host sends packets without a reservation
  The host reacts to observable events.
Each source determines how much capacity is available to a given flow in the network.
ACKs are used to ‘pace’ the transmission of packets such that TCP is “self-clocking”.

## Slide 47: AIMD (Additive Increase / Multiplicative Decrease)
CongestionWindow (cwnd) is a variable held by the TCP source for each connection.
cwnd is set based on the perceived level of congestion. The Host receives implicit (packet drop) or explicit (packet mark) indications of internal congestion.
MaxWindow :: min (CongestionWindow , AdvertisedWindow)
EffectiveWindow = MaxWindow – (LastByteSent -LastByteAcked)

## Slide 48: Additive Increase
Additive Increase is a reaction to perceived available capacity.
For each “cwnd’s worth” of packets sent, increase cwnd by 1 packet.
In practice, cwnd is incremented fractionally for each arriving ACK.
increment = MSS x (MSS /cwnd)
cwnd = cwnd + increment
Source
Destination

## Slide 49: Multiplicative Decrease
The key assumption is that a dropped packet and the resultant timeout are due to congestion at a router or a switch.
TCP reacts to a timeout by halving cwnd.
Although cwnd is defined in bytes, the literature often discusses congestion control in terms of packets.
  Formally, MSS == Maximum Segment Size
cwnd is not allowed below the size of a single packet.

## Slide 50: AIMD Drawbacks
Linear additive increase takes too long to ramp up a new TCP connection from cold start.
TCP Tahoe Slow start provides an initial exponential increase in the size of cwnd.

## Slide 51: TCP Tahoe
Slow Start – Increases the window size exponentially (e.g., for every ack, sends two packets)
Congestion Avoidance - Reducing sender’s window size by half at experience of loss, and increase the sender’s window at the rate of about one packet per RTT (NOTE: not per ack)
Fast Retransmit - Don’t wait for retransmit timer to go off, retransmit packet if 3 duplicate acks received

## Slide 52: Tahoe Slow Start
The source starts with cwnd = 1.
Every time an ACK arrives, cwnd is incremented.
  cwnd is effectively doubled per RTT (round-trip time).
Two slow start situations:
  At the very beginning of a connection
  When the connection goes dead waiting for a timeout to occur (i.e., the advertized window goes to zero!)
It has to be guarded by a threshold
  ssthresh
Source
Destination

## Slide 53
assume ssthresh = 8*MSS
Example: Slow Start/Congestion Avoidance
cwnd = 10
cwnd = 4
Eight ACKs
cwnd = 2
cwnd= 8
cwnd = 1
cwnd = 9
Eight packets
Nine ACKs
Nine packets
Ten ACKs
Ten packets
cwnd = 11
ssthresh
S
R

## Slide 54: Protocol of Slow Start & Congestion Avoidance
ssthresh
Initially:
- cwnd = 1*MSS
- ssthresh = very high
If a new ACK comes:
  - if cwnd < ssthresh  update cwnd according to slow start
  if cwnd > ssthresh  update cwnd according to congestion avoidance
  If cwnd = ssthresh  either
If timeout (i.e. loss) :
  - ssthresh = flight size/2;
  - cwnd = 1*MSS
time
cwnd
Loss, e.g. timeout
slow start – in green
congestion avoidance – in blue
(initial) ssthresh

## Slide 55: Fast Retransmit
Coarse timeouts remained a problem, and Fast retransmit was added with TCP Tahoe.
Since the receiver responds every time a packet arrives, this implies the sender will see duplicate ACKs.
Use duplicated ACKs to signal lost packet
  Three duplicated Acks

## Slide 56: TCP Tahoe’s Fast Retransmit
Sender receives 3 dupACKS.
  Sender infers that the segment is lost.
Sender re-sends the segment immediately!
Sender returns to slow-start.
ACK 1
segment 1
cwnd = 1
cwnd = 2
segment 2
segment 3
ACK 3
cwnd = 4
segment 4
segment 5
segment 6
segment 7
ACK 2
3 duplicate
ACKs
ACK 3
ACK 3
ACK 3
segment 4
fast-retransmit
of segment 4
S
R
Notes:   Recall: a duplicate ACK means that an out-of sequence segment was received
Notes:
  duplicate ACKs due packet reordering!
  if window is small don’t get duplicate ACKs!

## Slide 57: Fast Retransmit Benefits
Generally, fast retransmit eliminates about half the coarse-grain timeouts.
This yields roughly a 20% improvement in throughput.
Note – fast retransmit does not eliminate all the timeouts due to small window sizes at the source.

## Slide 58
Congestion
window
10
5
15
20
0
Round-trip times
Slow
start
Congestion
avoidance
Congestion occurs
Threshold
Figure 7.63
Possible Improvement to Tahoe?
Can it recover sooner?

## Slide 59: Fast Recovery Concept
Added with TCP Reno.
When fast retransmit detects three duplicate ACKs:
  Stop Fast Retransmit,
  Half cwnd and commence recovery from this point using linear additive increase ‘primed’ by left over ACKs in pipe.
Recovery starts congestion avoidance region
  ACKs in the pipe used to pace the sending of packets.
  Avoid slow start by inflating cwnd.
With fast recovery, slow start only occurs:
  At cold start
  After a coarse-grain timeout

## Slide 60: Diagram of Fast Recovery
cwnd
Slow Start
Congestion Avoidance
Time
“inflating” cwnd with dupACKs
“deflating” cwnd with a new ACK
(initial) ssthresh
new ACK
fast-retransmit
fast-retransmit
new ACK
timeout

## Slide 61: Protocol Changes for Fast Recovery
Send-side only
After receiving 3 dupACKS:
  Retransmit the lost segment.
  Set ssthresh = flight size/2
  Set cwnd = ssthresh, and ndupacks = 3
  In Reno: send_win = min (receiving window rwnd, cwnd + ndupacks)
If dupACK arrives:
  ++ ndupacks
  Transmit new segment, if allowed.
If new ACK arrives:
  ndupacks = 0
  Exit fast recovery
If retransmission timeout (RTO) expires:
  ndupacks = 0

## Slide 62: Can we do better?
TCP Reno:
  One RTT required before sending new segments
  Exit fast recovery with any new ack (higher than dupAck)
Partial Ack:
  An ACK that acknowledges some but not all the segments that were outstanding at the start of fast recovery.
  For dupAcks, increase sender window and send new packets
  Brings TCP Reno out of fast recovery
TCP NewReno
  When partial ACK received, re-transmit the next lost segment immediately and set ndupacks = 0 (deflate send_win).
  Sender remains in fast recovery until all data outstanding when fast recovery was initiated is ACK’ed. Additional dupACK’s increase ndupacks
  Tolerate multiple losses

## Slide 63: Anything more can be done?
Tahoe, Reno and NewReno detect congestion by creating congestion!
  Probing for congestion by slowly increasing their sending rate.
  Upon congestion, they cut sending rate at least in half!
This slow advance and rapid retreat approach results in a saw-toothed sending rate, and highly erratic throughput.
Can TCP detect congestion without causing congestion?

## Slide 64: TCP Vegas
Developed over TCP Reno
Modified Slow-Start (SS)
Modified Congestion Avoidance (CA)
Aggressive Retransmission (use fine grained timer)
  With dupacks
  With partial acks
Aggressive Congestion Window Adaptation
  With recovery
  With multiple loss
  Initial setting

## Slide 65: Vegas: Modified Slow-Start
Vegas Calculates (in every alternate RTT):
  Expected Throughput=WindowSize/BaseRTT
  Actual Throughput=ActualSentAmount/RTT
Static Parameters:
   = 1 pkts/RTT
Expected Throughput

Throughput
Actual Throughput
Actual Throughput
(Switch to CA)
(I Continue SS)

## Slide 66: Protocol of Modified Slow-Start
TCP keeps the congestion window fixed in every other RTT and it measures the throughput
On every next RTT, it does the following:
  Continue SS (Expected-Actual<):
  Exponential Increase.
    cwnd = cwnd + 1 for each ACK, that is,
    cwnd = 2 * cwnd for each RTT
  Switch to CA (Expected-Actual>):
    Set ssthresh=cwnd
    Follow the rules of CA

## Slide 67: Vegas: Modified Congestion Avoidance
Vegas Calculates (Once per RTT):
  Expected Throughput=WindowSize/BaseRTT
  Actual Throughput=ActualSentAmount/RTT
Static Parameters:
   = 1 pkts/RTT
   = 3 pkts/RTT
Expected Throughput


Throughput
Actual Throughput
Actual Throughput
Actual Throughput
(Tx Unchanged)
(Decrease Tx)
(Increase Tx)

## Slide 68: Protocol of Modified CA
TCP transmission rate = cwnd/RTT
TCP takes congestion window updating decision once per RTT
The decision is applied throughput the next RTT for each received ACK as follows:
  Increase Tx Rate (Expected-Actual<):
    cwnd = cwnd + 1/cwnd
  Decrease Tx Rate (Expected-Actual>):
    cwnd = cwnd - 1/cwnd
  Tx Rate Unchanged (<Expected-Actual<):
    cwnd = cwnd

## Slide 69: Vegas - Aggressive Retransmission
With dupacks
  When Vegas receives the first dupack or the second dupacks, it checks the fine grained timer
  If timer expires, it retransmits immediately
With partial acks
  For the first two partial acks, Vegas checks whether fine grained timer expires
  If timer expires, it retransmits immediately

## Slide 70: Vegas: Aggressive cwnd Updating
With recovery
  Reduce cwnd by ¼ instead of ½ when it enters into recovery
With multiple loss
  In case of multiple segment loss from a single window, it reduces the cwnd only once
With Initial setting
  cwnd is set to 2 instead of 1

## Slide 71: Benefits of Vegas
Less fluctuation
  Less fluctuation in bottleneck queue
  Less fluctuation in send rate
Enhanced Throughput
Better Utilization of bottleneck capacity
Unfair treatment of old connection
Ineffectiveness of congestion avoidance

## Slide 72: TCP with and w/o SACK
Cumulative Acknowledgement
  Out-of-order protocol data units (PDUs) are not ACKed.
  Receiver sends duplicate acknowledgement.
  Sender learns about a single lost packet per RTT.
Selective Acknowledgement (SACK)
  Receiver informs the sender about all the PDUs that have been received successfully.
  Sender retransmits only the PDUs that have not been Acked.
  Implemented using two TCP options.

## Slide 73: SACK –Permitted Option
First option: enabling option (2 bytes) sent in a SYN
Indicates SACK option can be used once connection established
  Receiver may return SACK’s
  Sender can process SACK’s
Source Port Address Destination Port Address
Sequence Number
Checksum Urgent Pointer
Window Size
Cumulative Acknowledgement Number
Kind = 4 Length = 2
Kind = 1 Kind = 1
TCP Header
Header Length
SYN
SACK-Permitted
NOP
NOP
1
6

## Slide 74: SACK – Permitted and SACK
SENDER
RECEIVER
KIND = 4
SYN = 1
KIND = 4
ACK = 1
SYN = 1
ACK = 1
TCP Connection Establishment Phase
Data Transfer Phase
ACK containing Cumulative Ack (CumAck) and Selective Ack (SACK)

## Slide 75: SACK example
SEQ 100, 200 bytes
SEQ 500, 200 bytes
SEQ 300, 200 bytes
ACK 300
SEQ 700, 200 bytes
ACK 300,SACK 500-700
100-300
100-300 500-700
100-300 500--900
ACK 300, SACK 500-900
Receiver
Sender
Receiver’s Buffer
Receiver informs sender of contiguous and isolated blocks of data that have been successfully received and queued.

## Slide 76: SACK Rules
SACK does not change the meaning of ACK field.
First SACK for most recently received out-of-order PDU.
Receiver
  returns as many distinct SACKs as possible.
  SACK option is filled out by repeating most recently reported SACK blocks. Records the SACK for future reference.
Sender
  Maintains a queue containing unacknowledged PDUs.
  Skips SACK PDUs during retransmission.
  Retransmits the PDUs not SACKed so far and less than the highest SACKed PDU.

## Slide 77: SACK Example
SEQ 100, 200 bytes
SEQ 500, 200 bytes
SEQ 300, 200 bytes
ACK 300
SEQ 700, 200 bytes
ACK 300,SACK 500-700
100-300
100-300 500-700
100-300 500-700 900-1100
ACK 300, SACK 900-1100, 500-700
Receiver
Receiver’s Buffer
Sender
SEQ 900, 200 bytes
SEQ 1100, 200 bytes

## Slide 78: SACK Cont’d
Receiver
SEQ 1100, 100 bytes
SEQ 300, 200 bytes
ACK 700, SACK 900-1100
100-300 300-500 500-700 700-900 900-1100
100-300 300-500 500-700 900-1100
SEQ 700, 200 bytes
ACK 1100
Sender
100-300 500-700 900-1100

## Slide 79: Summary of TCP Protocol Variants
TCP Tahoe
  Slow start
  Congestion Avoidance
  Fast Retransmit
TCP Reno
  Fast Recovery
TCP newReno
  Partial Ack
TCP Vegas
  Predict Congestion
  Modified slow start and congestion avoidance
  Aggressive retransmission and congestion window update
TCP SACK