## Slide 1: CUDA programming Performance considerations (CUDA best practices)
NVIDIA CUDA C programming best practices guide
ACK: CUDA teaching center Stanford (Hoberrock and Tarjan).

## Slide 2: Outline
Host to device memory transfer
Memory Coallescing
Variable type performance
Shared memory bank conflicts
Control flow divergence
Occupancy

## Slide 3: Host/device memory transfer
Should always be minimized
  GPU device memory bandwidth 100’s GB/s
  PCIe bandwidth 4-16 GB/s
Start-up overheads: large transfer is more efficient than multiple small transfers
Pinned memory:
  Memory that is always in physical memory
  Can achieve highest bandwidth between host and device
  Use as caution (reduce physical memory size).

## Slide 4: Host/device memory transfer
Asynchronous transfer and Overlapping memory copy with computation

## Slide 5: Host/device memory transfer
Staged concurrent copy and execute

## Slide 6: Memory coalescing
Off-chip memory is accessed in chunks
  Even if you read only a single word, they whole chunk still come in.
Chunks are aligned to multiples of 32/64/128 bytes
Example: threads 0-15 access 4-byte words at addresses 116-176
  Will bring in two chunks 0-127 and 127-255.
  256-64 = 192 bytes are wasted.

## Slide 7: Memory coalescing
Aligned and misaligned device memory accesses

## Slide 8: Memory coalescing
Aligned memory access .vs. unaligned memory access.
  Always try to align the memory and operate on the whole chunk
Sequence access .vs. stride access
      For (i=0; i<n; i++) {… = a[i];} // sequence access
      For (i=0; i<n; i++) { … = a[2*i];} // stride access
  Use sequence access as much as possible.

## Slide 9: Memory coalescing
Array of structure .vs. structure of array
    Struct record { struct record {
    int key; int *key;
    int value; int *value;
    int flag; int *flag;
    }; };
    Record myrecord[100]; record myrecord;
    __global__ void foo (….)
    { int I = blockDim.x * blockIdx.x + threadIdx.x;
    int key = myrecord[i].key; or int key = myrecord.key[i];
    }

## Slide 10: Memory coalescing
Array of structure .vs. structure of array
  Structure of array is often better than array of structures
    Clear win for sequence access.
    Unpredictable for irregular access pattern.

## Slide 11: CUDA variable type performance
Local variables and globals in uncached off-chip memory
Constant variable in cached off-chip memory
Use register, shared, and constant as much as possible.

## Slide 12: Shared memory bank conflicts
Shared memory is banked
  GTX 480 has 32 banks, each bank can read 32 bits in 2 cycles.
    Total shared memory bandwidth: 4 * 32 * 0.5 * 1400M * 15 = 1.33TBs
  Only matters for threads within a warp
  Full performance when
    Threads access different banks
Consecutive words are in different banks
If two or more threads access the same bank but different values, get bank conflicts.

## Slide 13: Examples: no bank conflicts

## Slide 14: Example: bank conflicts

## Slide 15: Thread scheduling and control flow divergence
HW schedules thread blocks onto available SMs
  No guarantee of ordering
  HW will schedule thread blocks as soon as a previous thread block finishes.

## Slide 16: Mapping of thread blocks
Each thread block is mapped to one or more warps
Warps are scheduled independently.

## Slide 17: Thread scheduling
SM supports zero-overhead warp scheduling
  At any time only one warp is executing on one SM
  Warp whose next instruction has its inputs ready are eligible for execution
  Eligible warps are selected with a prioritized scheduling policy
  All threads in a warp execute the same instruction when selected.

## Slide 18: Control flow divergence
What happen if we have an if statement?

## Slide 19: More complicated branches?

## Slide 20: More complicated branches?

## Slide 21: Control flow divergence
Due to SIMT, you don’t need to worry about correctness.
You will need to consider this for performance
  Performance drops off with the degree of divergence.
  Avoid diverging within a warp:
    Branch with divergence:
      If (threadIdx.x > 2) {…}
      Else { … }
    Branch without divergence
      if (threadIdx.x /WARP_SIZE > 2) { …}
      Else {…}
      Branch granularity is a multiple of warp size.

## Slide 22: Compute capability and occupancy
NVIDIA define compute capability that gives resources limitations for its devices
Run devicequery.cu to see the GPU properties.
Resources limit the number of warp/threads that can be executed simultaneously on SMs.

## Slide 23: Occupancy
Warps are stalled all the time (load/store to global memory).
  If all warps are stalled, no instruction is issued.
  Needs a lot of warps to keep SM busy.
  Maximizing the number of warps in an SM is very important (also called maximize occupancy).

## Slide 24: What determines occupancy?
Each SM has limited registers and shared memory
  Register and shared memory usage per thread will determine the occupancy.
  Hard limit of the number of thread blocks in each SM (8).

## Slide 25: Resource limits (1)
Pool of registers and shared memory per SM
  Each thread block grabs some resources
  If one or the other is fully utilized, no more thread blocks.

## Slide 26: Resource limits (2)
Can only have 8 thread blocks per SM
  If thread blocks are too small, they cannot fully utilize the SM
  Need at least 128/256 threads/block
    The number of threads per block should always be a multiple of 32.
  Higher occupany has diminishing return for hiding latency.

## Slide 27: How do you find out the register and shared memory usage
Use ‘nvcc –Xptxas –v a.cu’ to get register and shared memory usage.
You can plug the number to CUDA occupancy calculator to see the occupancy.
To change the register usage: use flag
    -maxrregcount=X
  This can significant affect the program performance as some register is now in memory.