## Slide 1: GPGPU introduction

## Slide 2: Why is GPU in the picture
  Seeking exa-scale computing platform
    Minimize power per operation.
      Power is directly correlated to the area in the processing chips.
      Regular CPU – what are the chip areas going into?
        Power per operation is low
      How to maximize power per operation?
        Give most area to build lots of ALUs, minimize area for control and cache.
        This is how GPU is built  power per operation is much better than regular CPU
          Most power efficient system built using CPU only, IBM Bluegene reaches 2Gflops/Watt
          System built using CPU+GPU can reach close to 4Gflops/Watt.

## Slide 3: Graphics Processing Unit (GPU)
  GPU is the chip in computer video cards, PS3, Xbox, etc
  Designed to realize the 3D graphics pipeline
    Application  Geometry  Rasterizer image
GPU development:
  Fixed graphics hardware
  Programmable vertex/pixel shaders
  GPGPU
    general purpose computation (beyond graphics) using GPU in applications other than 3D graphics
    GPGPU can be treated as a co-processor for compute intensive tasks
      With sufficient large bandwidth between CPU and GPU.

## Slide 4: CPU and GPU
GPU is specialized for compute intensive, highly data parallel computation
  More area is dedicated to processing
  Good for high arithmetic intensity programs with a high ratio between arithmetic operations and memory operations.
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU

## Slide 5: A powerful CPU or many less powerful CPUs?

## Slide 6: Flop rate of CPU and GPU
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2008 | 2010
GPU Single Precision | 25.6 | 76.8 | 165.12 | 518.4 | 933 | 1030
CPU Single Precision | 12 | 24 | 48 | 96 | 96 | 144
GPU Double Precision | 0 | 86 | 515
CPU Double Precision | 6 | 12 | 24 | 48 | 48 | 72
GFlop/Sec
Single Precision
Double Precision

## Slide 7: Compute Unified Device Architecture (CUDA)
Hardware/software architecture for NVIDIA GPU to execute programs with different languages
  Main concept: hardware support for hierarchy of threads

## Slide 8: Fermi architecture
First generation (GTX 465, GTX 480, Telsa C2050, etc) has 512 CUDA cores
  16 stream multiprocessor (SM) of 32 processing units (cores)
  Each core execute one floating point or integer instruction per clock for a thread
Latest Tesla GPU: Tesla K40 have 2880 CUDA cores based on the Kepler architecture. Warp size is still the same, but more everything.
Kepler architecture: 15 SMX

## Slide 9: Fermi Streaming Multiprocessor (SM)
32 CUDA processors with pipelined ALU and FPU
  Execute a group of 32 threads called warp.
  Support IEEE 754-2008 (single and double precision floating points) with fused multiply-add (FMA) instruction).
  Configurable shared memory and L1 cache

## Slide 10: Kepler Streaming Multiprocessor (SMX)
192 CUDA processors with pipelined ALU and FPU
  4 warp scheduler
    Execute a group of 32 threads called warp.
  Support IEEE 754-2008 (single and double precision floating points) with fused multiply-add (FMA) instruction).
  Configurable shared memory and L1 cache
  48K data cache

## Slide 11: SIMT and warp scheduler
SIMT: Single instruction, multi-thread
  Threads in groups (or 16, 32) that are scheduled together call warp.
  All threads in a warp start at the same PC, but free to branch and execute independently.
  A warp executes one common instruction at a time
    To execute different instructions at different threads, the instructions are executed serially
      To get efficiency, we want all instructions in a warp to be the same.
  SIMT is basically SIMD that emulates MIMD (programmers don’t feel they are using SIMD).

## Slide 12: Fermi Warp scheduler
2 per SM: representing a compromise between cost and complexity

## Slide 13: Kepler Warp scheduler
4 per SM with 2 instruction dispatcher units each.

## Slide 14: NVIDIA GPUs (toward general purpose computing)
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM

## Slide 15: Typical CPU-GPU system
Main connection from GPU to
CPU/memory is the PCI-Express (PCIe)
  PCIe1.1 supports up to 8GB/s (common systems support 4GB/s)
  PCIe2.0 supports up to 16GB/s

## Slide 16: Bandwidth in a CPU-GPU system

## Slide 17: GPU as a co-processor
CPU gives compute intensive jobs to GPU
CPU stays busy with the control of execution
Main bottleneck:
  The connection between main memory and GPU memory
    Data must be copied for the GPU to work on and the results must come back from GPU
    PCIe is reasonably fast, but is often still the bottleneck.

## Slide 18: GPGPU constraints
Dealing with programming models for GPU such as CUDA C or OpenCL
Dealing with limited capability and resources
  Code is often platform dependent.
Problem of mapping computation on to a hardware that is designed for graphics.