## Slide 1: SDN and Openflow

## Slide 2: Motivation
Since the invention of the Internet, we find many innovative ways to use the Internet
  Google, Facebook, Cloud computing, etc
  All achieved through software innovations.
Internet infrastructure, however, is virtually unchanged in the past 30-40 years.
  We get higher speed, but not much more. E.g. Ethernet at 100Gbps!!
  We start to see the gap between network applications and network infrastructure.
    Cloud computing data centers cannot be effectively supported using the traditional networking infrastructure
    Legacy software becomes cumbersome to maintain.
  Lots of proposals, but hard to make it into the real networks.

## Slide 3: Motivation
Why Internet (network) application is exploding while the network infrastructure is not?
  Applications are software that allows many people to work on – this facilitates innovation.
  Network infrastructure is basically hardware – only a handful of companies can really work on the network infrastructure – this limits the innovation.
We now see a need to innovate the network infrastructure
  We can continue to do what we used to do – patching up the network and putting off the fires
  A big idea that allows for continuous innovation: open up the network infrastructure and make it behave like software so as to facilitate continuous innovations.
    The is the core idea of Software Defined Network (SDN).

## Slide 4: Basic functions in a traditional router
For a packet at its input port
  Decide what to do this the packet – control plane
    Which output should this packet go to?
    Software system running protocols (OSPF, RIP)
  Move the packet from the input port to the output port – data plane
    This has to be done by hardware, why?
      40Gbps line speed, 1500 bytes packet, need to complete the move every 300 nano-seconds.
Control plane (software)
Data plane (hardware)
A router

## Slide 5: Current network: Closed boxes, fully distributed protocols.

## Slide 6: Some drawbacks
Bundling the forwarding hardware with control plane software
  Effectively makes it a closed system (the whole thing behaves like hardware)
  No way to perform experiments for any innovation on production networks – This kills the innovation.
  Innovative limited to interface – only the networking company can do anything meaningful
  Hardware centric
    Forwarding gets faster and faster using custom ASICs

## Slide 7: Software Defined Networks
Fundamental Characteristics
  Plane separation
  A simplified device
  Centralized control
  Network automation and virtualizztion
  Openness

## Slide 8: Software Defined Network
Keep the data plane hardware, open up the control plane software.
Control plane (software)
Data plane (hardware)
SDN client (Openflow)
Data plane (hardware)
SDN Server

## Slide 9: Openflow-based Software Defined Networks architecture
Note: An application can be as
simple as a simple forwarding switches
Controller provides common functions
like OS, topology, etc. Maintain a global
network view.
Switches are simple devices with
data forwarding capability with knowns
openflow.

## Slide 10: SDN devices
SDN hardware switch
Openflow API
Abstraction layer:
flow tables
HW: L3 Fwd with TCAMs
L2 Fwd with CAMs
SDN software switch
Openflow API
Abstraction layer:
flow tables
Packet processing logic
SDN software switch: Open vSwitch from Nicira and Indigo from Big Switch

## Slide 11: TCAMs and CAMs
TCAMs allows for wildcard (x), needed for Level 3 forwarding
CAMs only allows 0’s and 1’s in the matching, works for Level 2 forwarding
Both are very expensive memory.
Flow tables in SDN are realized with TCAMs

## Slide 12: SDN controller
Northbound API Java API… not well defined
Modules toopolgy Device Topo Flows
discovery manage stats
Southbound API: Openflow
GUI Learning Switch Router Others

## Slide 13: SDN controller core modules
End-user device discovery
Network device discovery
Network device topology management
Flow Management

## Slide 14: Some issues with SDN controllers
Coordination between applications
  E.g. flow prioritization with multiple applications
The lack of a standard northbound API

## Slide 15: SDN applications
An SDN application completes the network functionality
  Example: forwarding switch (all switches behave like the traditional forwarding switch) – the network behavior is now well defined.
  Responsible for managing the flow entries on network devices

## Slide 16: Openflow
An Openflow switch (Ethernet switch) has an internal flow table.
  If a packet matches an entry in the flow table, perform the actions (e.g. forward to port 10) according to the flow table.
  If a packet does not match any entry in the flow table. Send it to the Openflow controller
    The controller will figure out what to do with such packet
    The controller will then respond to the switch, informing how to handle such a packet so that the switch would know how to deal with such packets next time.
    For each flow, ideally the controller will be queried once.
Openflow defines the standard interface to add and remove flow entries in the table.

## Slide 17: Openflow specifications
From 1.0.0 to 1.5.0
Briefly introduce concepts in versions 1.0.0 to 1.2.0

## Slide 18: Openflow
An Openflow switch use s secure channel to connect to a controller
  Authentication in channel set up
  Communicate through the channel
Openflow switch decides
whether to (A) forward a
packet, (B) drop a packet
, and ( C) send packet to
controller.

## Slide 19: Centralized and distributed control of Openflow switches

## Slide 20: Openflow 1.0 concepts
Ports and Port queues
Flow table
Packet matching
Actions and packet forwarding
Messaging between controller and switch

## Slide 21: Open Flow Protocol Messages
Controller-to-switch: from the controller to manage or inspect the switch state
  Features, config, modify state, read state, packet-out, etc
Asynchronous: send from switch without controller soliciting
  Packet-in, flow removed/expired, port status, error, etc
Symmetric: symmetric messages without solicitation in either direction
  Hello, Echo, etc.

## Slide 22: Flow table entry
1.0 has all but VLAN ID

## Slide 23: Flow switching and routing
Each individual field + meta data
Wild Card aggregation
  E.g. IP-subnet: 192.168.*/24
Layer 4

## Slide 24: Instructions and action set
Each flow entry contains a set of instructions that are executed when a packet matches the entry
Instructions can have a set of actions to add to the action set, a list of actions to apply immediately to the packet, or modify pipeline processing
An action set is associated with each packet

## Slide 25: Openflow 1.1 concepts
Multiple flow tables
Groups
MPLS and VLANG tag support
Virtual ports
Controller connection failure

## Slide 26: Pipeline processing (Introduced in 1.1)
A switch can have many flow table that are matched in a pipeline fashion.

## Slide 27: Per table packet processing

## Slide 28: Groups
Group table: entries and actions
  To refine flooding
  Support multicast

## Slide 29: 1.2.0 concepts
Extensible match support
Extensible set_field packet-rewrite support
IPv6
Multiple controller enhancements
Etc.

## Slide 30: Most important function of Openflow
Setting up routes dynamically
  Flexible routing -- new routing scheme for data centers?
  Application specific routing
  Dynamic load balancing
  Network virtualization

## Slide 31: Some challenges in SDN
A complete paradigm shift, many unknowns
  Network OS abstraction, to clear what should and should not be done there? What is the right level of abstraction provided by the network OS?
  Flexibility .vs. performance: Can SDN keep up with the speed?
  Scalability: How can the controller be enabled to provide a global network view
  Security: how can we prevent misuse of network or defend against attack?
    Software defined network can have software bugs!!

## Slide 32: SDN and HPC
Can SDN help HPC?
  SDN needs to be incorporated into Infiniband
  Some claim that InfiniBand is already a SDN
    Can use user supplied subnet manager to do custom routing – not dynamic though
    Does it have the same capability as openflow?
SDN can help in some case
  Application specific networking
  SDN-enabled collective communication?

## Slide 33: Going further
Openflow is implemented in MiniNet (mininet.org)
Related resources
  Open Networking Foundation: https://www.opennetworking.org/
This lecture materials are based on various resources in the net, in particular this file
  https://www.clear.rice.edu/comp529/www/papers/tutorial_4.pdf
  And book “Software Defined Networks A Comprehensive Approach” by Paul Goransson and Chuck Black