## Slide 1: SDN Network Updates
Minimum updates within a single switch
Network-wide Consistent updates

## Slide 2: Updates within a single switch
Current State-of-the-art OpenFlow Switches can process tens to a few hundreds of flow-mod’s per second
  Rewriting the whole flow-table will take a while
Minimum update
  Given a configuration change (e.g. add and remove flows), how to issue the smallest number of flow-mod to achieve the objective
  Should do incremental update, but the current high-level language compiler mostly re-write the whole flow-table

## Slide 3: The minimum update problem
An example of Flow table (rules) before and after
 | Pattern | Priority | Action
A | [1, 2, *] | 5 | Port 1
B | [*, 2, 3] | 4 | Port 2
C | [1, *, 4] | 4 | Port 3
D | [1, *, 3] | 3 | Port 4
E | [*, *, 4] | 3 | Port 5
F | [*, *, 3] | 2 | Port 6
 | Pattern | Priority | Action
A | [1, 2, *] | 5 | Port 1
B | [*, 2, 3] | 4 | Port 2
G | [*, 2, 4] | 3 | Port 7
C | [1, *, 4] | 2 | Port 3
D | [1, *, 3] | 3 | Port 4
E | [*, *, 4] | 1 | Port 5
F | [*, *, 3] | 2 | Port 6
Inserting rule G [*, 2, 4] in the table with high priority, above all but rule A

## Slide 4: The minimum update problem
 | Pattern | Priority | Action
A | [1, 2, *] | 5 | Port 1
B | [*, 2, 3] | 4 | Port 2
C | [1, *, 4] | 4 | Port 3
D | [1, *, 3] | 3 | Port 4
E | [*, *, 4] | 3 | Port 5
F | [*, *, 3] | 2 | Port 6
Inserting rule G [*, 2, 4] in the table with high priority, above all but rule A.
  Insert the rule with the right priority
  Adjust the priority of other rules if necessary
  How to set the priority?

## Slide 5: The minimum update problem
 | Pattern | Priority | Action
A | [1, 2, *] | 5 | Port 1
B | [*, 2, 3] | 4 | Port 2
C | [1, *, 4] | 4 | Port 3
D | [1, *, 3] | 3 | Port 4
E | [*, *, 4] | 3 | Port 5
F | [*, *, 3] | 2 | Port 6
  Rule G: Pattern [*, 2, 4] above all but Rule A.
    Rules with overlapping patterns have interdependence
      Changing priority would change the dependence
    [*, 2, 4] overlaps with Rule A, C, and E.

## Slide 6: Capturing the dependence in the flow table – build the dependence graph
Finding the exact dependence can be tricky:
  Two rules may be independent even if their patterns overlap.
  Two rules are directly independent iff the patterns are disjoint or if the the joint of the pattern is shadowed by other rules they both depend on.

## Slide 7: The minimum update problem
Represent the minimum dependency in a flow table with a DAG
 | Pattern | Priority | Action
A | [1, 2, *] | 5 | Port 1
B | [*, 2, 3] | 4 | Port 2
C | [1, *, 4] | 4 | Port 3
D | [1, *, 3] | 3 | Port 4
E | [*, *, 4] | 3 | Port 5
F | [*, *, 3] | 2 | Port 6
A
B
C
D
E
F

## Slide 8: The minimum update problem
Insert G into the DAG
A
B
C
D
E
F
A
B
G
D
C
F
E
 | Pattern | Priority | Action
A | [1, 2, *] | 5 | Port 1
B | [*, 2, 3] | 4 | Port 2
C | [1, *, 4] | 2 | Port 3
D | [1, *, 3] | 3 | Port 4
E | [*, *, 4] | 1 | Port 5
F | [*, *, 3] | 2 | Port 6
G | [*, 2, 4] | 3 | Port 7

## Slide 9: The system
Building DAG from prioritized flowtable entries
  Incurs complicated header space computation

## Slide 10: The system
Building DAG along with policy compilation
  Rule dependency can be recursively inferred from policy composition process
  Incurs little additional overhead over compilation

## Slide 11: Priority Value Distribution
Discrete priority values
  Integers ranging [0-65535] for OpenFlow
  If new rule is inserted between adjacent priority values, we have to shift existing rules to make room for them
How to assign priority values for priority levels
  Minimize the estimation of priority shifts
Online strategy
  Unknown future policy update sequence

## Slide 12: Some things unclear
How to compute exact dependence DAG?
How to allocate priority value for each rules so as to minimize the priority changes?
Is there a way to rewrite the priority values to minimize future changes?

## Slide 13: Whole network consistent updates
“Abstractions for Network Updates”, SIGCOMM 2012.

## Slide 14: Background
Network updates happen when the network configuration changes
  Maintenance
  Failures
  ACL updates
  Etc
With traditional distributed protocol – the system will converge to a new stable, consistent state; but the transient state is hard to reason and guarantee
  Black-holes
  Loops
  Security violations
With SDN and a consistent network update abstraction, even the transient state can be managed.

## Slide 15: Network Updates challenges
Global network updates may affect many routers, must define and solve a distributed computing problem.

## Slide 16: An example

## Slide 17: An example

## Slide 18: An example

## Slide 19: Naïve Update: F1->F2->F3->I, security policy failed!

## Slide 20: An abstraction: Per-packet consistent update
Per-packet consistent update: each packet processed with old or new configuration, but not a mixture of the two.

## Slide 21: Universal Property Preservation
Theorem: Per-packet consistent update preserves all trace properties.
Trace property of a single packet’s path through the network
Example of trace Properties: Loop freedom, access control, etc

## Slide 22: Formal Verification
Corollary: to check an invariant, verify the old and new configurations.

## Slide 23: Mechanism: 2-phase update
Runtime instruments configurations
Edge rules stamp packets with version
Forwarding rules match on version
Algorithm:
  Install new rules on internal switches, leave old configuration in place
  Install edge rules that stamp with the new version number

## Slide 24: 2-phase update example

## Slide 25: 2-phase update example

## Slide 26: 2-phase update example

## Slide 27: 2-phase update example

## Slide 28: 2-phase update example

## Slide 29: 2-phase update example

## Slide 30: Optimizations
Add a path: install rules internally and then at the edge, no version.
Remove a path: update the edge, wait for all to drain, update the internal
Modify a path: subset optimization to affect the smallest number of paths.

## Slide 31: Correctness
Build an operational semantics, formalize the mechanism and prove them correct.

## Slide 32: Conclusion
Update abstractions
  Per-packet consistency
  Per-flow consistency
Mechanisms
  2-phase update
  Optimizations
Formal model
  Network operational semantics
  Universal property preservation