## Slide 1: SDN and Security
Security as a service in the cloud
  “CloudWatcher: Network Security Monitoring Using OpenFlow in Dynamic Cloud Networks”, NPSec 2012
Security extension to OpenFlow data plane
  “AVANT-GUARD: scalable and vigilant switch flow management in software-defined networks.” the ACM SIGSAC Conference on Computer & Communications Security (CCS '13), Berlin, Germany.

## Slide 2: CloudWatcher
A new framework
  Provide monitoring services for large and dynamic cloud networks
  Automatically detours network packets to be inspected by pre-installed network security devices
    OpenFlow
  Provide a script to operate this framework

## Slide 3: Operating Scenario
Register Security Devices
Create Security Policies
Parse Security Policies
Create Routing Rules
Enforce Flow Rules into Routers
Translate Routing Rules into OpenFow Rules
Administrator
Router (Device ID = 8)
{ID, TYPE, LOCATION, MODE, Func}
{1, NIDS, 8, PASSIVE, Detect HTTP}
NIDS (ID = 1)
{FLOW CONDITON, DEVICE SET}
{10.0.0.1  20.0.0.2, {1}}

## Slide 4: How to Control Flows
4 approaches
  Multipath naïve
  Shortest through
  Multipath shortest
  Shortest inline
- Sample network -
S: start node, E: end node
R: router, C: security device

## Slide 5: Simple Shortest Path
Basic routing scheme (NOT CloudWatcher’s idea)
  Find the shortest path between a start host and an end host
  Path: S  R1  R5  R6  E

## Slide 6: Multipath Naïve (algorithm 1)
Find multiple paths
  Shortest path between S and E
  Shortest path between S and C
  Path
    S  R1  R5  R6  E
    S  R1  R2  R3  R4
OpenFlow provides a function to send packets to multiple outputs
  E.g., R1  {R2, R5}

## Slide 7: Shortest Through (algorithm 2)
Find the shortest path passing through R4
  Shortest path between S and R4
  Shortest path between R4 and E
  Path: S  R1  R2  R4  R4  R6  E

## Slide 8: Multipath Shortest (algorithm 3)
Improved version of multipath naïve
Two phase
  Find the shortest path (P1)
    S  R1  R5  R6  E
  Find the shortest path between routers on the path P1 and R4
    R6  R4
    R6  {R4, E}

## Slide 9: Shortest Inline (algorithm 4)
Find a path passing through (a) specific link(s) (not node)
Good for delivering network packets to inline devices
  E.g., IPS (intrusion prevention system)

## Slide 10: Summary for Flow Control Methods
 | Pros | Cons | When to use
Multipath Naïve | Simple and fast | Redundant flows | Enough network capacity, delay is important
Shortest Through | Efficient | Computation overhead, when multiple devices | Not enough network capacity, delay is not so important
Multipath Shortest | Efficient | Computation overhead | Not many hops (e.g., communication between inside VMs)
Shortest Inline | Guarantee passing through a specific link | Computation overhead, when multiple devices | For an inline security device (e.g., IPS)

## Slide 11: Implementation and Evaluation
CloudWatcher is implemented
  As an OpenFlow application
    Running on NOX controller
    Implemented in Python
Verify each algorithm on emulated networks
  Use Mininet to emulate networks supporting OpenFlow

## Slide 12: Conclusion
CloudWacther provides a new framework to monitor cloud networks
  With the help of the SDN technology
A cloud administrator can select algorithms based on network status
A cloud administrator can monitor his network by writing simple scripts

## Slide 13: Avant-Guard
  “AVANT-GUARD: scalable and vigilant switch flow management in software-defined networks.” the ACM SIGSAC Conference on Computer & Communications Security (CCS '13), Berlin, Germany.
  Address two challenges
    Speed mismatch between data and control plane makes OpenFlow network vulnerable to control plane saturation attack (DDOS) – connection migration to reduce the interaction between data plane and control plane
    Expedite the detection and responses to the changing network dynamics – actuating triggers over data plance’s existing statistics collection services

## Slide 14: Architecture of Avant-Guard

## Slide 15: Connection Migration - Idea
Inspired by TCP SYN Cookie
Concept
  TCP connection will stat from a SYN packet, and an initiator will wait for TCP SYN/ACK packet
  TCP-handshake does not issue any kind of data delivery
  Then, how about treating this TCP-handshake at network devices
  instead of target hosts
SYN
SYN/ACK
ACK
SYN
SYN/ACK
ACK
Source: S. Shin, et al.

## Slide 16: Connection Migration – Access Table
List of visiting clients
  Format
    Client IP address: # of TCP connection trials
      # of TCP connection trials include wrong trials (ACK, FIN, and RST)
    Simple data structure : 6 bytes (4 bytes for IP and 2 bytes for
    counter)
Overhead
  1,000,000 client IP addresses  less than 6 MB of memory
A controller application can read this table
10.0.0.1
15
12.2.0.1
1
40.0.0.4
100
IP Address
Counter
Source: S. Shin, et al.

## Slide 17: Connection Migration – State Diagram
Distinguish between TCP connections that will complete (good) and not complete (bad)
4 state
  Classification
    Distinguish useful TCP connections
  Report
    Report to a controller
  Migration
    Migrate a TCP connection
    if it is a useful (or valid) connection
  Relay
    Relay all TCP packets between a
    connection source and a destination
Classification stage
Report
stage
Migration
stage
Replay
stage
TCP sessions
Failed
TCP sessions
Then, Ignore
Established
TCP sessions
Allow
Migration
Success or
Failure
Allow
Relay
Source: S. Shin, et al.

## Slide 18: Connection Migration : classification stage
Flow chart
- The case of receiving TCP SYN/RST/FIN packet

## Slide 19: Connection Migration: classification stage
Flow chart
- The case of receiving TCP ACK packet

## Slide 20: Connection Migration – Packet Diagram
A
B
Control Plane
(1) TCP SYN
(2) TCP SYN/ACK
(3) TCP ACK
(6) TCP SYN
(7) TCP SYN/ACK
(8) TCP ACK
(11) TCP ACK
TCP Data
(12) TCP ACK
TCP Data
(4)
(5)
(9)
(10)
A-1: A --> B: Migrate
A-2: A --> B: Relay
Data Plane
Classification stage
Relay stage
Migration stage
Relay stage
Report stage
Report stage
Source: S. Shin, et al.

## Slide 21: Delayed Connection Migration
Concept
  Delay Connection Migration until the data plane receives (a) data
  packet(s)
Why?
  Good for reducing the effects of some advanced attacks
    E.g., fake TCP connection setup
A
B
Control Plane
(1) TCP SYN
(2) TCP SYN/ACK
(3) TCP ACK
(7) TCP SYN
(8) TCP SYN/ACK
(9) TCP ACK
(4) TCP ACK
TCP Data
(12) TCP ACK
TCP Data
(5)
(6)
(10)
(11)
A-1: A --> B: Migrate
A-2: A --> B: Relay
Data Plane
Classification stage
Migration stage
Relay stage
Report stage
Report stage

## Slide 22: Actuating Trigger - Idea
Two functions
  Report the following items to the control plane
  asynchronously
    Network status
    Payload information
  Activate flow rules based on some predefined conditions
    Security application can use this feature to turn on security policies without delay
Source: S. Shin, et al.

## Slide 23: Activating Trigger – Operations
4 main operations
  In the control plane
    Define a condition
    Register the condition
  In the data plane
    Check the condition
    When the condition is satisfied,
      Report a network
      status or payload
      Activate a flow rule
Flow Rule
Condition
Predefined Flow Rule
Control Plane
Host
(1) Define condition
(2) Register condition
(3) Check condition
(4-2) Activate a flow rule
(4-1) Report status
Data Plane
match
Source: S. Shin, et al.

## Slide 24: Activating Trigger - Example
Example of reporting payload
  1) defined a condition : want to see payloads of packet from 10.0.0.1
  2) register this condition to the data plane
  3) packet is delivered from 10.0.0.1
  4) payload is delivered to the control plane
10.0.0.1 *
1: Condition for payload
Control Plane
10.0.0.1
(1)
Data Plane
10.0.0.2
(2)
(3)
(4)
Source: S. Shin, et al.

## Slide 25: Implementation
Data plane
  Implemented in the Software-based OpenFlow reference switch
    Covers OpenFlow spec. 1.0.0
Control plane
  Implemented in the POX controller
Extend OpenFlow protocols for
  Connection migration
    E.g., OFPFC_MIGRATE, …
  Actuating trigger
    E.g., OFPFC_REG_PAYLOAD, …
  More in the paper (Table 1)
Source: S. Shin, et al.

## Slide 26: Evaluation – Use Case
Network saturation attack case
  A normal client sends HTTP requests to a web server
  An attacker tries a SYN flooding attack to a web server
Test Scenario
Packet delivered rate to a web server
Nearly 0 loss
Normal
Attacker
OF switch
POX Controller
Web Server
Normal
Attacker
OF switch
(Avant-Guard)
Modified
POX Controller
Web Server

## Slide 27: Evaluation – Use Case
Detecting SYN flooding/scanning
  Approach
    SYN flooding packets are automatically rejected
    Network scanning attackers will be confused by our response
    packets
      They may think that all network hosts are alive and all network ports
      are open (a kind of White hole)
SYN
SYN/ACK
(1)
(2)
No packet delivery
SYN
SYN/ACK
(1)
(2)
SYN Flooding
Network Scanner
No packet delivery
Attacker receives SYN/ACK packets even though there are no hosts
 White hole

## Slide 28: Evaluation – Use Case
Intelligent Honeynet
  Approach
    When we try to do connection migration,
      If we can not find a real target host, we may consider this
      connection as suspicious
    Then, a security application can redirect this connection to our honeynet automatically
    Finally, this attacker will perform malicious operations inside a honenet
SYN
SYN/ACK
ACK
SYN
(1)
(2)
(3)
(4)
No host
SYN
(5)
SYN/ACK
(6)
(7)
ACK
attacker
honeynet
Source: S. Shin, et al.

## Slide 29: Evaluation - Overhead
Connection migration
normal | connection migration | overhead
1608.6 us | 1618.74 us | 0,626 %
Actuating trigger
item | time
Traffic-rate based condition check | 0.322 us
Payload based condition check | = 0
Rule activation | 1.697 us
Source: S. Shin, et al.

## Slide 30: Summary
Avant-Guard
  New data plane architecture for addressing the problems of OpenFlow, when devising network security applications
    Address the scalability issue with the connection migration scheme
    Address the responsiveness issue with the actuating trigger scheme
  Can be a new candidate architecture of the future data plane for SDN
Source: S. Shin, et al.