## Slide 1: Software Defined Networking (SDN)
  A brief introduction
  SDN promises and challenges

## Slide 2: What and Why “software defined?”
“Software defined” becomes very popular words
  Software defined networking, software defined storage, software defined radio, etc.
What is it?
  Underlying system feature is exposed to the upper layer application developer through an API.
  System functionality is implemented over the API as an app.
Another word for “Software defined” is “Programmable.”

## Slide 3: Software defined networking
Basic network functions: allowing nodes in the network to communicate with one another.
  Network elements connected by links form a topology
  Each node runs some kind of distributed algorithm, e.g. OSPF, to figure out the path from A to B.
  Network administrator can change network parameters to achieve certain objective: e.g. changing routes
    Limited programmability
  Equipment vendors provide a set of routing (network control) choices: OSPF, ISIS, BGP, etc
    If one wants something beyond this set, he is out of luck.
    This is what SDN tries to overcome: making the network control like an APP that user can develop by themselves.
    SDN is to make network control programmable.
A
B
C
D
E

## Slide 4: SDN motivation
Why do we want to make network control programmable?
  Short term:
    Existing network control is no longer sufficient in several important areas, need innovation here!
      Data centers, Wireless, network security
    Existing network control is getting too complicated.
      A lot of different middleboxes, each speaks its own language, and interferences with one another
        NAT, firewall, IDS, WAN optimizer, load balancer, traffic shapers, transparent web proxy, application accelerators
      Would be nice to provide a unified mechanism to deploy and manage these middleboxes
      SDN promises this.
  Long term: innovation is good for the networking industry.

## Slide 5: Computing systems once upon a time
Vertically integrated systems
  Proprietary hardware
  Proprietary OS
  Proprietary applications
  Highly reliable
  Can you picture google, yahoo, facebook on such a platform?
    Slow software innovation
      Proprietary development
    Small industry

## Slide 6: Computing systems now
App
App
App
App
App
App
App
App
App
App
App
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Microprocessor
Open interfaces
Fast innovation
  Everyone can
  participate
Hugh industry
  Software is now part of everything.

## Slide 7: Conventional networking system today (before SDN)
Mainframe mindset: software for the control plane cannot be separated from the forwarding hardware in the data plane.
  Vertically integrated, complex, closed, proprietary
  Innovation is only possible if one has access to the router box.
    No significant innovation in the past 40 years.
Custom hardware
OS
Bundled applications

## Slide 8: Ideal networking system for innovation
App
App
App
App
App
App
App
App
App
App
App
Net Linux
Net Mac
OS
Net Windows
or
or
Open Interface
Open Interface
Network hardware
API for controlling
Network hardware
Network Operating Systems
API of Net OS
Network apps

## Slide 9: Control plane and data plane
Control plane of a network
  The functions of a network that control the behavior of the network
    E.g.: Which path to take for a packet? Which port to forward a packet? Should the packet be dropped?
  Control plane functions are typically realized by software such as routing protocols, firewall code, etc.
Data plane of a network
  The functions of a network that actually forward or drop packets.
  Data plane functions are typically realized by hardware
Control plane and data plane are vertically integrated in traditional networking equipment
  Separating software from hardware  separating control plane from data plane.

## Slide 10: Ideal networking system for innovation
Separate hardware from software
Standardize the interface
  Each layer provides an abstraction
Innovation is possible for anyone just like software development for a computing system.
This is the vision of SDN/OpenFlow.
App
App
App
App
App
App
App
App
App
App
App
Net Linux
Net Mac
OS
Net Windows
or
or
Open Interface
Open Interface

## Slide 11: SDN now: separate forwarding hardware from controlling software
App
App
App
App
App
App
App
App
App
App
App
Net Linux
Net Mac
OS
Net Windows
or
or
Open Interface
Open Interface
OpenFlow: standardized for
Ethernet/IP/TCP
2. OpenFlow enabled switches/routers
simple hardware doing forwarding only
forwarding table can be set by other
entity through OpenFlow
3. SDN controllers (floodlight, nox, etc)
4. Firewall, virtual network, TE, etc
Northbound API, not standardized yet

## Slide 12: Contrast between SDN and conventional network
SDN | Conventional
Controller may not be in the same box as the forwarding hardware | Forwarding hardware and its control are in the same box
Centralized routing algorithm with logically global view | Distributed routing algorithm
Network functions are realized with a global view | Network functions must be realized in a distributed manner, error-prone
New abstraction must be developed for the centralized view | Network abstraction is embedded in the distributed algorithms

## Slide 13: Major paradigm shift with SDN
No longer use distributed control protocols
  Design one distributed system (NOS) with the global view of the network
  Use for all control functions
Now just defining a centralized control function
  Configuration = Function(global view)
This may look easier, but this is not how it used to work, everything is new – innovation at all levels for this to happen.
  High level programming languages to describe network configuration
  Compiling and runtime system to realize the program efficiently, correctly, and safely.
  Abstraction design
  Debugging infrastructure
  network OS design
  etc.

## Slide 14: How an SDN operates?
Network applications specification the network functions (not the detailed implementation on the physical devices):
  Access control: who can talk to who
  Isolation: who can hear my broadcasts
  Routing: only specify routing to the degree you care
    Some flows over satellite, others over landline
  TE: specify in terms of quality of service, not routes
Network OS (or something like a compiler) compiles the network application and computes the configurations on physical devices based on the global view
Network OS distributes the configuration to physical devices through OpenFlow.

## Slide 15: SDN promises
A lower-entry point for innovation in the network control.
Solve the issues in the current network configuration challenges.
  data plane interacts with many control entities
  Configure locally to achieve a global network function.

## Slide 16: Some SDN issues
Abstraction
  A new programming system to specify network functions (programming SDN)
  An API that provides network abstraction to network application (SDN controller design)
Performance (scalability)
  Controller
  Communication between controller and devices
  Forwarding
Correctness and debugging – A SDN program has a higher bar than a typical program, multiple levels
Security