## Slide 1: Mininet and Openflow Labs

## Slide 2: Install Mininet (do not do this in class)
Download VirtualBox
Download Xming for windows (X11)
Download Mininet VM for linux-ubuntu
Start VirtualBox
Create a new VM for linux-ubuntu and the Mininet VM as the disk image
Start the VM
Set network device forwarding 127.0.0.1:2222 to virtual machine port 22.
  This allows you to ssh to 127.0.0.1:2222 to login to the Mininet VM
Login with mininet:mininet – this is just like any other Linux machine.

## Slide 3: Lab 1: Mininet Walkthrough
Perform the steps at http://mininet.org/walkthrough
Objective:
  Understand how to use mininet
  How to run a command on each host
  Learn how to change network parameters in mininet
    Link bandwidth, latency, topology, etc
  Learn how to write python code for new topologies
    Make sure that you understand the custom topology example

## Slide 4: Lab 1: Mininet Walkthrough
Login to crux (enable X11 forwarding).
crux>ssh mininet@localhost –p 2222 (3333, 4444, …)
password: mininet
Follow the walk through.

## Slide 5: Lab 1 exercise
Write the Python script to create the topology in hw1.

## Slide 6: Lab 2: Manually configure Openflow switches with dpctl
  Objectives
    Understand how an Openflow switch behaves
    Understand what an Openflow controller supposes to do to enable communication.
  Dpctl: a command-line utility that sends openflow messages to a switch
    View switch configuration and capability
    View flow table entries
    Add, delete, and modify flow table entries
  Useful tool for learning and debugging
    Human faking an openflow controller
  ‘man dpctl’ for more details

## Slide 7: Lab 2: Manually configure Openflow switches with dpctl
  $ sudo mn --topo single,3 --mac --switch ovsk --controller remote
    This creates a simple host with 3 switches, the mac addresses are assigned in a certain way, the switch is an Open vSwitch (software OpenFlow switch), controller is supposed to be at local host with port number 6633.
    Mininet> net
    Mininet> h1 ifconfig
    Mininet> h2 ifconfig
    The switch can be controlled at tcp:127.0.0.1:6634
  Mininet>pingall
    This fails as the switch has nothing in its flow table
  Start another window do ‘man dpctl’ and ‘man ovs-dpctl’
  $ dpctl show tcp:127.0.0.1:6634
    Tcp:127.0.0.1:6634 is the switch port for control
  $dpctl dump-flows tcp:127.0.0.1:6634
    The flow table is empty

## Slide 8: Lab 2: Manually configure Openflow switches with dpctl
$dpctl add-flow tcp:127.0.0.1:6634 in_port=1,idle_timeout=1000,actions=output:2
$dpctl add-flow tcp:127.0.0.1:6634 in_port=2,idle_timeout=1000,actions=output:1
  $dpctl dump-flows tcp:127.0.0.1:6634
  Mininet> pingall
    H1 and h2 are now connected.
  $dpctl dump-flows tcp:127.0.0.1:6634
    Check the statistics
  Mininet> s1 dpctl dump-flows tcp:127.0.0.1:6634
  Continue the exercise to completely install flow table for all hosts.
  Try the following:
$dpctl add-flow tcp:127.0.0.1:6634 dl_dst=0:0:0:0:0:1,idle_timeout=1000,actions=output:1
$dpctl add-flow tcp:127.0.0.1:6634 dl_dst=0:0:0:0:0:2,idle_timeout=1000,actions=output:2
$dpctl add-flow tcp:127.0.0.1:6634 dl_dst=0:0:0:0:0:3,idle_timeout=1000,actions=output:3
  $dpctl dump-flows tcp:127.0.0.1:6634
  Mininet> pingall

## Slide 9: Lab 2: Manually configure Openflow switches with dpctl
  Try the following:
  $dpctl add-flow tcp:127.0.0.1:6634 idle_timeout=1000,actions=flood
  Mininet> pingall
$dpctl add-flow tcp:127.0.0.1:6634 dl_dst=ff:ff:ff:ff:ff:ff,idle_timeout=1000,actions=flood
Mininet>pingall
dpctl del-flows tcp:127:0.0.1:6634
dpctl dump-flows tcp:127.0.0.1:6634
$dpctl add-flow tcp:127.0.0.1:6634 dl_dst=ff:ff:ff:ff:ff:ff,idle_timeout=1000,actions=flood
$dpctl add-flow tcp:127.0.0.1:6634 dl_dst=0:0:0:0:0:1,idle_timeout=1000,actions=output:1
Mininet>pingall
how to make the ping successful for one pair of hosts?

## Slide 10: Lab 2 execise: manually setup openflow switches with dpctl
Set up a network with the following topology such that all communication can be realized between each pair of hosts: using destination based routing. Using hw1 topology
  $ dpctl show tcp:127.0.0.1:6634
  $ dpctl show tcp:127.0.0.1:6635
  $ dpctl show tcp:127.0.0.1:6636

## Slide 11: Lab 3: a naïve POX controller
Objectives
  Moving commands from dpctl to a POX controller
  Understand how the POX controller interacts with switches
POX document
  https://openflow.stanford.edu/display/ONL/POX+Wiki
See POX controller examples forwarding/hub.py at pox/forwarding/hub.py
  See the flow_mod message that add one flow table entry to flood all packets – turning each connected switch to a hub.
  To use the controller:
    $ sudo mn --topo linear,4 --mac --switch ovsk --controller remote
      The default controller is at the same machine with port number 6633.
      Different switches are at tcp:127.0.0.1:6634{6635, 6636,…}
    $./pox.py forwarding.hub
      Create a controller running on local machine port 6633, will connect with the openflow switches.
      Pay attention to how the flow table entries are created
      Pay attention to the connectionup event
    $dpctl dump-flows tcp:127.0.01:6634
    $dpctl dump-flows tcp:127.0.01:6635
    Mininet> pingall

## Slide 12: Lab3: A naïve POX controller
See lab3.py and lab3_controller.py
Put lab3_controller.py under pox/ext
Run lab3.py with ‘$sudo ./lab3.py’
Use dpctl to see the flow-table on each switch.
s1 s2 s3
h1
h3
h2

## Slide 13: Lab3 exercise: A naïve POX controller
Modify lab3.py and lab3_controller.py to setup the connectivity of the topology of hw1.

## Slide 14: Lab4: Shortest path forwarding
Try my_lab4.py (‘sudo ./my_lab4.py’)
Read the code for topology discovery and path calculation in forwarding/l2_multi.py