## Slide 1: Chapter 5: Network Layer (Part III)
Routing Protocols in the Internet
  RIP, OSPF, BGP
More on IP
  Fragmentation and Reassembly
  ICMP
Readings
  Sections 5.5-5.6

## Slide 2: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
special routers in AS
run intra-AS routing protocol with all other routers in AS
also responsible for routing to destinations outside AS
  run inter-AS routing protocol with other gateway routers
gateway routers

## Slide 3: Intra-AS and Inter-AS routing
Gateways:
  perform inter-AS routing amongst themselves
  perform intra-AS routing with other routers in their AS
inter-AS, intra-AS routing in
gateway A.c
network layer
link layer
physical layer
a
b
b
a
a
C
A
B
d
A.a
A.c
C.b
B.a
c
b
c

## Slide 4: Intra-AS and Inter-AS routing
Inter-AS
routing
between
A and B
Host
h2
a
b
b
a
a
C
A
B
d
c
A.a
A.c
C.b
B.a
c
b
Host
h1
Intra-AS routing
within AS A
Intra-AS routing
within AS B

## Slide 5: Why different Intra- and Inter-AS routing ?
Policy:
Inter-AS: admin wants control over how its traffic routed, who routes through its net.
Intra-AS: single admin, so no policy decisions needed
Scale:
hierarchical routing saves table size, reduced update traffic
Performance:
Intra-AS: can focus on performance
Inter-AS: policy may dominate over performance

## Slide 6: Intra-AS Routing
Also known as Interior Gateway Protocols (IGP)
Most common IGPs:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 7: RIP ( Routing Information Protocol)
Distance vector algorithm
Included in BSD-UNIX Distribution in 1982
Distance metric: # of hops (max = 15 hops)
  Can you guess why?
Distance vectors exchanged
  every 30 sec (plus a jitter) via Response Message (also called advertisement)
  When network topology changes
Each advertisement: route to up to 25 destination nets

## Slide 8: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec  neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to other neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly propagates to entire net

## Slide 9: RIP Table processing
RIP routing tables managed by application-level process called routed (daemon)
advertisements sent in UDP packets, periodically repeated

## Slide 10: OSPF (Open Shortest Path First)
“open”: publicly available
  Gated
Uses Link State algorithm
  LS packet dissemination
  Topology map at each node
  Route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor router
Advertisements disseminated to entire AS (via controlled flooding)

## Slide 11: Neighbor Discovery and Maintenance
OSPF Hello protocol
Sends Hello packets on all its interfaces
  Every Hello Interval (default 10 sec)
Helps detect the failure of neighbors
Neighbor is designated as failed
  If no Hello for Dead Interval (40 sec)

## Slide 12: OSPF “advanced” features (not in RIP)
Security: all OSPF messages authenticated (to prevent malicious intrusion);
Multiple same-cost paths allowed (only one path in RIP)
For each link, multiple cost metrics for different TOS (eg, satellite link cost set “low” for best effort; high for real time)
Integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
Hierarchical OSPF in large domains.

## Slide 13: Inter-AS routing

## Slide 14: Internet Inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto standard
Path Vector protocol:
  similar to Distance Vector protocol
  each Border Gateway broadcast to neighbors (peers) entire path (I.e, sequence of ASs) to destination
  E.g., Gateway X may send its path to dest. Z:
Path (X,Z) = X,Y1,Y2,Y3,…,Z

## Slide 15: Internet Inter-AS routing: BGP
BGP messages exchanged using TCP.
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 16: Internet Inter-AS routing: BGP
Suppose: gateway X send its path to peer gateway W
W may or may not select path offered by X
  cost, policy (don’t route via competitors AS), loop prevention reasons.
If W selects path advertised by X, then:
Path (W,Z) = W, Path (X,Z)
Note: X can control incoming traffic by controlling its route advertisements to peers:
  e.g., don’t want to route traffic to Z  don’t advertise any routes to Z

## Slide 17: BGP: an example
NLRI=128.186.0.0/16
ASPATH=[0]
128.186.0.0/16
NLRI=128.186.0.0/16
ASPATH=[10]
NLRI=128.186.0.0/16
ASPATH=[10]
NLRI=128.186.0.0/16
ASPATH=[210]
NLRI=128.186.0.0/16
ASPATH=[610]
NLRI=128.186.0.0/16
ASPATH=[610]
NLRI=128.186.0.0/16
ASPATH=[210]
NLRI=128.186.0.0/16
ASPATH=[7610]
NLRI=128.186.0.0/16
ASPATH=[4210]
NLRI=128.186.0.0/16
ASPATH=[3210]
[3210]*
[4210]
[7610]
NLRI=128.186.0.0/16
ASPATH=[53210]

## Slide 18: A feature of BGP
X
Y
Z
W
[Z]
[YZ]
[YZ]
[XYZ]
[WYZ]
[YZ]*
[WYZ]
[YZ]*
[XYZ]
Avoid looping problem in distance vector algorithms

## Slide 19: Shortcoming of BGP
May still take long time to converge
  Invalid routes can still be selected/propagated
[3210]*
[4210]
[7610]
NLRI=128.186.0.0/16
ASPATH=[57610]
NLRI=128.186.0.0/16
ASPATH=[54210]
NLRI=128.186.0.0/16
Withdrawal
  Situation can be worse on global Internet
    Up to 15 minutes converging time observed in Internet
    O(k!) alternative paths explored theoretically

## Slide 20: Solving BGP Path Exploration
Idea is simple, but extremely hard
  Scalability
  Confidentiality
Simple AS graph vs. actual Internet topology
  Each network has multiple BGP routers
    Intra-domain vs. inter-domain errors
  Two Ases may have multiple peering links
    Single link failure vs. mulit-link failure
  Links have diff prop delays and events occur in short duration
    Which update is newer?

## Slide 21: BGP Security
Accidents (caused by human errors)
  Most of them not malicious
  June 2015, Malaysian route leak
  2010, Chinese hijack (affects cnn.com, amazon.de, and rapidshare.com etc)
  24 Feb 2008, Pakistan knocked Youtube offline
  07 May 2005, AS 174 took Google’s 64.233.161.0/24
  24 Dec 2004, Anatomy of a Leak: AS9121
    100K+ routes announced
  6 Apr 2001: C&W routing instability
  25 Apr 1997: 7007 Explanation and Apology
  Check NANOG mailing list for more accidents

## Slide 22: The Internet Network layer
routing
table
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 23: More on IP

## Slide 24: IP Packet Format

## Slide 25: Fields in IP Packet
IP protocol version
  Current version is 4
Header length
  Number of 32-bit quantities in the header
Type of Service
  3-bit Priority
  Delay, Throughput, Reliability bits
Total length
  Including header (maximum 65535 bytes)

## Slide 26: Fields in IP Packet
Identification
  All fragments of a packet have same identification
Flags
  Don’t Fragment, More Fragments
Fragment offset
  Where in the original packet (count in 8 byte units)
Time to live
  Life time of packet
Protocol Type
  TCP, UDP etc

## Slide 27: IP Fragmentation & Reassembly
Each subnet has its own MTU size
  Maximum Transmission Unit
An IP packet is chopped into smaller pieces if
  Packet size is greater than network MTU, and
  Don’t fragment option is not set
Each datagram has unique identification
  All fragments carry original datagram id
All fragments except the last have more flag set

## Slide 28: IP Fragmentation &Reassembly
Datagram assembly done only at destination
  Why not at a router?
Use datagram id to put pieces together
  The last piece indicated with more bit 0
  Offset plus the length tell whether any
    Holes missing in the middle
Setup a reassembly timer after first fragment
  If all pieces in time, pass the pkt to upper layer
  If some do not arrive in time, discard the fragments
No recovery from lost fragments (why?)

## Slide 29: IP Fragmentation & Reassembly
large IP datagram fragmented within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
reassembly

## Slide 30: IP Fragmentation and Reassembly
ID
=x
offset
=0
moreflag
=0
length
=4000
ID
=x
offset
=0
moreflag
=1
length
=1500
ID
=x
offset
=1480
moreflag
=1
length
=1500
ID
=x
offset
=2960
moreflag
=0
length
=1040
One large datagram becomes
several smaller datagrams

## Slide 31: Fragmentation Example

## Slide 32: Internet Control Message Protocol
An error reporting mechanism
  Time exceeded
    Packet discarded because TTL was 0
  Destination unreachable
    Router cannot locate destination
  Source quench
    Buffer overflow, request source to reduce rate
  Redirect
    Suggest a better router

## Slide 33: ICMP Message Transport
ICMP messages carried in IP datagrams
Treated like any other datagram
  But no error message sent if
    ICMP message causes error
Message sent to the source
  Original Internet header, plus
  8 bytes of the original datagram’s data included
  For source to match original process.

## Slide 34: ICMP Usage
Testing reachability
  ICMP echo request/reply
  ping
Tracing route to a destination
  Time-to-live field
  Traceroute
Path MTU discovery
  Don’t fragment bit

## Slide 35: Other Internet Control Protocols
ARP solves problem
  Given IP address, find MAC address
Reverse Address Resolution Protocol (RARP)
  Given MAC address, find IP address, and more …
  Used by, e.g., diskless machines
Items to be configured
  IP address
  Default router address
  Subnet mask
  DNS server address

## Slide 36: IP addresses: how to get one?
Hard-coded by system admin in a file
Dynamic Host Configuration Protocol
  dynamically get address: “plug-and-play”
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 37: Network Layer Summary
Network service
  datagram vs virtual circuit
Routing protocols
  Link state and distance vector
  RIP, OSPF, BGP
Fragmentation and Reassembly
Case studies
  IPv4