## Slide 1: Chapter 6: Transport Layer (Part II)
Transmission Control Protocol (TCP)
  Connection Management
  Error/Flow/Congestion Control
User Datagram Protocol (UDP)
Readings
  Sections 6.4, 6.5, 5.3.1, 5.3.2, 5.3.4

## Slide 2: TCP: Overview
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 3: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)
PSH: push data now
(generally not used)

## Slide 4: TCP Connection Management: establish a connection
TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  seq. #s
  buffers, flow control info
client: connection initiator
server: contacted by client
Three-way handshake:
Step 1: client end system sends TCP SYN control segment to server
  specifies initial seq #
Step 2: server end system receives SYN, replies with SYNACK control segment
  ACKs received SYN
  allocates buffers
  specifies server  receiver initial seq. #
Step 3: client replies with an ACK segment

## Slide 5: TCP Connection Management: close a connection
Modified three-way handshake:
client closes socket:
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait
Step 3: client receives FIN, replies with ACK.
Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Socket programming interface
  close() vs shutdown()

## Slide 6
CLOSED
LISTEN
SYN_RECV
SYN_SENT
CLOSE_WAIT
LAST_ACK
ESTABLISHED
FIN_WAIT_1
FIN_WAIT_2
CLOSING
TIME_WAIT
Initial state
Application.: passive Öpening
Send: ---
Application.: active opening send: SYN
Passive opening
Receive: SYN;
send: SYN, ACK
Receive: RST
Application.: send data Send: SYN
Receive: SYN send: SYN, ACK
Simultanous opening
Receive: SYN, ACK Send: ACK
Receive: ACK Send: ---
Receive: FIN Send: ACK
Application: close Send: FIN
Application: close
Send: FIN
Receive: ACK Send: ---
Application: close
Send: FIN
Receive: ACK Send: ---
Receive: FIN Send: ACK
Receive: FIN Send: ACK
Receive: FIN, ACK Send: ACK
Receive: ACK Send: ---
2 MSL timeout
MSL: max. segment life
Send timeout: RST
Passive close
Active close
Simultanous close
Data transmission
Application: close or timeout
TCP connection
Management
Finite state machine

## Slide 7: TCP Seq. #’s and ACKs
time
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
simple telnet scenario
Seq. #’s:
byte stream “number”of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
  cumulative ACK

## Slide 8: TCP SYN/FIN Sequence #
TCP SYN/FIN packets consume one sequence number
For simplification, seq # counts pkts numbers in the example
In reality, it is byte counts
client
server
SYN(J)
SYN/ACK(K,J+1)
ACK(K+1)
FIN(M)
ACK(M+1)
FIN(N)
ACK(N+1)
DATA(J+1)
ACK(J+2)

## Slide 9: TCP data reliable transmission
Theoretically, for every packet sent for which the sender expects an ACK,
  A timer is started
    What is the timeout duration?
  When timer expires, this packet retransmitted
  This applies to both data packets and control packets SYN and FIN
  Note that ACK is cumulative
Receiver
  Accept out-of-order packets
  Respond by acking last pkt received in order
So, is TCP using Go-Back-N or Selective Repeat?
  Hybrid, more like GBN

## Slide 10: TCP: Timeout and retransmission scenarios
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
time
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
Host A
Seq=100, 20 bytes data
ACK=100
Seq=92 timeout
time
premature timeout,
cumulative ACKs
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=100 timeout
ACK=120

## Slide 11: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
longer than RTT
  note: RTT will vary
too short: premature timeout
  unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions, cumulatively ACKed segments
SampleRTT will vary, want estimated RTT “smoother”
  use several recent measurements, not just current SampleRTT

## Slide 12: TCP Round Trip Time and Timeout
EstimatedRTT = (1-x)*EstimatedRTT + x*SampleRTT
Exponential weighted moving average (EWMA)
influence of given sample decreases exponentially fast
typical value of x: 0.1
Setting the timeout
EstimtedRTT plus “safety margin”
large variation in EstimatedRTT  larger safety margin
Timeout = EstimatedRTT + 4*Deviation
Deviation = (1-x)*Deviation +
x*|SampleRTT-EstimatedRTT|

## Slide 13: TCP RTT and Timeout (Cont’d)
What happens when a timer expires?
  Exponential backoff: double the Timeout value
  An upper limit is also suggested (60 seconds)
How about the timeout value for the first packet?
  It should be sufficient large
  3 seconds recommended in RFC1122
That is, when a timer expires, we do not use the
above formulas to compute the timeout value for TCP

## Slide 14: Flow/Congestion Control
Sometimes sender shouldn’t send a pkt whenever its ready
  Receiver not ready (e.g., buffers full)
  Avoid congestion
    Sender transmits smoothly to avoid temporary network overloads
  React to congestion
    Many unACK’ed pkts, may mean long end-end delays, congested networks
    Network itself may provide sender with congestion indication

## Slide 15: TCP Flow Control
receiver: explicitly informs sender of (dynamically changing) amount of free buffer space
  RcvWindow field in TCP segment
sender: keeps the amount of transmitted, unACKed data less than most recently received RcvWindow
sender won’t overrun
receiver’s buffers by
transmitting too much,
too fast
flow control
receiver buffering
RcvBuffer = size of TCP Receive Buffer
RcvWindow = amount of spare room in Buffer

## Slide 16: What is Congestion?
Informally: “too many sources sending too much data too fast for network to handle”
Different from flow control!
Manifestations at the end points:
  First symptom: long delays (long queuing delay in router buffers)
  Final symptom: Lost packets (buffer overflow at routers, packets dropped)

## Slide 17: Effects of Retransmission on Congestion
Ideal case
  Every packet delivered successfully until capacity
  Beyond capacity: deliver packets at capacity rate
Reality
  As offered load increases, more packets lost
    More retransmissions  more traffic  more losses …
  In face of loss, or long end-end delay
    Retransmissions can make things worse
  Decreasing rate of transmission
    Increases overall throughput

## Slide 18: Congestion: Moral of the Story
When losses occur
  Back off, don’t aggressively retransmit
Issue of fairness
  Social versus individual good
  What about greedy senders who don’t back off?

## Slide 19: Taxonomy of Congestion Control
Open-Loop (avoidance)
  Make sure congestion doesn’t occur
  Design and provision the network to avoid congestion
Closed-Loop (reactive)
  Monitor, detect and react to congestion
  Based on the concept of feedback loop
Hybrid
  Avoidance at a slower time scale
  Reaction at a faster time scale

## Slide 20: Closed-Loop Congestion Control

## Slide 21: Closed-Loop Congestion Control
Explicit
  network tells source its current rate
  Better control but more overhead
Implicit
  End point figures out rate by observing network
  Less overhead but limited control
Ideally
  overhead of implicit with effectiveness of explicit

## Slide 22: Closed-Loop Congestion Control
Window-based vs Rate-based
  Window-based: No. of pkts sent limited by a window
  Rate-based: Packets to be sent controlled by a rate
    Fine-grained timer needed
    No coupling of flow and error control
Hop-by-Hop vs End-to-End
  Hop-by-Hop: done at every link
    Simple, better control but more overhead
  End-to-End: sender matches all the servers on its path

## Slide 23: Approaches towards Congestion Control
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
Network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (TCP/IP ECN, SNA DECbit, ATM)
  explicit rate sender should send at
Two broad approaches towards congestion control:

## Slide 24: TCP Congestion Control
Idea
  Each source determines network capacity for itself
  Uses implicit feedback, adaptive congestion window
  ACKs pace transmission (self-clocking)
Challenge
  Determining the available capacity in the first place
  Adjusting to changes in the available capacity

## Slide 25: Additive Increase/Multiplicative Decrease
Objective: Adjust to changes in available capacity
  A state variable per connection: CongWin
    Limit how much data source has is in transit
  MaxWin = MIN(RcvWindow, CongWin)
Algorithm
  Increase CongWin when congestion goes down (no losses)
    Increment CongWin by 1 pkt per RTT (linear increase)
  Decrease CongWin when congestion goes up (timeout)
    Divide CongWin by 2 (multiplicative decrease)

## Slide 26: TCP Congestion Control
Window-based, implicit, end-end control
Transmission rate limited by congestion window size, Congwin, over segments:
w segments, each with MSS bytes sent in one RTT:
throughput =
w * MSS
RTT
Bytes/sec
Congwin

## Slide 27: TCP Congestion Control
two “phases”
  slow start
  congestion avoidance
important variables:
  Congwin
  threshold: defines threshold between slow start phase and congestion avoidance phase
“probing” for usable bandwidth:
  ideally: transmit as fast as possible (Congwin as large as possible) without loss
  increase Congwin until loss (congestion)
  loss: decrease Congwin, then begin probing (increasing) again

## Slide 28: Why Slow Start?
Objective
  Determine the available capacity in the first place
Idea
  Begin with congestion window = 1 pkt
  Double congestion window each RTT
    Increment by 1 packet for each ack
Exponential growth but slower than one blast
Used when
  First starting connection
  Connection goes dead waiting for a timeout

## Slide 29: TCP Slowstart
exponential increase (per RTT) in window size (not so slow!)
loss event: timeout (Tahoe TCP) and/or or three duplicate ACKs (Reno TCP)
initialize: Congwin = 1
for (each segment ACKed)
Congwin++
until (loss event OR
CongWin > threshold)
Slowstart algorithm
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 30: TCP Congestion Avoidance
/* slowstart is over */
/* Congwin > threshold */
Until (loss event) {
every w segments ACKed:
Congwin++
}
threshold = Congwin/2
Congwin = 1
perform slowstart
Congestion avoidance

## Slide 31: Fast Retransmit/Fast Recovery
Coarse-grain TCP timeouts lead to idle periods
Fast Retransmit
  Use duplicate acks to trigger retransmission
  Retransmit after three duplicate acks instead of waiting for timer to expire
Fast Recovery
  Remove the slow start phase
  Go directly to half the last successful CongWin

## Slide 32: TCP Fairness
Fairness goal: if N TCP sessions share same bottleneck link, each should get 1/N of link capacity
TCP connection 1
bottleneck
router
capacity R
TCP
connection 2
AIMD makes TCP flows roughly fair (bias towards flows with short RTT).

## Slide 33: Dealing with Greedy Senders
Scheduling and dropping policies at routers
First-in-first-out (FIFO) with tail drop
  Greedy sender can capture large share of capacity
Solutions?
  Fair Queuing
    Separate queue for each flow
    Schedule them in a round-robin fashion
    When a flow’s queue fills up, only its packets are dropped
    Insulates well-behaved from ill-behaved flows
  Random early detection (RED)

## Slide 34: More on TCP
Deferred acknowledgements
  Piggybacking for a free ride
Deferred transmissions
  Nagle’s algorithm
TCP over wireless

## Slide 35: Connectionless Service and UDP
User datagram protocol
Unreliable, connectionless
No connection management
Does little besides
  Encapsulating application data with UDP header
  Multiplexing application processes
Desirable for:
  Short transactions, avoiding overhead of establishing/tearing down a connection
    DNS, time, etc
  Applications withstanding packet losses but normally not delay
    Real-time audio/video

## Slide 36: UDP packet format
Source port
UDP length
Destination port
UDP checksum
Payload (if any)
0
16
31
15
UDP packet format

## Slide 37: UDP packet header
Source port number
Destination port number
UDP length
  Including both header and payload of UDP
Checksum
  Covering both header and payload