## Slide 1: Introduction to Networking and Overview of TCP/IP
Distributed memory parallel applications .vs. network applications
Introduction to networking
Basic networking protocol concepts
Common TCP/IP protocols
IP addresses and byte orders
Readings
  UNP Ch1 and Ch2

## Slide 2: Distributed memory parallel applications vs network applications
Distributed memory parallel applications (training LLM)
  Multiple processes cooperate to solve a computational problem.
  Exploit distributed parallelism with SPMD, message passing, synchronization, and work distribution.
Network applications (websites, online games)
  Similar to parallel applications: multiple processes cooperate to provide a functionality.
  Exploit distributed parallelism with client-server/peer-to-peer paradigm, request/response communication, protocol coordination, and socket programming.

## Slide 3: What is a Computer Network
A computer network consists of a set of end-systems/hosts and switches/routers connected by communication links. It supports communications among entities in the network.
  Many types of networks
    network on chip, system area network, person area network, local area network, data center network, wide area network, and so on
  Many topologies - how the devices are connected in the network

## Slide 4: Elements of a Network
Hosts, end-systems
  pc’s, workstations, servers
  PDA’s, phones, toasters
  CPUs, memory controllers
  running network applications
  Operate at the edge of the network
Routers, switches, and middleboxes:
  Forward/filter packets (chunks) of data thru network
  Operate at the core of the network
Communication links
  Point-to-point, multiaccess
  fiber, copper, radio, satellite
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 5: Challenges in the Networking System
What problems need to be solved for the Internet to behave like it does today?
  Dealing with heterogeneity in the networking environment
    different types of media: wired, wireless, satellite, radio, etc
    Dealing with different types of networks: telephone, data, ATM, fiber channel, Cable network, DSL
  Complex network functionality
    Reliability, routing, network congestion, speed-mismatch between communicating parties (flow control), naming and addressing, fragmentation and reassembly
What are the common techniques in computing to deal with complexity and heterogeneity in Computer Science?

## Slide 6: Challenges in Networking Software
What the common techniques in computing to deal with complexity and heterogeneity?
  Divide-and-conquer: partitioning the software to smaller pieces such that each piece becomes more manageable.
  Abstraction:
Result: Layered architecture in networking software

## Slide 7: Layered Architecture
Layering simplifies the architecture of a complex system
Layer N relies on services from layer N-1 to provide a service to layer N+1
Interfaces define the services offered
Service required from a lower layer is independent of the implementation
  Layer N change doesn’t affect other layers
Layer N+1 Protocol
Layer N Protocol

## Slide 8: Layered Architecture
Entities in the same layer on different hosts interact (peer entities) through a protocol.
  An entity can be an IO chip, a process, a procedure, etc
  A protocol governs how communication should happen between entities in the same layer on different hosts.
Entities on the same machine between two adjacent layers interact through the service interface.
Layer N+1 Protocol
Layer N Protocol

## Slide 9: Type of Communication Services
Reliable and unreliable – loss or no loss of packets
  reliable: all packets sent are received correctly
  unreliable: packets sent may not be received
Connection-oriented service & connectionless service -- order of packets
  Connection-oriented -- like the telephone.
    Establish the connection, use the connection, then release the connection. Even when multiplexed, minimal header information
    The packets received are in the same order as the packets sent.
  Connectionless (datagram) -- like the postal system.
    Each message carries its destination’s address and is routed to the destination independently.
    The packets received may not be in the same order as the packets send.

## Slide 10: Type of Communication Services
Four combinations of service types:
  Reliable connection-oriented
  Reliable connectionless
  Unreliable connection-oriented
  Unreliable connectionless
Example:
  send 1 2 3 4 5
  receive: 1 2 3 4 5
  1 3 2 5 4
  1 2 4
  3 1 4
Many applications use reliable connection-oriented service. Why not just do reliable connection-oriented all the time?

## Slide 11: TCP/IP Reference Model
TCP/IP reference model:
    Application layer (ssh, FTP SMPT, DNS, NNTP, HTTP) --- application, presentation, session
    Transport layer (TCP, UDP)
    Internet layer (IP) – network
    Host to Network layer (Ethernet, FDDI, X.25) -- data link, physical

## Slide 12: TCP/IP Reference Model
Application layer (HTTP, SSH, FTP SMPT, DNS, NNTP)
Interface – socket programming: (socket, TCP_send, TCP_recv, UDP_send, UDP_recv) ------- OS interface (system calls)
Transport layer (TCP, UDP) -- performed at the end host
  Major function: end-to-end communicate
  TCP (transmission control protocol): reliable connection-oriented
  UDP (user datagram protocol): unreliable connectionless
Interface: (IP_send, IP_recv)
Internet layer (IP) – unreliable connectionless -- performed at routers (and end-hosts)
  Major function: Routing – packet can reach destination multiple hops away
  A packet switching network based on connectionless communication. Hosts send packets into the network and then the packets travel independently to their destinations.
  Format conversion: for different networks.
  Packet format and protocol: IP
Interface – network dependent, Ethernet: (Eth_send, Eth_recv) ---- HW/SW interface
Host to Network layer (Ethernet, FDDI, X.25)
  Major function: Communication between directly connected devices
  Undefined, rely on the existing technology - must be able to send IP packets over this layer.

## Slide 13: Networked Applications
Application layer --- this is where network applications are!
Interface – socket programming (OS system call interface)
Transport layer (TCP, UDP)
Internet layer (IP)
Host to Network layer (Ethernet, FDDI, X.25)
Network applications: Use TCP or UDP (through socket programming) to perform communication between programs (application) on different machines.
  A network application usually has its own protocol, which decides how the programs in the application will communicate.

## Slide 14: Port number
The port number is a 16-bit number
  0 to 1023 are reserved ports to well known services
  Example: ssh (22), http(80)
1024-65535 are ephemeral ports that you can use for your application.
  Many ports are blocked by the firewall, so to open to public, you need to work with the system administrator.
  On linprog, use port 50000 and above for your application.
You can try to connect to a service using telnet from linprog
  Try ‘telnet www.cnn.com 80’ and then ‘GET / HTTP/1.1’.

## Slide 15: Networked Applications
Application layer --- this is where network applications are!
Need to have a way to identify another application on another machine
  This is done through the pair: (IP address, port number)
IPv4 addresses are 32 bit binary numbers
  Often represented as dotted decimal notation – 4 decimal values, each representing 8 bits in the range 0 to 255
    Example linprog1.cs.fsu.edu, 128.186.120.188
  It is supposed to be replaced by IPv6, but is still going strong
IPv6 addresses are 128 bits binary numbers
Machines often have both IPv4 and IPv6 addresses

## Slide 16: Network performance metrics
Latency and bandwidth
  Hardware latency and bandwidth
  End-to-end latency and bandwidth
Network latency is the amount of time it takes for data to travel from one point to another across a network.
  Units: second (s), millisecond (), microseconds (, etc
Bandwidth: the rate that data can be injected to the network (and transferred).
  Units: the network bandwidth is measured in bits per second. E.g. 1000 bps or 1kbps.

## Slide 17: Network performance metrics
Bandwidth units (bits per seconds)
  B and b:
    B – bytes: data size or memory size is measured in bytes (B).
      Example: 10KB (), 100MB (), 16GB (
    b – bits: network bandwidth is measured in bits per seconds
      Example 100Mbps Ethernet: 100,000,000 bits per second
    1 Byte = 8 bits
    Pay attention to the b/B in the spec: 1Gbps is different from 1GBps
  Most wired desktops are connected over 1Gbps links (1,000,000,000 bits per second)
    Faster ones can be 10Gbps, 100Gbps, or more
    Slower ones may be 100Mbps (100,000,000 bits per second)
  Wireless Ethernet (Wifi): Wi-Fi 6 (802.11ax) 2021, up to 10Gbps. This is shared by all users on the network.
You have a 1Gbps Internet service, what is the minimum amount of time to download a 10GB movie?

## Slide 18: Network performance metrics
Bandwidth determines the message injection (and transmission) time
  Let W bits per second be the bandwidth of a link. Given a message of size M bytes (or 8M bits), it will take 8M/W seconds to transmit the message: transmission time = 8M/W
  What is the transmission time to send 10000 bits over a 1Gbps link?
Time of flight (propagation delay) is another component of the hardware communication time
  The time between the first bit is placed on the wire in the sender to the time it reaches the receiver. This time is bounded by the speed of light.
    If we send a message from Tallahassee to LA (distance roughly 3000 miles), what is the time of flight for this message assuming that the signal propagation speed on the wire is 2/3 of the speed of light (300,000,000 meters per second)?
    The distance of a geostationary satellite from the earth is 22,236 miles (35,786km), estimate the communication latency when a communication goes through the such a satellite?
      How does Space X’s Starlink make this work?

## Slide 19: Network performance metrics
End-to-end latency: the amount of time from the time the sender calls write() to the time the receiver receives the data.
  Software time at both sender (OS runs the write() code) and receiver (interrupt and OS runs the read() code) and
  Hardware time: propogation time (time of flight) + transmission time
    The propogation time is determined by the physical law (bound by the speed of light).

## Slide 20: Network performance metrics

## Slide 21: Network performance metrics
End-to-end bandwidth: the amount of data transferred / the time to transfer the data from sender to receiver.
  An application: Internet speed test
  In an Internet speed test, 500MB of data is transferred in 10 seconds over the uplink, what is the uplink bandwidth?

## Slide 22: Overview of TCP/IP Protocols
Application layer (email, http, ssh, ftp, etc)
  The things that we use daily.
  Main functionality: run application protocols
Transport layer (TCP, UDP)
  Allows processes (on different machines) to communicate (reliably or unreliably) with each other.
  Main functionality: end-to-end communication (reliability)
Network layer (IPv4, IPv6)
  Allows machines to talk to one another
  Main functionality: routing/fragmentation/internetworking
Host to Network layer (Ethernet)
  Allows directly connected machines to talk to one another
  Main functionality: medium access, encoding

## Slide 23: Some TCP/IP Protocols
TCP: transmission control protocol
  connection-oriented, reliable, full duplex, byte stream service
UDP: User datagram protocol
  Connectionless, unreliable
IPv4: Internet Protocol, version 4.
  The protocol that glues the Internet together. Provides (unreliable) packet delivery service for TCP, UDP, ICMP, IGMP.
IPv6: Internet Protocol, version 6.
  128 bits address, newer version of Internet Protocol.
  Will it ever happen?

## Slide 24: Some TCP/IP Protocols
ICMP: Internet Control Message Protocol.
  Handles errors and control information for IP (ping, traceroute).
IGMP: Internet Group Management Protocol.
  Used in IP multicast
Socket Programming:
  The use of TCP and UDP
    Can also access the lower layers directly (raw socket)

## Slide 25: User Datagram Protocol (UDP)
Unreliable/connectionless service
  Data may be lost, duplicated and reordered.
  Client/server don’t have any long term relation.
Can perform (unreliable) multicast.
Interface
  socket, bind, sendto, recvfrom
  Can also use the TCP interface (connect/read/write)

## Slide 26: Transmission Control Protocol (TCP)
Connection-oriented, reliable, full duplex, byte stream service
Interface
  socket, bind, listen, accept, connect, read, write, close.
An analogy
  Socket: telephone
  Bind: assign telephone number to a telephone
  Listen: turn on the ringer so that you can hear the phone call
  Connect: dial a phone number
  Accept: answer the phone
  Read/write: talking
  Close: ???

## Slide 27: Reliable Communications
Realizing reliable communication means a lot:
  Sequence number, acknowledgement, retransmission, timeout (RTT)
  Sliding window protocol for efficiency
  Flow control
  Connection establishment/release

## Slide 28: Basic Functionality of TCP and UDP
Allow processes on different machines to communicate.
  One crucial issue: addressing
    how to identify your peer?
    Two components: identifying the peer machine and identifying the peer process.
  Identifying peer machine: IP address
  A unique identifier for each network interface connected to an IP network.
    A machine may have multiple IP addresses, one for each interface.

## Slide 29: IP Address (IPv4)
32 bit binary number (IPv4)
Represented as "dotted decimal" notation:
  4 decimal values, each representing 8 bits (octet), in the range 0 to 255.
Example:
  Dotted Decimal: 140 .179 .220 .200
  Binary: 10001100.10110011.11011100.11001000

## Slide 30: IP Address Structure
Two parts.
  Network prefix
  Host ID (remaining).
Network Prefix Host ID
0
31

## Slide 31: Identifying Processes
Using PID?
Port - A 16-bit number to identify the application process that is a network endpoint.
Reserved ports or well-known ports (0 to 1023)
  Standard ports for well-known applications.
  Telnet (23), ftp(21), http (80).
  See /etc/services file on any UNIX machine for listing of services on reserved ports
Ephemeral ports (1024-65535)
  For ordinary user-developed programs.

## Slide 32: Identifying Connection
A 5-tuple that completely specifies the two end-points of a connection:
{protocol, local-IP, local-port, remote-IP, remote-port}

## Slide 33: The Byte Order Problem
Two ways to store 16-bit/32-bit integers
Little-endian byte order (e.g. Intel)
Big-endian byte order (E.g. Sparc)
See example1.c
High-order byte Low-order byte
Address A
Address A+1
High-order byte Low-order byte
Address A+1
Address A

## Slide 34: Network-byte Ordering (Cont.)
How do two machines with different byte-orders communicate?
  Using network byte-order
  Network byte-order = big-endian order

## Slide 35: Network-Byte Ordering (Cont’d)
Converting between host and network byte order
  htonl, htons, ntohl, htohs
  See example2.c
    #include <netinet/in.h>
    uint16_t htons(uint16_t host16bitvalue);
    uint32_t htonl(uint32_t host32bitvalue);
    uint16_t ntohs(uint16_t net16bitvalue);
    uint32_t ntohl(uint32_t net32bitvalue);