## Slide 1: Counters

## Slide 2: In class excercise
How to implement a “counter”, which will count as 0,3,1,4,5,7,0,3,1,……
Q2 | Q1 | Q0 | D2 | D1 | D0
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 

## Slide 3: Finite State Machines

## Slide 4: Parity checking
Design a parity checking circuit that has one input X, and one output O.
X may change every clock cycle. The change happens at the falling edge.
The circuit samples the input at every rising edge of the clock. If the input is 1, consider as read a 1, else read a 0.
O is 1 if all the bits read so far contains an odd number of 1s and 0 otherwise.

## Slide 5: Parity checking
Note that the output of the circuit depends on ALL past inputs.
So one possible implementation is to remember all past inputs.
Obviously bad…

## Slide 6: Parity checking
A better implementation is to “summarize” the past inputs into some “states.” For what we are concerned about,
  Knowing the current state, the value of the output can be uniquely determined.
  Given the current state, the future state transition does not depend on the past inputs.
Note that
  The states are just some binary numbers.
  The number of states is significantly less than the number of input combinations, so we have a better circuit.

## Slide 7: The difference from the counters
Counters also have states. For example, the state of the 3-bit counters are 0,1,2,3,4,5,6,7.
But counters have only the clk input, and is driven only by the clk. Knowing what the current state is, we know exactly what the next state should be.
Here, obviously, the next state also depends on the input X.
So we are moving to a more sophisticated example.

## Slide 8: States
Finding out what the states should be is a bit of art.
Problems are different, so the solutions are also different.
Experience will help.
What the states of the parity checking circuit should be?

## Slide 9: State
The state is the parity of the bits read so far.
Two states: S0 and S1.
  S0: the bits have parity 0.
  S1: the bits have parity 1.

## Slide 10: State Diagram
The state transition diagram.
  Draw a circle around the state.
  Draw arrows from one state to another.
  Beside the arrows, show the values of the inputs that caused this transition.
S0
S1
X = 1
X = 0
X=1
X=0
X=1
X=0

## Slide 11: Assign states
Need to assign binary number representations to the states.
Only one bit is needed. Let S0=0, S1=1.

## Slide 12: Next State Function
Q | X | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
D = Q^X

## Slide 13: Output function
The circuit should generate the output.
Clearly, the output function is O=Q.

## Slide 14: Another FSM example – A sequence detector
One input X, and one output O.
X may change every clock cycle. The change happens at the falling edge.
The circuit samples the input at every rising edge of the clock. If the input is 1, consider as read a 1, else read a 0.
O is 1 (for one clock cycle, from positive edge to positive edge) if the last three bits read are 101.

## Slide 15: Suggestions?
Do we need to remember any states?
What states do we need to remember?

## Slide 16: Suggestions?
Maybe we just connect 3 Dffs and output 1 if Q2Q1Q0=101?
That is, we need to remember 8 states.
Can do better than that.
Remember what fractions of the sequence I have got.

## Slide 17: 4 states
S0: got nothing. The initial state.
S1: got 1.
S2: got 10.
S3: got 101.
S0
S1
X = 1
X = 0
S2
S3
X=0
X=0
X=0
X=0
X=1
X=1
X=1
X=1

## Slide 18: Assign states
S0 = 00
S1 = 01
S2 = 10
S3 = 11

## Slide 19: Next State Function
Q1 | Q0 | X | D1 | D0
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 20: Next State Function
Q1 | Q0 | X | D1 | D0
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
D1 = (Q0&~X)|(Q1&~Q0&X)
D0 = X

## Slide 21: The output function
Clearly, O = Q1&Q0.