## Slide 1: MIPS processor continued

## Slide 2: Question
How to implement the datapath of a processor supporting jal and R type?

## Slide 3: jal and R-type

## Slide 4: Control Signals
Control signals include ALUCtrl and the signals to control the 2-1 selectors
They are generated according to the current instruction, using the opcode [31-27] and the funct [5-0] field in the instruction.

## Slide 5: Datapath for Memory, R-type and Branch Instructions, plus the control signals

## Slide 6: The Effect of Control Signals
Signal name | Effect when deasserted | Effect when asserted
RegDst | The register destination number for the Write register comes the rt field (20:16) | The register destination number for the Write register comes the rd field (15:11)
RegWrite | None. | The register on the Write register input is written with the value on the Write data input.
ALUSrc | The second ALU operand comes from the second register file output | The second ALU operand is the sign-extended, lower 16 bits of the instruction
PCSrc | The PC is replaced by the output of the adder that computes the value of PC + 4 | The PC is replaced by the output of the adder that computes the branch target
MemRead | None. | Data memory contents designated by the address input are out on the Read data output.
MemWrite | None. | Data memory contents designated by the address input are replaced by the value on the Write data input.
MemtoReg | The value fed to the register Write data input comes from the ALU | The value fed to the register Write data input comes from the data memory

## Slide 7: Table for Control Line Setting
Instruction | RegDst | ALUSrc | Memto- Reg | Reg Write | Mem Read | Mem Write | Branch | ALUOp1 | ALUOp0
R-format |  |  |  |  |  |  |  |  | 
Lw |  |  |  |  |  |  |  |  | 
Sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
Note: Branch is anded with ALU zero output to produce PCSrc

## Slide 8: Table for Control Line Setting
Instruction | RegDst | ALUSrc | Memto- Reg | Reg Write | Mem Read | Mem Write | Branch | ALUOp1 | ALUOp0
R-format | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0
beq | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 1

## Slide 9: Truth Table for Control Function

## Slide 10: Implementation Using PLA
The way to
read this --
There are only 4
possible combination
of inputs
R
beq
sw
lw
Notes: 0

## Slide 11: MIPS ALU unit

## Slide 12: ALU Control
Use Opcode to get ALUOp, then combine ALUOp with Funct
Two levels of decoding, more efficient
Assume ALUOp has been determined as such for each instruction

## Slide 13: One Implementation
ALU control bit 3 is always 0 for this set of instructions
Can verify that the output is correct for lw, sw, beq
For R-type, op2=F1, op1= ~F2, op0 = F3 | F0