## Slide 1: Other Processors

## Slide 2: Other Processors
Having learnt MIPS, we can learn other major processors.
Not going to be able to cover everything; will pick on the interesting aspects.

## Slide 3: ARM
Advanced RISC Machine
The major processor for mobile and embedded electronics, like iPad
Simple, low power, low cost

## Slide 4: ARM
One of the most interesting features is the conditional execution.
That is, an instruction will execute if some condition is true, otherwise it will not do anything (turned into a nop).

## Slide 5: ARM
A set of flags, showing the relation of two numbers : gt, equal, lt.
  cmp Ri, Rj # set the flags depending on the values in Ri and Rj
  subgt Ri, Ri, Rj # i = i – j if flag is gt
  sublt Ri, Ri, Rj # i = i – j if flag is lt
  bne Label # goto Label if flag is not equal

## Slide 6: ARM
How to implement
    while (i != j) {
    if (i > j)
    i -= j;
    else
    j -= i;
    }

## Slide 7: ARM
In MIPS, assume i is in $s0, j in $s1:
    Loop: beq $s0, $s1, Done
    slt $t0, $s0, $s1
    beq $t0, $0, L1
    sub $s0, $s0, $s1
    j Loop
    L1: sub $s1, $s1, $s0
    L2: j Loop

## Slide 8: ARM
In ARM,
  Loop: cmp Ri, Rj
  subgt Ri, Ri, Rj
  sublt Rj, Rj, Ri
  bne Loop

## Slide 9: ARM
Discussion: Given the MIPS hardware setup, can we support conditional execution? How?
Will have to introduce the cmp instruction

## Slide 10: Intel Processor

## Slide 11: Basic Program Execution Registers
General purpose registers
  There are eight registers (note that they are not quite general purpose as some instructions assume certain registers)
Segment registers
  They define up to six segment selectors
EIP register – Effective instruction pointer
EFLAGS – Program status and control register

## Slide 12: General Purpose and Segment Registers

## Slide 13: General Purpose Registers
EAX — Accumulator for operands and results data
EBX — Pointer to data in the DS segment
ECX — Counter for string and loop operations
EDX — I/O pointer
ESI — Pointer to data in the segment pointed to by the DS register; source pointer for string operations
EDI — Pointer to data (or destination) in the segment pointed to by the ES register; destination pointer for string operations
ESP — Stack pointer (in the SS segment)
EBP — Pointer to data on the stack (in the SS segment)

## Slide 14: Alternative General Purpose Register Names

## Slide 15: Segment Registers

## Slide 16: SIMD
To improve performance, Intel adopted SIMD (single instruction multiple data) instructions.
Streaming SIMD Extensions (SSE) introduced eight 128-bit data registers (called XMM registers)
  In 64-bit modes, they are available as 16 64-bit registers
  The 128-bit packed single-precision floating-point data type, which allows four single-precision operations to be performed simultaneously

## Slide 17: GCC Inline Assembly
GCC inline assembly allows us to insert inline functions written in assembly
  http://www.ibiblio.org/gferg/ldp/GCC-Inline-Assembly-HOWTO.html
  GCC provides the utility to specify input and output operands as C variables
  Basic inline
  Extended inline assembly

## Slide 18: GCC Inline Assembly
A simple example:

## Slide 19: Using SSE
#define mulfvec4_SSE(a, b, c) \
{ \
__asm__ __volatile__ ("movups %1, %%xmm0 \n\t" \
"movups %2, %%xmm1 \n\t" \
"mulps %%xmm0, %%xmm1 \n\t" \
"movups %%xmm1, %0 \n\t" \
:"=m" (c) \
:"m" (a), \
"m" (b)); \
}

## Slide 20: BCM4306 Wireless Card Processor

## Slide 21: A Part of the Code from http://www.ing.unibs.it/~openfwwf/