## Slide 1: MIPS Assembly

## Slide 2: Why are we learning assembly
Comparing to higher level languages such as C, assembly languages
  are more difficult to write, read, and debug.
  have poor portability – Every processor has its own assembly language. The MIPS code you write is NOT going to run on Intel processors.
Then why are we learning it?
  After learning the first assembly language, the second will be MUCH easier
  It brings us closer to the processor, which is the goal of this course.

## Slide 3: MIPS ISA
There are many different Instruction Set Architectures designed for different applications with different performance/cost tradeoff
  Including Intel-32, PowerPC, MIPS, ARM ….
We focus on MIPS architecture
  Microprocessor without Interlocked Pipeline Stages
  A RISC (reduced instruction set computer) architecture
    In contrast to CISC (complex instruction set computer)
  Similar to other architectures developed since the 1980's
  Almost 100 million MIPS processors manufactured in 2002
  Used by NEC, Nintendo, Cisco, Silicon Graphics, Sony, …

## Slide 4: A peek into the future…

## Slide 5: Abstract View of MIPS Implementation

## Slide 6: MIPS Instruction Set
An instruction is a command that hardware understands
  Instruction set is the vocabulary of commands understood by a given computer
  It includes arithmetic instructions, memory access instructions, logical operations, instructions for making decisions

## Slide 7: Arithmetic Instructions
Each MIPS arithmetic instruction performs only one operation
  Each one must always have exactly three variables
  add a, b, c # a = b + c
    Note that these variables can be the same though
  If we have a more complex statement, we have to break it into pieces

## Slide 8: Arithmetic Instructions
Example
  f = (g + h) – (i + j)

## Slide 9: Arithmetic Instructions
Example
  f = (g + h) – (i + j)
  add t0, g, h # temporary variable t0 contains g + h
  add t1, i, j # temporary variable t1 contains i + j
  sub f, t0, t1 # f gets t0 – t1

## Slide 10: Operands of Computer Hardware
In C, we can define as many as variables as we need
  In MIPS, operands for arithmetic operations must be from registers
  MIPS has thirty-two 32-bit registers

## Slide 11: MIPS Registers

## Slide 12: Arithmetic Instructions
Example
  f = (g + h) – (i + j)
  #In MIPS, add can not access variables directly
  #because they are in memory
  # Suppose f, g, h, i, and j are in $s0, $s1, $s2, $s3, $s4 respectively
  add $t0, $s1, $s2 # temporary variable t0 contains g + h
  add $t1, $s3, $s4 # temporary variable t1 contains i + j
  sub $s0, $t0, $t1 # f gets t0 – t1

## Slide 13: Memory Operands
Since variables (they are data) are initially in memory, we need to have data transfer instructions
  Note a program (including data (variables)) is loaded from memory
  We also need to save the results to memory
  Also when we need more variables than the number of registers we have, we need to use memory to save the registers that are not used at the moment
Data transfer instructions
  lw (load word) from memory to a register
  sw (store word) from register to memory

## Slide 14: Using Load and Store
Memory address in load and store instructions is specified by a base register and offset
  This is called base addressing

## Slide 15: Using Load and Store
How to implement the following statement using the MIPS assembly we have so far?
  Assuming the address of A is in $s3 and the variable h is in $s2
  A[12] = h + A[8]

## Slide 16: Specifying Memory Address
Memory is organized as an array of bytes (8 bits)

## Slide 17: Specifying Memory Address
MIPS uses words (4 bytes)
  Each word must start at address that are multiples of 4
  This is called alignment restriction
  Big Endian

## Slide 18: Example of Endianness
Store 0x87654321 at address 0x0000, byte-addressable

## Slide 19: Example of Endianness
Store 0x87654321 at address 0x0000, byte-addressable