## Slide 1: MIPS Functions

## Slide 2: Character and String Operations
Characters are encoded as 0’s and 1’s using ASCII most commonly
  American Standard Code for Information Interchange
  Each character is represented using 8 bits (or a byte)
MIPS provides instructions to move bytes
  Load byte (lb) loads a byte to the rightmost 8 bits of a register
  Store byte (sb) write the rightmost 8 bits of a register to memory

## Slide 3: SPIM syscalls
li $v0,1 # print an integer in $a0
li $a0,100
syscall
li $v0,5 # read an integer into $v0
syscall
li $v0,4 # print an ASCIIZ string at $a0
la $a0,msg_hello
syscall
li $v0,10 #exit
syscall

## Slide 4: String Copy Procedure

## Slide 5
.data
msg_hello: .asciiz "Hello\n“
msg_empty: .space 400
.text
.globl main
Main: li $v0,4
la $a0,msg_hello
syscall
li $v0,4
la $a0,msg_empty
syscall
la $a0,msg_empty #dst
la $a1,msg_hello #src
jal strcpy
li $v0,4
la $a0,msg_empty
syscall
li $v0,10 #exit
syscall
strcpy: lb $t0, 0($a1)
sb $t0, 0($a0)
addi $a0, $a0, 1
addi $a1, $a1, 1
bne $t0, $0, strcpy
jr $ra

## Slide 6: Stack
Key things to keep in mind:
  Stack is a software concept – last in first out, that’s it.
  In MIPS, you implement the stack by yourself by keeping $sp always pointing to the top element on the stack
  Stack can be used in functions to save register values, and is the standard approach to save register values. But
    You can also use stack for other purposes
    This is not the only way to save register values.

## Slide 7
.data
msg: .asciiz "hello world"
endl: .asciiz "\n"
.text
.globl main
main: addi $sp,$sp,-1 sb $0,0($sp)
la $t1, msg
L0: lb $t0,0($t1)
beq $t0,$0, L1
addi $sp,$sp,-1 sb $t0,0($sp)
addi $t1,$t1,1
j L0
L1: la $t1,msg
L2: lb $t0,0($sp)
addi $sp,$sp,1
sb $t0,0($t1)
beq $t0, $0, L3 addi $t1,$t1,1
j L2
L3: la $a0,msg
li $v0,4
syscall
la $a0,endl
li $v0,4
syscall
li $v0,10 #exit
syscall