## Slide 1: Writing an Embedded Controller

## Slide 2: Writing an Embedded Controller
It usually consists of two parts
  Initialization
  A main loop
Experience:
  The main loop usually has to deal with many things. It is important NOT to stay in any job for too long. You should process an event and almost immediately return to the main loop.

## Slide 3: A Simple Program to Get Started
Write a program which
  Prints out “TV is working” every 3 seconds
  Print out the ASCII of any key you have pressed immediately.

## Slide 4: Two Jobs
The simple program has two jobs:
  A periodical job executed every 3 seconds
  A job to process the input
Note:
  Cannot sleep for 3 seconds and then print out the sentence because cannot process the input while sleeping
Must make sure that each iteration of the main loop is short, such that you can check at a fine time granularity if
    need to print status
    Has new keyboard input

## Slide 5: The code should look like
loop: if key pressed
print ascii value
if 3 sec timer expires
print msg
goto loop

## Slide 6
.data
new_line: .asciiz "\n"
msg_tvworking:
.asciiz "TV is working\n"
.text
.globl main
main: mfc0 $a0, $12 # read from the status register
ori $a0, 0xff11 # enable all interrupts
mtc0 $a0, $12 # write back to the status register
lui $t0, 0xFFFF # $t0 = 0xFFFF0000;
ori $a0, $0, 2 # enable keyboard interrupt
sw $a0, 0($t0) # write back to 0xFFFF0000;
li $s0, 300 #
li $s6, 10000 # $s6 used to pass the ascii code
li $s7, 10000 # a large number impossible to be an ascii code
loop: beq $s6, $s7, mainloopnext1
ori $a0, $s6, 0
li $v0,1 # print it here.
syscall
li $v0,4 # print the new line
la $a0, new_line
syscall
mfc0 $t0, $12 # Set Status register
andi $t0, 0xfffe # clear ENABLE
mtc0 $t0, $12 # write back to status
li $s6, 10000 # $s0 used to pass the ascii code
mfc0 $t0, $12 # Set Status register
ori $t0, 1 # set ENABLE
mtc0 $t0, $12 # write back to status
mainloopnext1:
# 2. delay for 10ms to emulate time-consuming jobs
jal delay_10ms
# 3. print status
addi $s0, $s0, -1
bne $s0, $0, mainloopnext4
li $s0, 300
la $a0, msg_tvworking
li $v0, 4
syscall
mainloopnext4:
j loop
li $v0, 10 # exit,if it ever comes here
syscall
delay_10ms:
li $t0, 3000
delay_10ms_loop:
addi $t0, $t0, -1
bne $t0, $0, delay_10ms_loop
jr $ra
.ktext 0x80000180 # kernel code starts here
mfc0 $k0, $13 # Cause register
srl $k0, $k0, 2 # Extract ExcCode Field
andi $k0, $k0, 0x1f
bne $k0, $zero, kdone # Exception Code 0 is I/O. Only processing I/O here
lui $k0, 0xFFFF # $k0 = 0xFFFF0000;
lw $s6, 4($k0) # get the input key
kdone: mtc0 $0, $13 # Clear Cause register
mfc0 $k0, $12 # Set Status register
andi $k0, 0xfffd # clear EXL bit
ori $k0, 0x11 # Interrupts enabled
mtc0 $k0, $12 # write back to status
eret # return to EPC

## Slide 7: A Slightly More Advanced Version
Write a process_input function that responds to `m’, `h’, `q’ (ascii code 109, 104, 112, respectively).
Basically, the TV is initially not in the ``menu state.’’ When the user presses `m’ while the TV is not in the menu state, the TV should show a very simple menu, and enters the menu state:
  “`h' to print hello, `q' to quit.”
In the menu state,
  if the user presses `h’, print out “Hello!”
  if the user presses `q’, print out “quit” and quits the menu state.
If not in the menu state,
  the TV does not respond to `h’ and `q’.

## Slide 8: The Challenge
How do you know whether to respond to ‘h’ or ‘q’ or not?
  Should not respond in the normal state
  Should respond under menu
A naïve way is to write a process_input function that
  Called when ‘m’ is pressed then waits there for ‘h’ and ‘q’
  Problem?
Notes: Problem is cannot print the “TV okay” message while waiting

## Slide 9: The solution
Maintain a global variable to remember if we are in the menu state
Write the process_input function by checking the variable first
The program almost inevitably has states which makes it complicated.

## Slide 10
In menu state?
n
Is the key ‘m’
y
Print the menu, set the menu state flag
Is the key ‘h’
y
Print “Hello”
Is the key ‘q’
y
Print “Quit”, clear the menu state flag
y
n
n
n

## Slide 11: The code
.data
menuLevel: .word 0
msg_tvworking:
.asciiz "tv is working\n"
msg_menu:
.asciiz "`h' to print hello, `q' to quit.\n"
msg_hello:
.asciiz "hello!\n"
msg_quit:
.asciiz "quit.\n"
# --------------------
# --------------------
.text
.globl main
main: mfc0 $a0, $12 # read from the status register
ori $a0, 0xff11 # enable all interrupts
mtc0 $a0, $12 # write back to the status register
lui $t0, 0xFFFF # $t0 = 0xFFFF0000;
ori $a0, $0, 2 # enable keyboard interrupt
sw $a0, 0($t0) # write back to 0xFFFF0000;
li $s0, 300 #
li $s6, 10000 # $s6 used to pass the ascii code
li $s7, 10000 # a large number impossible to be an ascii code
mainloop:
# 1. read keyboard input, and process it
beq $s6, $s7, mainloopnext1
ori $a0, $s6, 0
mfc0 $t0, $12 # Set Status register
andi $t0, 0xfffe # clear ENABLE
mtc0 $t0, $12 # write back to status
li $s6, 10000 # $s0 used to pass the ascii code
mfc0 $t0, $12 # Set Status register
ori $t0, 1 # set ENABLE
mtc0 $t0, $12 # write back to status
jal process_input
mainloopnext1:
# 2. update counter, check sleep timer
jal delay_10ms
# 3. $s0 as the 10ms counter, go from 0 to 299
addi $s0, $s0, -1
bne $s0, $0, mainloop
li $v0, 4
la $a0, msg_tvworking
syscall
addi $s0, $0, 300
j mainloop
li $v0,10 # exit
syscall
# --------------------
delay_10ms:
li $t0, 1000
delay_10ms_loop:
addi $t0, $t0, -1
beq $t0, $0, delay_10ms_done
j delay_10ms_loop
delay_10ms_done:
jr $ra
# --------------------
process_input:
la $t0, menuLevel
lw $t1, 0($t0)
bne $t1, $0, pi_menu_L_1
li $t0, 109 # comparing with the ascii of `m'
bne $a0, $t0, process_input_done
la $t0, menuLevel
li $t1, 1
sw $t1, 0($t0)
la $a0, msg_menu
li $v0, 4
syscall
j process_input_done
pi_menu_L_1:
li $t0, 104 # comparing with the ascii of `h'
bne $a0, $t0, pi_menu_L_1_comp_q #
la $a0, msg_hello
li $v0, 4
syscall
j process_input_done
pi_menu_L_1_comp_q:
li $t0, 113 # comparing with the ascii of `q'
bne $a0, $t0, process_input_done #
la $a0, msg_quit
li $v0, 4
syscall
la $t0, menuLevel
sw $0, 0($t0)
j process_input_done
process_input_done:
jr $ra
# --------------------
# --------------------
.ktext 0x80000180 # kernel code starts here
mfc0 $k0, $13 # Cause register
srl $k0, $k0, 2 # Extract ExcCode Field
andi $k0, $k0, 0x1f
bne $k0, $zero, kdone # Exception Code 0 is I/O. Only processing I/O here
lui $k0, 0xFFFF # $k0 = 0xFFFF0000;
lw $s6, 4($k0) # get the input key
kdone: mtc0 $0, $13 # Clear Cause register
mfc0 $k0, $12 # Set Status register
andi $k0, 0xfffd # clear EXL bit
ori $k0, 0x11 # Interrupts enabled
mtc0 $k0, $12 # write back to status
eret # return to EPC
# --------------------