## Slide 1: Pseudo instructions

## Slide 2: Pseudo instructions
MIPS supports pseudo instructions. We have seen some like
  li $t0, 4
  which set $t0 to 4.
  la $t0, A
  which puts the address of label A (a 32-bit value) into $t0.
  bgt $t0, $t1, L1
  which goes to L1 if $t0 > $t1

## Slide 3: Pseudo instructions
Pseudo instructions are not real instructions implemented in hardware. They are created to make the program more readable.
A pseudo instruction usually (not always) maps to one or several real instructions. The mapping is one-to-one.

## Slide 4: Pseudo instructions
For example,
  li $t0, 4
  translate to
  ori $t0, $0, 4
  but what should
  li $t0, 90000
  translate to?

## Slide 5: Pseudo instructions
So
  li $t0, 90000
  translates to
  lui $1, 1 #load upper 16 bits
  ori $t0, $1, 24464
The special register $1 is $at and should only be used for pseudo instructions.

## Slide 6: MIPS mul div, and MIPS floating point instructions

## Slide 7: Multiply and Division Instructions
mul rd, rs, rt
  put the result of rs times rt in rd
div rd, rs, rt
  A pseudo instruction
  put the quotient of rs/rt into rd

## Slide 8: hi and lo
mult rs,rt
  put the high word in hi and low word in lo.
div rs, rt
  put the remainder in hi and quotient in lo.

## Slide 9: Floating Point

## Slide 10: Load and Store
Load or store from a memory location (pseudoinstruction ). Just load the 32 bits into the register.
  l.s $f0, val
  s.s $f0, val
Load immediate number (pseudoinstruction )
  li.s $f0, 0.5

## Slide 11: Print and Read
Print:
  li $v0, 2
  li.s $f12, 0.5
  syscall
Read
  li $v0, 6
  syscall
  (the read will be in $f0)

## Slide 12: Arithmetic Instructions
abs.s $f0, $f1
add.s $f0, $f1, $f2
sub.s $f0, $f1, $f2
mul.s $f0, $f1, $f2
div.s $f0, $f1, $f2
neg.s $f0, $f1

## Slide 13: Data move
mov.s $f0, $f1
copy $f1 to $f0.
mfc1 $t0, $f0
copy $f0 to $t0.
mtc1 $t0, $f0
copy $t0 to $f0.

## Slide 14: Convert to integer and from integer
cvt.s.w $f0, $f1
  convert the 32 bits in $f1 currently representing an integer to float of the same value and store in $f0
cvt.w.s $f0, $f1
  the reverse

## Slide 15: Comparison instructions
c.lt.s $f0,$f1
  set a flag in coprocessor 1if $f0 < $f1, else clear it. The flag will stay until set or cleared next time
c.le.s $f0,$f1
  set flag if $f0 <= $f1, else clear it
bc1t L1
  branch to L1 if the flag is set
bc1f L1
  branch to L1 if the flag is 0

## Slide 16: Computing the square root of a number n
The Newton’s method
  x’=(x+n/x)/2
  For any n, guess an initial value of x as the sqrt of n and keep on updating x until is the difference between the two updates are very close.
  The idea is that x’=x-f(x)/f’(x), where f(x) is x2-n=0.

## Slide 17
.data
val1: .float 0.6
val2: .float 0.8
msg_done: .asciiz "done\n"
.text
.globl main
main:
li.s $f0, 361.0
mfc1 $a0, $f0
jal calsqrt
done:
mtc1 $v0, $f12
li $v0,2
syscall
eixt:
li $v0,10
syscall
# calsqrt:
# calculating the square root of n
# using the formular x'=(x+n/x)/2
# loop until |x'-x| < 0.001
calsqrt:
addi $sp, $sp, -24
swc1 $f0, 20($sp)
swc1 $f1, 16($sp)
swc1 $f2, 12($sp)
swc1 $f3, 8($sp)
swc1 $f20, 4($sp)
swc1 $f21, 0($sp)
mtc1 $a0, $f0 # $f0 gets n
li.s $f20, 2.0 # $f20 storing constant 2 for dividing
li.s $f21, 0.001 # $f21 storing constant 0.001 for exit comparision
div.s $f1, $f0, $f20 # $f1 gets n/2
calsqrtloop:
div.s $f2, $f0, $f1 # $f2 gets n/x
add.s $f2, $f2, $f1 # $f2 gets n/x + x
div.s $f2, $f2, $f20 # $f2 gets x'=(n/x + x)/2
sub.s $f3, $f2, $f1 # $f3 gets x'-x
abs.s $f3, $f3 # $f3 gets |x'-x|
c.lt.s $f3, $f21 # set the flag if |x'-x| < 0.001
bc1t calsqrtdone
mov.s $f1, $f2
j calsqrtloop
calsqrtdone:
mfc1 $v0, $f2
lwc1 $f0, 20($sp)
lwc1 $f1, 16($sp)
lwc1 $f2, 12($sp)
lwc1 $f3, 8($sp)
lwc1 $f20, 4($sp)
lwc1 $f21, 0($sp)
addi $sp, $sp, 24
jr $ra