## Slide 1: Digital Logic

## Slide 2: Abstractions in CS (gates)
Basic Gate: Inverter
I
O
0
1
1
0
I
O
GND
I
O
Vcc
Resister (limits conductivity)
Truth Table

## Slide 3: Abstractions in CS (gates)
I
O
0
1
1
0
I
O
Truth Table

## Slide 4: Abstractions in CS (gates)
Basic Gate: NAND (Negated AND)
A
B
0
0
1
1
0
1
0
1
1
1
1
0
Y
A
B
Y
GND
A
B
Y
Vcc
Truth Table

## Slide 5: Abstractions in CS (gates)
Basic Gate: AND
A
B
0
0
1
1
0
1
0
1
0
0
0
1
Y
A
B
Y
Truth Table

## Slide 6: Abstractions in CS (gates)
Other Basic Gates: OR gate
A
B
0
0
1
1
0
1
0
1
0
1
1
1
Y
A
B
Y
Truth Table

## Slide 7: Abstractions in CS (gates)
Other Basic Gates: XOR gate
A
B
0
0
1
1
0
1
0
1
0
1
1
0
Y
A
B
Y
Truth Table

## Slide 8: Logic Blocks
Logic blocks are built from gates that implement basic logic functions
  Any logical function can be constructed using AND gates, OR gates, and inversion.

## Slide 9: Adder
In computers, the most common task is add.
In MIPS, we write “add $t0, $t1, $t2.” The hardware will get the values of $t1 and $t2, feed them to an adder, and store the result back to $t0.
So how the adder is implemented?

## Slide 10: Half-adder
How to implement a half-adder with logic gates?
A half adder takes two inputs, a and b, and generates two outputs, sum and carry. The inputs and outputs are all one-bit values.
a
b
carry
sum

## Slide 11: Half-adder
First, how many possible combinations of inputs?

## Slide 12: Half-adder
Four combinations.
a | b | sum | carry
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 13: Half-adder
The value of sum should be? Carry?
a | b | sum | carry
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 14: Half-adder
Okay. We have two outputs. But let’s implement them one by one.
First, how to get sum? Hint: look at the truth table.
a | b | sum
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 15: Half-adder
Sum
a
b
sum

## Slide 16: How about carry?
The truth table is
a | b | carry
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 17: Carry
So, the circuit for carry is
a
b
carry

## Slide 18: Half-adder
Put them together, we get
a
b
sum
carry

## Slide 19: 1-Bit Adder
1-bit full adder
  Also called a (3, 2) adder

## Slide 20: Constructing Truth Table for 1-Bit Adder

## Slide 21: Truth Table for a 1-Bit Adder

## Slide 22: Sum?
Sum is `1’ when one of the following four cases is true:
  a=1, b=0, c=0
  a=0, b=1, c=0
  a=0, b=0, c=1
  a=1, b=1, c=1

## Slide 23: Sum
The idea is that we will build a circuit made of and gates and or gate faithfully according to the truth table.
  Each and gate corresponds to one ``true’’ row in the truth table. The and gate should output a ```1’’ if and only if the input combination is the same as this row. If all other cases, the output is ``0.’’
  So, whenever the input combination falls in one of the ``true’’ rows, one of the and gates is ``1’’, so the output of the or gate is 1.
  If the input combination does not fall into any of the ``true’’ rows, none of the and gates will output a ``1’’, so the output of the or gate is 0.

## Slide 24: Boolean Algebra
We express logic functions using logic equations using Boolean algebra
  The OR operator is written as +, as in A + B.
  The AND operator is written as ·, as A · B.
  The unary operator NOT is written as . or A’.
Remember: This is not the binary field. Here 0+0=0, 0+1=1+0=1, 1+1=1.

## Slide 25: Sum

## Slide 26: Carryout bit?
Carryout bit is ‘1’ also on four cases. When a, b and carryin are 110, 101, 011, 111.
Does it mean that we need a similar circuit as sum?

## Slide 27: Carryout bit
Actually, it can be simpler

## Slide 28: Delay
Hardware has delays.
Delay is defined as the time since the input is stable to the time when the output is stable.
How much delay do you think the one-bit half adder is and the one-bit full adder is?

## Slide 29: 1-Bit Adder

## Slide 30: 32-bit adder
How to get the 32-bit adder used in MIPS?

## Slide 31: 32-bit adder